## Slide 1: WBA E2E QoS and L4S over Wi-Fi Links
Date: 2023-01-15
Authors:

## Slide 2: Abstract
Document 23/1206 was presented in the July 23 Plenary where we described the WBA E2E QoS project Phase-1. We also mentioned a Phase-2 of the project where E2E QoS (optimizing QoS end-to-end over links that are not exclusively IEEE802.11 links).
Document 23/2118 was discussed in the Nov 23 Plenary – the discussion led to
(a) interest in performance improvement for latency sensitive traffic when L4S is enabled over the 802.11 link, and
(b) a look at IEEE802.1Q-2022 Clause 30, 31, 32 and 33 in the context of IEEE802.11 MAC/PHY
  The mechanisms defined in IEEE802.1Q-2022 target networks with low bandwidth-delay product (5 Mbits or less), specifically Data Center Ethernet. These mechanisms, however, can co-exist and work with higher layer congestion management protocols like L4S.
This submission covers the following:
  What gain does L4S over Wi-Fi provide for Latency-sensitive traffic? At what cost?
  Can Quantized Congestion Notification (.1Q-2020 Cl. 30.2) be used in managed Wi-Fi deployments to achieve bounded latency?

## Slide 3: L4S Performance in a proof-of-concept implementation
Focus is on downlink performance
The medium access used in the setup is EDCA (.11ac and below; no triggered access
Goal was to demonstrate bounded latency for latency-sensitive and throughput-demanding flows in the presence of network load
Setup
  The AP has a dual queue coupled AQM (RFC 9332) implementation (an L4S queue and a non-L4S queue)
  20MHz channel in an open office environment (the channel was in use by other BSSs). Five bi-directional 25 Mbps traffic in 5 AP-STA pairs.
  Single AP-STA pair under test
  5 TCP downstream flows to the STA either TCP-Cubic (non-L4S) and TCP-Prague (L4S)

## Slide 4
Classic Latency
L4S Latency
Classic Thruput
L4S Thruput
P99 Latency
L4S: 13 ms
Classic: 274 ms
Nokia Beacon 6 Wi-Fi AP

## Slide 5: L4S: Tradeoff Through for better latency
As can be seen from the Data Rate Time Series plot, L4S gains latency performance by trading off throughput
    With classic behavior (without L4S), Wi-Fi link would be unusable for interactive latency-sensitive applications.
    L4S enables latency-sensitive apps to maintain latency performance while sending at high rate.

## Slide 6: Detect and Notify Congestion
Tx buffer is getting filled such that the transmission of the one or more of the frames in the queue will exceed the latency deadline for the frame(s)
With IEEE802.11 this depends on the channel conditions, mechanism used to access the channel (EDCA versus Triggered Access)
  L4S operation: In heterogeneous IP networks, L4S provides end-to-end [Transport Layer] Congestion Notification
    The 802.11 MAC has the best knowledge of the channel conditions and can set the ECN bits in the IP header (to congestion experienced),
    Propagates to the Listener which causes a higher layer ECN message to be sent to the Talker
  IEEE802.1Q QCN operation: defined for data-center networks (BDP < 50mbits), can initiate the CP Algorithm as defined in Cl. 30.2.1 of IEEE802.1Q-2022
    Causes an L2 Congestion Notification Message (CNM) to be sent from the Congestion Point directly to the Talker

## Slide 7: General Approach to mitigating latency issues
At each node in the path between the Talker and the Listener, keep buffering small enough to meet latency requirements
Proactively signal congestion conditions and
  Leverage drop-eligibility, if available
  L4S: Provide feedback to the Talker to throttle down transmission (TCP Prague) – requires only support at the Talker, Listener and ‘weak links’
    E.g., adapt to congestion conditions by reducing requirements (drop to a lower video resolution, more aggressive compression, etc.)
  Needs further study: IEEE802.1Q-2022 Congestion Detection/Notification, Congestion Isolation (IEEE802.1Qcz-2023) when Bandwidth Delay Product meets .1Q design constraints
    Requires support in all the nodes end to end
    May fit only constrained deployments (managed networks, factory automation, etc)
Some implementation-specific strategies
  Distinct queues for latency-bound and non-latency-bound traffic (DSCP-agnostic)

## Slide 8: Next Steps
Support for ECN – IP Headers, LLDP TLV (Access Points)
Support for Network Congestion Notification – above the IP layer (e.g., RTP over UDP or TCP headers)
Define primitives for exchange of information from the IEEE802.11 MAC to higher layers
Over-the-air signaling indicating support for L4S
Explore IEEE802.1Q-2022 QCN for managed Wi-Fi deployments (factory automation)
Explore if the benefits of L4S and IEEE802.1Q-2022 QCN are additive

## Slide 9: References
https://mentor.ieee.org/802.11/dcn/23/11-23-2065-00-0wng-l4s-and-implications-for-wi-fi.pptx Greg White (CableLabs)
L4S Architecture: https://datatracker.ietf.org/doc/rfc9330/
Discussion on considerations prior to deploying L4S over Wi-Fi: domos.no/blog/an-introduction-to-l4s
Quantized Congestion Notification: https://www.ietf.org/proceedings/87/slides/slides-87-iccrg-9.pdf
IEEE802.1Q-2022: https://standards.ieee.org/ieee/802.1Q/10323/

## Slide 10: Backup

## Slide 11: TCP Evolution
Reference: Document 11-23/2065r0 (Greg White, CableLabs)
TCP Reno (1986): Uses a linear function to increase window size; low BDP conditions; Packet loss indicates congestion
TCP CUBIC (2008): most deployed flavor; uses a cubic function to increase window size, large BDP conditions; packet loss indicates congestion
TCP Prague: Explicit Congestion Notification [transport layer] messages indicates congestion (no packet loss); early and frequent signaling of congestion prior to any packet loss.

## Slide 12
How does it work
Fairness to Classic traffic: DualPI2 (RFC9332)
Every 15ms
PI2
ect(1), ce
ect(0), non-ect
pC
L4S
Classic
qC
ECN
Classifier
CE marker
Drop
>1ms
qL
&
pL
Network node
Prague
Reno/Cubic
WRR
90%
10%
p²
2p
Congestion Control
Overrules scheduling
Interactive applications
set L4S ECT1 in IP header
and use L4S CC
Download applications
set non-ECT and
use Classic CCs
Slide 12

## Slide 13: Discussion
Tx Queueing strategies
  Single MAC layer Queue
  Dual MAC layer Queues (one for L4S and one for non-L4S) – PoC implementation
Network layer congestion management is orchestrated by L4S and is media agnostic
MAC layer congestion management – as defined in IEEE802.1Q Cl. 30-33
  30.2 CP Algorithm and RP Algorithm need to be revisited for IEEE802.11 media
  Enabled only when Bandwidth Delay Product is less than 50 mbits
  Can this augment congestion management protocol and provide additional benefit?

## Slide 14: End-to-End QoS Enablement in Wired/Wireless (IEEE802.11) deployments
Leveraging .1Qcz mechanisms (IEEE802.1Qcz-2023 Cl. 49) and IEEE802.1Q-2022 Clause 30 (Principles of Congestion Notification)
Low Latency Low Loss Scalable Throughput (L4S)
  a fast and explicit feedback loop from the network node managing the queue latency to the end systems and applications