## Slide 1: Smooth Roaming Follow Up
Date: 2024-01-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Roaming AP MLD
Roaming AP MLD for smooth roaming support includes multiple AP MLDs.
  Roaming AP MLD support is optional at UHR non-AP MLD side.
  Roaming AP MLD is not visible to EHT non-AP MLDs and UHR non-AP MLDs without roaming support.
A MAC SAP address is defined for a roaming AP MLD.
The BA agreement is negotiated between an UHR non-AP MLD and the roaming AP MLD if the UHR non-AP MLD supports the roaming.
The PMKSA, PTK of an UHR non-AP MLD are negotiated between an UHR non-AP MLD and the roaming AP MLD.
Some non-link level MAC features are at MLD level while the other non-link level MAC features are at roaming MLD level.
Two types of roaming are MLD level roaming and optional Link level roaming.
In a roaming AP MLD, a non-AP MLD is identified by AP MLD roaming ID + AID where AID is defined by AP MLD.
The link of roaming AP MLD is identified by AP MLD roaming ID + Link ID where Link ID is defined by AP MLD.
The MLD level features being separated between MLD level and roaming AP MLD level are discussed.
The new Basic ML element, updated BTM and MLD reconfiguration are used for smooth roaming.
AP MLD11
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD12
MLD common MAC
5GHz
AP121
6GHz
AP122
AP MLD13
MLD common MAC
5GHz
AP131
6GHz
AP132
AP MLD14
MLD common MAC
5GHz
AP141
6GHz
AP142
Roaming AP MLD1
Roaming AP
MLD common MAC
Visible to an EHT non-AP MLD and
UHR non-AP MLD without roaming support
Visible to an UHR non-AP MLD
support roaming

## Slide 3: AP MLD Level vs Roaming AP MLD Level Features
The roaming AP MLD level features are
  The features related to discovery, ML setup, roaming,
  the information that doesn’t change when the serving AP MLD is changed,
  Features related to frame exchange context existed at the current serving AP MLD,
The other features are AP MLD level features.
the information on roaming AP MLD level may be at the location common to all AP MLDs, e.g. the distribution of the individually addressed data frames of a non-AP MLD to the current serving AP MLD of the non-AP MLD.

## Slide 4: MLD Level vs Roaming MLD Level MLD Features
The following features are MLD level features:
  Link management
    TID-to-Link mapping, link disable/enable, link recommendation
  BSS parameter critical update
  Multi-Link power management except maximal idle period
    Buffer frame indication, listen interval, WNM sleep mode, power state etc.
  Group-addressed frames
  Management frames
  Multi-link medium access
    STR, NSTR, medium access recovery etc.
  EMLSR, EMLMR

## Slide 5: AP MLD Level vs Roaming AP MLD Level Features
The following features are roaming MLD level features:
  Discovery
  ML setup
  ML reconfiguration if the roaming from the current serving AP MLD to the new serving AP MLD is done through ML reconfiguration
  BSS transition management if it is used for recommending the new serving AP MLD
  Multi-Link power management
    maximal idle period
  Proxy ARP
  For EPCS at least the authority result of non-AP MLD’s usage of EPCS.
    As a general rule, all the services that need the authority of the outside server are roaming MLD level features.
  Block Ack
    This is useful when the reorder buffer, transmit window are transferred from the current roaming AP MLD to the new serving AP MLD.
  Individual-addressed frame delivery without BA agreement
  PMK, PTK, PN
The last three items will be further discussed in the following slides.

## Slide 6: Frame Exchange Context from Current Serving AP MLD to New Serving AP MLD
Frame exchange context for DL frame transmission (Tx)
  PTK, PN for unicast Data frames frames.
  Next SN being used (SN (sequence number) space) for unicast QoS Data frames of each TID addressed to the non-AP MLD that does the smooth roaming.

## Slide 7: Frame Exchange Context from Current Serving AP MLD to New Serving AP MLD
Frame exchange context for UL frame transmission (Rx)
  PTK (same as PTK in Tx part), Replay Counters for unicast Data frames;
    One replay counter for unicast QoS Data frames each TID,
  The duplicate detection cache for unicast QoS Data frames of each TID from the non-AP MLD that has no BA agreement.

## Slide 8: UL TID with BA Agreement
The BA reorder buffer of the current serving AP MLD (the frames in reorder buffer that can’t be sent to up layer) may be moved to the new serving AP MLD or may not be moved to the new serving AP MLD.
  A non-AP MLD needs to know how the roaming AP MLD process the BA reorder buffer.
If the new serving AP MLD acquires the reorder buffer information of the current serving AP MLD, the WinStartB in the new serving AP MLD will be the same as the WinStartB of the current serving AP MLD.
  The discarding of the frames in Transmit Buffer may create unnecessary frame discarding.

## Slide 9: UL TID with BA Agreement
If the new serving AP MLD has no the reorder buffer information of the current serving AP MLD, the WinStartB in the new serving AP MLD will be the SN that is not less than the largest sequence number of the frame that is sent to the upper layer for the further processing.
  The retransmission of the frames whose sequence numbers are less than WinStartB of the new serving AP MLD will be discarded by the new serving AP MLD after roaming to the new serving AP MLD.
  The new serving AP MLD notifies the non-AP MLD the WinStartB of each UL TID with the BA agreement.
    The non-AP MLD uses the WinStartB as its WinStartO.
  The new serving AP MLD flushes its scoreboard context for the non-AP MLD.

## Slide 10: DL TID with BA Agreement
It is up to the roaming AP MLD to decide whether the transmit buffer control (frames in transmit buffer) is moved from the current serving AP MLD to the new serving AP MLD.
The new serving AP MLD may notify the non-AP MLD its WinStartO.
  The non-AP MLD uses the WinStartO to update its WinStartB and WinStartR.
  Another variant is that the BAR is used for such operation.

## Slide 11: NSTR Link Pair for Links associated with Two Serving AP MLDs
For link level roaming, the two links temporally associated with two serving AP MLDs may be NSTR link pair.
In 11be, when two APs of an AP MLD transmit PPDUs to a non-AP MLD simultaneously through two links of a NSTR link pair, the two PPDUs need to stop at the same time.
  This may not be easy to do when two APs belong to tow serving AP MLDs.
Solution 1:
  A non-AP MLD notifies the two serving AP MLDs that its two links associated with the two serving AP MLDs are NSTR link pair.
  When a serving AP MLD intends to use one link of a NSTR link pair to do frame exchanges with the non-AP MLD that announces the NSTR link pair with two serving AP MLDs, the serving AP MLD (related AP in the link) needs to start its TXOP by using (MU-)RTS/CTS frame exchange.
    A variant to this is that another new defined control frame exchange is defined for such purpose where the responding frame notify whether it can continue the TXOP and if it can’t do the frame exchanges now the responding frame notifies the time when it will be available.
  If the non-AP MLD does the frame exchanges with one serving AP MLD through one link of a NSTR link pair and receives a (MU-)RTS in another link of the NSTR link pair from another serving AP MLD, the non-AP MLD will not respond with the CTS.
  The requirement of stopping the two PPDUs at the same time is relaxed.

## Slide 12: NSTR Link Pair for Links associated with Two Serving AP MLDs
Solution 2:
  A non-AP MLD can’t do the link level roaming if two links of the non-AP MLD that associated with two serving AP MLDs belong to a NSTR link pair.
Solution 3:
  A non-AP MLD notifies the two serving AP MLDs that its two links associated with the two serving AP MLDs are NSTR link pair.
  The non-AP MLD negotiates the individual TWT agreements in two links of the NSTR link pair where the individual TWT agreements in two links don’t overlap with each other in time domain.
    The STAs in the links of the NSTR link pair are in power save mode.

## Slide 13: MLSR non-AP MLD with Two Serving AP MLDs
When a MLSR non-AP MLD is associated with two serving AL MLDs at the same time, the two serving AP MLD can’t transmit the PPDUs to the MLSR non-AP MLD at the same.
Solution 1:
  A MLSR non-AP MLD can’t do the link level roaming.
Solution 2:
  A non-AP MLD notifies the two serving AP MLDs that it is MLSR non-AP MLD.
  the non-AP MLD negotiates the individual TWT agreements for two EMLSR links with two serving AP MLDs where the individual TWT agreements in two links don’t overlap with each other in time domain.
  The STAs of the MLSR non-AP MLD are in power save mode.

## Slide 14: EMLSR/EMLMR non-AP MLD with Two Serving AP MLDs
When an EMLSR/EMLMR non-AP MLD is associated with two serving AL MLDs at the same time, one serving AP MLD can’t initiate the frame exchange in one EMLSR/EMLMR link when another AP MLD is doing the frame exchanges in another EMLSR/EMLMR link.
Solution 1:
  An EMLSR/EMLMR non-AP MLD can’t do the link level roaming.
Solution 2:
  A non-AP MLD notifies the two serving AP MLDs that it is EMLSR/EMLMR non-AP MLD.
  the non-AP MLD negotiates the individual TWT agreements in two links of the EMLSR/EMLMR link pair where the individual TWT agreements in two links don’t overlap with each other in time domain.
  The STAs of the EMLSR/EMLMR non-AP MLD are in power save mode.
Solution 3:
  A non-AP MLD notifies the two serving AP MLDs that it is EMLSR/EMLMR non-AP MLD.
  The requirement of no initiating frame exchange in one EMLSR/EMLMR link when doing frame exchanges in another EMLSR/EMLMR link at the same time is relaxed.

## Slide 15: UL TID and DL TID Restriction of Serving AP MLDs
UL TID solution 1:
  After a non-AP MLD has two serving AP MLDs with one serving AP MLD (AP MLD2) as the new serving AP MLD and another serving AP MLD (AP MLD1) as the current serving AP MLD, the frames of UL TIDs will be transmitted to AP MLD2.
UL TID solution 2:
  It is up to the roaming AP MLD to decide whether a non-AP MLD can transmit the frames of the UL TIDs to its two serving AP MLDs during the time when it has two serving AP MLDs.
    The TID-to-link mapping of the two serving AP MLDs can be used, e.g. both serving AP MLD allows the non-AP MLD to transmit frames of UL TIDs to them.
    Another variant is that the non-AP MLD and the roaming AP MLD negotiate whether the two serving AP MLDs can do the frame exchanges for the UL TIDs.
Option 2 is not suitable to TID without BA agreement, Prefer option 1

## Slide 16: UL TID and DL TID Restriction of Serving AP MLDs
It is up to the roaming AP MLD to decide whether the multiple serving AP MLDs transmit the frames of the DL TIDs to a non-AP MLD during the time when the non-AP MLD has two serving AP MLDs.
  The TID-to-link mapping of the two serving AP MLDs can be used, e.g. both serving AP MLD allow them to transmit frames of DL TIDs to the non-AP MLD.
  Another variant is that the non-AP MLD and the roaming AP MLD negotiate whether the two serving AP MLDs can do the frame exchanges for the DL TIDs.
  When the DL frame exchanges can be done with both serving AP MLDs, the current serving AP MLD needs to forward its transmit buffer (WinStartO, WinSizeO, the buffered frames etc.) to the new serving AP MLD

## Slide 17: Summary
The feature separation between roaming AP MLD level and AP MLD level is discussed.
The information of the features at roaming AP MLD that is not stored at a common location needs to switch from the current roaming AP MLD to the new serving AP MLD.
  The information for Data, Management frame exchange.
  The service agreed by the serving AP MLD and still provided in the new serving AP MLD.
The medium access with the links associated with two AP MLDs during roaming is discussed:
  The processing of NSTR/MLSR/EMLSR/EMLMR link pair connected with the current serving AP MLD and the new serving AP MLD.