## Slide 1: Considerations on Multi-AP Operation – Follow Up
Date: 2024-09-09
Authors:

## Slide 2: Abstract
In PAR of P802.11bn, the Ultra High Reliability (UHR) capability has been defined to improve Rate-vs-Range enhancement, reduce latency, and reduce power consumption for AP, compared to Extremely High Throughput (EHT) MAC/PHY operation.
Multi-AP operation (aka. Multi-AP coordination/transmission) has been discussed as one of the key candidate features to meet the requirement of UHR capability.
In this contribution, we share some considerations on multi-AP operation, including the support of selecting multi-AP transmission schemes and the support of scheduling the multi-AP transmission.

## Slide 3: Recap: Multi-AP Operation [1~8]
Multi-AP operation may include several phases/procedures between overlapping basic service sets (OBSSs).
Multi-AP operation procedures may be performed as long-term or short-term operations:
  Long-term operation: e.g., one or more beacon interval level
  Short-term operation: e.g., one or more transmission opportunity (TXOP) level
The multi-AP transmission may be carried in a multi-AP data transmission phase, preceded by one or more multi-AP coordination phases, including a multi-AP selection phase.
Some multi-AP operation procedures may repeat optionally for follow-up or new transmissions.

## Slide 4: Multi-AP Transmission Scheme Selection
The multi-AP selection phase may include frame exchanges to allow a sharing AP (AP1) to determine whether a candidate shared AP (AP2) may participate in a multi-AP transmission.
However, the existing procedure relies on the sharing AP determining a multi-AP transmission scheme without consideration of whether the selected scheme can be adequately performed by the shared AP.
Solution
  The sharing AP and/or the shared AP may support more than one multi-AP transmission schemes.
  The shared AP (AP2) provides the sharing AP (AP1) a preferred multi-AP transmission scheme.
  The sharing AP may consider the preferred multi-AP transmission scheme when selecting a multi-AP transmission scheme by the sharing AP.
  The sharing AP announces to the shared AP the multi-AP transmission scheme.

## Slide 5: Multi-AP Transmission Scheduling
After a sharing AP (AP1) selects a shared AP (AP2) for a multi-AP transmission, the shared AP may become unavailable before the beginning of the multi-AP data transmission phase. (e.g., AP power saving)
Solution 1: Shared AP Unavailability Window
  The shared AP (AP2) signals to the sharing AP (AP1) an unavailability window, during which the shared AP is unavailable to participate in a multi-AP transmission.
  The sharing AP schedules the multi-AP transmission to avoid the unavailability window of the shared AP.
Solution 2: Multi-AP Transmission Window
  The sharing AP (AP1) signals to the shared AP (AP2) a multi-AP transmission window.
  The shared AP responds the sharing AP a decision of participating or not in the multi-AP transmission window.

## Slide 6: Summary
In this contribution, we shared some thoughts on multi-AP operation. We proposed the method of selecting multi-AP transmission schemes and methods of scheduling the multi-AP transmission.

## Slide 7: Q&A Discussion (Sept. 2023)
C: The sharing AP will give the shared AP some notification. for confirmation frame, it could simplify the case. We don’t need to have confirmation frame. It can help AP2 know it is selected. Multi-AP trigger fame serves the same function.
A: Yes, it could be merged with the multi-AP trigger frame. This is an example shows the selection phase. There may be other examples.

## Slide 8: Q&A Discussion (Mar. 2024)
C: What’s the definition of terms used for sharing AP and shared AP?
A: We reuse the terminologies in TGbe SFD [2].
C: It’s better to run SPs after TGbn agreeing the terminology.
A: Two multi-AP coordination modes, i.e. coordinated spatial reuse (CSR) and coordinated beamforming (CBF), are defined in TGbn SFD [1].

## Slide 9: Straw Poll 1
Do you support the following text?
  A shared AP may provide a sharing AP a preferred multi-AP transmission scheme of the shared AP, when the shared AP supports more than one multi-AP transmission schemes.
  Note: the multi-AP transmission schemes may include but not limited to CSR, CBF, C-TDMA, etc.
  Yes
  No
  Abstain

## Slide 10: Straw Poll 2
Do you support the following text?
  A sharing AP and a shared AP may coordinate availability/unavailability periods used for performing a multi-AP transmission.
  Yes
  No
  Abstain

## Slide 11: References
11-24/0209r4, Specification Framework for TGbn
11-19/1262r23, Specification Framework for TGbe
11-18/1982r1, Consideration On Multi-AP Coordination for EHT
11-19/0448r1, Multi-AP Transmission Procedure
11-19/1102r0, A Unified Transmission Procedure for Multi-AP Coordination
11-19/1129r2, Consideration-on Multi-AP Coordination
11-19/1143r3, Efficient Operation for Multi-AP Coordination
11-19/1895r2, Setup for Multi-AP Coordination
11-20/0596r1, AP Candidate Set Follow-AP
11-20/0617r3, Multi-AP Operation Basic Definition
11-22/1512r0, Multi-AP Coordination for UHR
11-22/1515r0, A Candidate Feature Multi-AP
11-22/1530r1, Multi-AP Coordination for Next-generation Wi-fi
11-22/1822r0, Recap On Coordinated Spatial Reuse Operation
11-23/0325r0, Coordinated Spatial Reuse for UHR
11-23/0776r1, Performance Of C-BF And C-SR
11-23/1023r2, Coordinated Spatial Reuse In A 4 AP Topology
11-23/1037r0, Performance Of Coordinated Spatial Reuse
11-23/1832r0, Multi-AP Coordinated Spatial Reuse
11-23/1917r0, Coordinated Spatial Reuse
11-24/0095r0, Efficient Coordinated Spatial Reuse Follow Up
11-24/0529r0, Coordinated Spatial Reuse Discussion
11-24/0577r0, Thoughts On Coordinated Spatial Reuse (C-SR)
11-24/0635r0, Coordinated Spatial Re-use And Coordinated Spatial Nulling Follow-up
11-24/0639r1, MAC Protocol Aspects Of Multi-AP Coordination
11-24/0640r0, Consideration On C-SR Types
11-24/0839r0, System-level Evaluation Of Coordinated Spatial Reuse
11-24/0880r0, CBF Recap And Way Forward
11-24/1204r0, Coordinated Beamforming for 11bn
11-24/1211r1, Coordinated BF Goodput Discussion