## Slide 1: mmWave RTS/CTS
Date: 2024-01-15
Authors:

## Slide 2: Abstract
Multiple contributions [1-4] agree to aggressively reduce complexity and power consumption of IMMW technology.
Some proposals mention that management frames (discovery, association, scheduling) can be supported in the lower bands.
In this contribution, we discuss leveraging the lower bands for RTS/CTS protection.

## Slide 3: mmWave Hidden Node Problem
mmWave transmissions are much more prone to the hidden node problem than sub-7GHz links due to antenna directionality.
Q-omni RTS/CTS range
Omnidirectional pattern
Directional pattern

## Slide 4: RTS/CTS for sub-7GHz Links
Due to generally omnidirectional antenna pattern, RTS/CTS can be reliably received by all STAs in the vicinity of the TXOP holder (AP) and TXOP responder (STA 1)
AP
RTS
STA 1
CTS
DATA
BA
STA 2
STA 2 hears STA 1
STA 3
STA 3 hears AP
STA 4
STA 4 hears AP
and STA 1
AP
STA1
STA3
STA2
STA4
NAV
NAV
NAV

## Slide 5: RTS/CTS for mmWave Links
Due to antenna directionality in mmWave links, RTS or CTS may not be heard reliably by STAs depending on their location. Collisions may still happen even after a successful RTS/CTS exchange.
AP
RTS
STA 1
CTS
DATA
BA
STA 2
STA 2 hears AP
STA 3
STA 3 hears STA 1
STA 4
STA 4 doesn’t hear AP or STA 1
DATA
may result in packet error for AP-STA1 transmission
AP
STA1
STA3
STA2
STA4
NAV
NAV

## Slide 6: Possible solutions
All transmissions are scheduled by the AP.
  Requires developing new or modified MAC protocol (i.e. DMG, E-DMG access, R-TWT)
  Complexity should be minimized.
RTS/CTS transmissions are done omni-directionally
  May require higher transmit powers to support the same range as a directional RTS/CTS.
Leverage sub-7GHz links for NAV protection of mmWave transmissions (e.g. Cross-link RTS/CTS).
  Crosslink synchronization issues for STAs with different response times need to be studied further.
  May require new control frames for cross-link operation.

## Slide 7: Cross-link RTS/CTS 1
AP
Sub 7GHz
mmWave
Duration sub 7GHz = 0
Duration mmWave = T
RTS*
STA 1
Sub 7GHz
mmWave
CTS*
BA
DATA
Other STAs
Sub 7GHz
mmWave
Duration sub 7GHz = 0
Duration mmWave = T
NAV( RTS*)
NAV( CTS*)

## Slide 8: Cross-link RTS/CTS 2
AP
Sub 7GHz
mmWave
Duration sub 7GHz = 0
Duration mmWave = T
RTS*
STA 1
Sub 7GHz
mmWave
CTS*
BA
DATA
Other STAs
Sub 7GHz
mmWave
Duration sub 7GHz = 0
Duration mmWave = T
NAV( RTS*)
NAV( CTS*)
NAV
Duration sub 7GHz = 0
Duration mmWave = T
RTS*
retransmit
NAV( RTS*)
NAVTimeout
CTS*

## Slide 9: Cross-link RTS/CTS 3
AP
Sub 7GHz
mmWave
Duration sub 7GHz = 0
Duration mmWave = T
RTS*
STA 1
Sub 7GHz
mmWave
CTS*
BA
DATA
Other STAs
Sub 7GHz
mmWave
Duration sub 7GHz = 0
Duration mmWave = T
NAV( RTS*)
NAV( CTS*)
NAV
ACK

## Slide 10: Summary
- mmWave links are prone to hidden node problems.
- DMG/EDMG has plenty of mechanisms to solve it but it may result in high complexity.
- We presented an alternative mechanism that leverages the sub-7GHz band to provide NAV protections to the mmWave bands.

## Slide 11: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-1819-00-immw-integrated-mmwave-design-considerations.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-2004-00-immw-technical-scope-proposal.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-1878-00-immw-high-level-design-considerations-of-immw.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-1905-00-immw-high-level-thoughts-on-immw.pptx