## Slide 1: AP Power Management – Follow-up
Date: 2024-01-17
Authors:

## Slide 2: Abstract
There are requirements and recommendations to improve the energy efficiency of APs [1-4].
The previous contribution [5] presents
  A brief summary of existing protocols and proposals [6-15] for scheduled and unscheduled AP power save, for example, utilizing TWT, MLD, EMLSR, etc.
  A proposal of scheduled AP power save to improve the energy efficiency of APs while limiting the negative impact on functionality and performance.
This contribution is a follow-up on scheduled AP power save [5]
  Procedures and operations for AP and non-AP STAs
  Information elements and options for schedule, power state, power state transition, capability, and management information

## Slide 3: Recap: AP Power Save Proposal
The AP balances power save levels and performance requirements by adjusting its schedule & capability. In the scheduled time window, the AP may be in
  Doze state: The AP sends Absence Notification in Beacon, Probe Response, or Action frames to other STAs. The AP remains in the doze state and is absent during the scheduled time window.
  Listen state: The AP remains in the listen state performing CCA or signal detection. The AP may respond to legacy devices or on-demand data in deferred or immediate manners. This state allows everything on the AP to be turned off except for RX signal detection and this may mean the host in the AP is in low power state and the AP would not transmit.
  Reduced capability: The AP may use a reduced capability subset, such as single antenna, reduced BW, etc., instead of utilizing the full capability set.

## Slide 4: Procedures and Operations
Basic operations
  The AP sends out schedule in Beacons and turns into doze/listen state based on the schedule.
  STAs receive the schedule and may turn to doze state during the time window when the AP is in doze/listen state.
Presence Request or schedule change
  STAs may send Presence Request in probe request or Action frames to the AP.
  The AP may accept the request and send the confirmation to STAs in Beacon and response frames.
  The AP may also change the schedule itself without any Presence Request from other STAs.
Schedule update
  If the schedule is changed: the AP shall send the new schedule in Beacons; The AP may send the new schedule in Action/Response frames during the Active state according to the previous schedule.
  STAs need to receive Beacons and Action frames to know the current schedule information.
  STAs may send schedule request to the AP asking for the current schedule. Note that the AP may not receive the request if the AP is in doze state.
  One link of an AP MLD may send the schedule & capability info. of other links. Similarly for RNR and multi-AP.

## Slide 5: Procedures and Operations (Cont.)
Some rules to avoid potential issues
  The AP should not go into doze state if there is any legacy device associated
  STAs should wait for Beacons to know the AP’s status before taking other actions, especially for STAs newly-arrived or in PS
  Backoff counters should be maintained correctly, given AP in doze state may cause confusion about whether the channel is busy or idle. Suspend backoff counter for UHR devices.
  The AP may have a schedule to be in Active state with 20MHz-only primary channel and single antenna to meet power saving requirements while supporting legacy devices and on-demand data.
    The signaling to inform peers is TBD, only applicable to new STAs
STAs in power save mode
  STAs need to know the correct schedule and state of the AP, especially if the schedule is changed
    Operations of APs: send any update in Beacons (don’t change it unless STAs are aware, the AP should decide it directly or indirectly)
    Operations of STAs: listen to Beacons or send schedule request upon waking up
Schedule with the AP in listen state
  If listen state is interrupted/stopped: only the current time window, or the whole schedule instance
Can be used together with unscheduled AP power save, providing predictable behaviors for STAs
Other procedures are TBD: MLD, multi-AP, synchronization, roaming, P2P, etc.

## Slide 6: Information Elements: Schedule and Capability Info.
The AP needs to specify the schedule and capability: when, how long/often, what state/capability
  Option 1: define new information elements for schedule, power state, and capability information
Example 1: AP in doze state
Example 2: AP in 20MHz-only and NSS=1 mode
20MHz-only
(NSS=1)-only
 | Schedule info |  |  |  |  | Power state info |  |  | Extension (capability info) |  |  | 
ID and other info | Start time/offset | Duration | Interval | Count | … | Power state | Power state transition | … | Extension present | Supported channel width | Supported NSS | …
… | 2304 | 51200 | 102400 | 255 | … | Doze | N/A | … | 0 | N/A | N/A | …
… | 2304 | 51200 | 102400 | 255 | … | Active | N/A | … | 1 | 1 | 1 | …

## Slide 7: Information Elements: Schedule and Capability Info. (Cont.)
The AP needs to specify the schedule and capability: when, how long/often, what state/capability
  Option 2: reuse existing information elements. In addition, define new information elements for power state and capability information.
    Example 1: reuse TWT element
Power state info (outside of TWT) |  |  |  | Extension (capability info) |  |  | 
ID and other info | Power state | Power state transition | … | Extension present | Supported channel width | Supported NSS | …
Schedule info (reuse TWT)

## Slide 8: Information Elements: Schedule and Capability Info. (Cont.)
The AP needs to specify the schedule and capability: when, how long/often, what state/capability
  Option 2: reuse existing information elements. In addition, define new information elements for power state and capability information.
    Example 2: reuse TID-To-Link Mapping element in broadcast frames
Power state info (for each link) |  |  |  | Extension (capability info) |  |  | 
ID and other info | Power state | Power state transition | … | Extension present | Supported channel width | Supported NSS | …
Schedule and link info (reuse TID-To-Link Mapping)
Repeat if applicable, or add subfields for periodic/long-term patterns

## Slide 9: Information Elements: Schedule and Capability Info. (Cont.)
The AP needs to specify the schedule and capability: when, how long/often, what state/capability
  Option 2: reuse existing information elements. In addition, define new information elements for power state and capability information.
    Other examples: similar concept to reuse Quiet element or Schedule element

## Slide 10: Information Elements: Presence/Schedule Request
Procedures and IEs needed for STAs/APs to manage the AP’s schedule & capability
  Option 1: Presence/Schedule Request in a single IE with a request type field
  Option 2: Presence/Schedule Request in separate IEs
    STAs can send Schedule Request IE in Probe Request or Action frames to request for the current schedule.
    STAs can send Schedule & Capability IE in Probe Request or Action frames to request to disable AP power save or request for a certain schedule.
    The AP can send Schedule & Capability IE in Beacon or Action frames to STAs to confirm/reject the request.
  Can use existing frames or add subfields, e.g., any legacy or latency sensitive frame can disable AP power save.
0 | STAs request the AP to disable AP power save
1 | STAs request the AP to send out the current schedule
2 | STAs request the AP to use a certain schedule attached
3 | STAs cancel a previous Presence/Schedule Request
… | 
STAs to request the AP not entering a certain state, can either
add new request types
or use request type 2 with the requested schedule attached
ID and other info | Request type | Present for certain request type | …

## Slide 11: Conclusion
This contribution gives a follow-up on scheduled AP power save [5]
  Procedures and operations for AP and non-AP STAs
  Information element options for schedule, power state, capability, and management info.

## Slide 12: References
[1] Dorothy Stanley, Liaison statement from Wi-Fi Alliance re: energy efficiency, IEEE 802.11-23/0917r0, 2023
[2] Amelia Andersdotter, et al., 802.11 AP Power Save PAR addition proposal, IEEE 802.11-23/0244r1, 2023
[3] Amelia Andersdotter, et al., Green AP and resilience requirements for home networks, IEEE 802.11-22/1790r0, 2022
[4] Lili Hervieu, et al., A Perspective on UHR Features for Operator Residential Deployments, IEEE 802.11-22/1809r0, 2022
[5] Yongsen Ma, et al., AP Power Management, IEEE 802.11-23/1835r0, 2023
[6] Liwen Chu, et al., AP MLD power management, IEEE 802.11-23/0015r0, 2023
[7] Alfred Asterjadhi, et al., Considerations for enabling AP power save, IEEE 802.11-23/0010r0, 2023
[8] Guogang Huang, et al., Considering Unscheduled AP Power Save, IEEE 802.11-23/0225r0, 2023
[9] Stefan Aust, AP Power Saving, IEEE 802.11-11/0046r2, 2011
[10] Stefan Aust, TGah Use Case AP Power Saving in Smart Grid, IEEE 802.11-11/0273r0, 2011
[11] Xiaofei Wang, et al., AP Power Saving, IEEE 802.11-17/0728r2, 2017
[12] Xiaofei Wang, et al., On AP Power Saving Usage Model, IEEE 802.11-17/1388r2, 2017
[13] Jay Yang, et al., MLD AP Power-saving(PS) Considerations, IEEE 802.11-20/1115r6, 2020
[14] Kyumin Kang, et al., Considerations on Soft AP Power Saving, IEEE 802.11-21/0885r1, 2021
[15] George Cherian , et al., Enabling AP power save_follow up, IEEE 802.11-23/2040, 2023