## Slide 1: Multi-AP Coordinated Puncturing
Date: 2024-01-13
Authors:
Name | Affiliations | Address | Phone | email
Shawn (Sanghyun) Kim | WILUS Inc. | 216 Hwangsaeul-ro, Seongnam-si, Gyeonggi-do, Korea | +82-31-712-0523 | shawn.kim@wilusgroup.com
John (Ju-Hyung) Son |  |  |  | john.son@wilusgroup.com
Jin Sam Kwak |  |  |  | jinsam.kwak@wilusgroup.com
Greg Geonjung Ko |  |  |  | greg.ko@wilusgroup.com
January 2024
Sanghyun Kim (WILUS), et al.

## Slide 2: Abstract
Many contributions have been submitted on M-AP coordination features;
  Coordinated resource sharing [1][2]
  Coordinated spatial reuse [3][4]
  Coordinated R-TWT [5-10]
  Coordinated transmission [11-13]
Each M-AP feature requires a different level of coordination among APs
  We can consider coordination schemes with a long coordination cycle and infrequent information exchange among APs as low-level M-AP coordination schemes
In this contribution, we propose multi-AP coordinated puncturing which requires low-level of coordination among APs
January 2024
Sanghyun Kim (WILUS), et al.

## Slide 3: Recap: Preamble Puncturing
Disabled Subchannel is defined in EHT
  35.15.2 Preamble puncturing operation (11be D5.0)
AP can disable (static puncturing) any subchannel(s) of the BSS by including Disabled Subchannel Bitmap in the EHT Operation element
    The AP sets a bit in the bitmap to 1 to indicate that the corresponding subchannel as a punctured subchannel of its BSS
    Then, associated STAs of the BSS set the TXVECTOR parameter INACTIVE_SUBCHANNELS of an HE, EHT, or non-HT duplicate PPDU based on the value indicated by the subfield
January 2024
Sanghyun Kim (WILUS), et al.

## Slide 4: Proposed solution
M-AP Coordinated Puncturing
  Coordinating APs exchange operating channel information
    e.g., Primary channel, minimum required BW, etc.
  Then each AP can set subchannel(s) overlapped with primary channel of the other BSS(s) as disabled (punctured) subchannel(s) for its BSS
January 2024
Sanghyun Kim (WILUS), et al.
Disabled Subchannel @BSS1
AP1
AP2
Beacon
(Disabling Ch_3)
P_20 info.
Ch_1 (P_20)
Ch_2
Ch_3 (disabled)
Ch_4
Ch_1 (disabled)
Ch_2
Ch_3 (P_20)
Ch_4
Ch_3
Ch_1
Beacon
(Disabling Ch_1)
Frame exchanges
Frame exchanges
Punctured
Frame exchanges
Frame exchanges
Frame exchanges
Frame exchanges
Frame exchanges
Disabled Subchannel @BSS2
Punctured
LL traffic
LL traffic

## Slide 5: M-AP Coordinated Puncturing
Benefits
  Reducing contentions from OBSS on each BSS’s primary channel
  Allow in-time transmission of Low Latency (LL) traffic
Discussions (details in the following pages)
  Under utilization of disabled subchannel(s)
  When BSSs have the same primary channel
  Relationship with non-primary channel access [14][15][16]
Limited overheads
  Long Coordination Cycle
    After initial coordination, the next coordination would occur only when one of the APs change its primary channel
  Small amount of information for coordination
    Primary channel and required minimum BW to be exchanged
  No new operations defined for Non-AP STAs
    Non-AP STAs follow the EHT’s disabled subchannel operations
January 2024
Sanghyun Kim (WILUS), et al.

## Slide 6: Discussions (1)
Disabled Subchannel @BSS2
(temporal)
Consistently puncturing my BSS’ subchannel(s) for neighbor BSS may lead to channel under utilization ?
  We can consider to apply puncturing only during a specific time period (e.g., R-TWT SP of the neighbor BSS)
January 2024
Sanghyun Kim (WILUS), et al.
AP1
AP2
P_20 info.
&
R-TWT SP info.
Ch_1 (P_20)
Ch_2
Ch_3 (disabled)
Ch_4
Ch_1 (disabled)
Ch_2
Ch_3 (P_20)
Ch_4
Ch_3
Ch_1
Frame exchanges
Frame exchanges
Frame exchanges
R-TWT SP of AP2
R-TWT SP of AP1
Frame exchanges
Frame exchanges
Disabled Subchannel @BSS1
(temporal)
Frame exchanges
Frame exchanges
Frame exchanges
AP2 doesn’t occupy P20 of AP1 during R-TWT SP of AP1
AP1 doesn’t occupy P20 of AP2 during R-TWT SP of AP2

## Slide 7: Discussions (2)
Multi-AP coordination can only be applied to BSSs using different Primary channels?
  During the Multi-AP coordination procedure, one of the AP may consider changing its Primary channel to utilize M-AP coordinated puncturing.
  If two BSSs share the same primary channel and Non-Primary Channel Access is allowed, puncturing subchannels matching to a neighbor BSS’ alternative primary channel (S20 in the example below) would be helpful
January 2024
Sanghyun Kim (WILUS), et al.
AP1
AP2
TXOP of AP1
S20 info.
non-primary channel access mode (Busy_OBSS TXOP)
P20
S20
40 MHz
DL PPDU
BA
40 MHz
DL PPDU
BA
P20
S20: Subchannel for non-primary channel access
80+40 MHz PPDU
(S20 of AP2 is punctured)
S20 of AP2
DL PPDU
DL PPDU
BA
BA
DL PPDU
DL PPDU
BA
BA
40 MHz
DL PPDU
BA
BA
40 MHz
DL PPDU
P20 of AP2

## Slide 8: Summary
In this submission, the Multi-AP Coordinated Puncturing scheme is proposed to
  reduce contentions from OBSS on each BSS’s primary channel,
  which allows in-time transmission of Low Latency (LL) traffic.
January 2024
Sanghyun Kim (WILUS), et al.

## Slide 9: Straw Poll 1
Do you agree that an AP may set disabled subchannel for its BSS based on the primary channel of a neighboring BSS?
January 2024
Sanghyun Kim (WILUS), et al.

## Slide 10: Straw Poll 2
Do you agree to define mechanism(s) where an AP coordinates disabled subchannel(s) of its BSS with neighboring AP(s)?
  Disabled subchannel(s) refers subchannel(s) punctured for the BSS.
  The detail is TBD.
January 2024
Sanghyun Kim (WILUS), et al.

## Slide 11: Reference
[1] 11-23/41 Considerations on Coordinated TDMA (Yanjun Sun)
[2] 11-23/768 Discussion on C-OFDMA operation (Jinyoung Chun)
[3] 11-23/1037 Performance of Coordinated Spatial Reuse (Kanke Wu)
[4] 11-23/325 Coordinated Spatial Reuse for UHR (Jason Yuchen Guo)
[5] 11-23/226 Coordination of R-TWT for Multi-AP Deployment (Abdel Karim)
[6] 11-23/250 AP coordination with R-TWT (Liwen Chu)
[7] 11-23/291 R-TWT Multi-AP Coordination (Muhammad Kumail Haider)
[8] 11-23/293 Follow-up on TWT-based Multi-AP Coordination (Rubayet Shafin)
[9] 11-23/297 rTWT for Multi-AP (Laurent Cariou)
[10] 11-23/771 Coordinated R-TWT Protection in Multi-BSS (SunHee Baek)
[11] 11-22/1821 System Level Simulation of Co-BF and Joint Tx (Kosuke Aio)
[12] 11-23/243 Joint Transmission for UHR - Additional Results (Ron Porat)
[13] 11-23/1176 Multi-AP Simulations: framework and Joint Transmission results (Rainer Strobel)
[14] 11-23/797 Non-primary channel access (Yongho Seok)
[15] 11-23/961 UHR secondary channel access (Minyoung Park)
[16] 11-23/1365 Discussions on Non-primary Channel Access (Sanghyun Kim)
January 2024
Sanghyun Kim (WILUS), et al.