## Slide 1: Uplink Modulations Comparison for AMP Devices
Date: 2024-01-14
Authors:

## Slide 2: Abstract
This comparison provides our views on several modulations, as options to consider for the AMP uplink transmission part, in terms of energy, size and performance, focusing on the analog front end (AFE).
Due to the asymmetry in the capabilities of the stations, we consider the downlink to require a separate analysis.

## Slide 3: Consideration for Uplink of AMP Devices
AMP devices have very low energy storage and thus require very energy efficient transmission in terms of Joules/bit, as well as a very power efficient transmitter.
AMP devices are expected to be very simple with a very small silicon footprint. This requires a very small transmitter in the AMP device tag.
AMP devices have very limited information to transmit. No more than few hundreds bits

## Slide 4: Considered Modulations
Even though there are many modulations, we wanted to focus the comparison on the common and well-known ones.
On/Off Keying (OOK)
  Used for 802.11ba, RFID,
FSK: MSK, BFSK, 4-FSK
  Used for Bluetooth, Zigbee, GSM,…
PSK: BPSK, QPSK
  Used for DSSS+CCK+RFID
OFDM (orthogonal frequency domain modulation)
  Used for WiFi, LTE, …

## Slide 5: Minimal Transmitter Complexity
We estimate a minimal complexity of a transmitter for the compared modulations, taking into account only deployed and established technologies and architectures.
OOK
  Requires local oscillator (LO) with fast ON/OFF switching.
MSK, BFSK, 4-FSK
  Requires frequency controlled LO (e.g. [1])
  Frequency can be changed by control of the oscillator
BPSK/QPSK
  Requires I only TX chain for BPSK, I+Q for QPSK
  LO+Mixer+base band+PA are required in order to change phase of the signal
OFDM
  Requires full, multi-bit, I+Q TX chain, with a good EVM
133nH
~
Control
PA
mod
~

## Slide 6: Low Power Transmitter AFE - Power Consumption Estimations
Required components in the TX-AFE per modulation | Local Oscillator/ Power Oscillator (LO/PO) | DAC | I&Q Baseband | Mixer + Drivers | PA | Examplary total AFE power consumption
OOK | ✓ |  |  |  |  | 100uW
MSK/BFSK/4-FSK | ✓ |  |  |  |  | 100uW
BPSK | ✓ | ✓ | ✓ | ✓ | ✓ | 500uW
OFDM | ✓ | ✓ | ✓ | ✓ | ✓ | 1.5mW
For the example above, we assumed the AFE architectures from previous slide, without a crystal, with a 1000ppm accuracy and with a target EIRP of -25dBm
Additional power consumption of digital parts and other components was not included

## Slide 7: Performance
OOK
  Sensitive to interference and to various system noises like DC or active gains – works in high SNRs
  Less suitable for long ranges (>50m) and high bandwidths, since the equalizer is less efficient for these modulations
MSK/BFSK/4-FSK/BPSK/QPSK
  Work in low SNRs (for binary signaling)
  Less suitable for long ranges (>50m) and high bandwidths, since the equalizer is less efficient for these modulations
OFDM
  Medium/high SNR
  Efficient equalization for frequency selective fading channels, suitable for long ranges (>50m) with high delay spreads.

## Slide 8: Example for Energy Consumption
Energy consumption is a combined measure of transmission rate and power consumption. As such, it depends on the required modulation and link performance.
For this analysis we focused on ranges of 5 and 20m
 |  | 1 | 4 | 8
FSK/OOK | 100 | 51.2 | 12.8 | 6.4
BPSK | 500 | 256.0 | 64.0 | 32.0
OFDM | 1500 | 768.0 | 192.0 | 96.0
Rate [Mbps]
Power [uW]
AFE energy consumption estimation [nJ] for transmission of 512bits
 | 1 | 4 | 8
5 | 28 | 22 | 19
20 | 16 | 10 | 7
BW [MHz]
Range [m]
SNR [dB] for NF=7dB and EIRP=-25dBm
for the 2.4GHz band and Friis channel
Energy efficiency [Eemitted/Econsumed] | Energy efficiency
FSK/OOK | 3.2%
BPSK | 0.6%
OFDM | 0.2%

## Slide 9: Uplink Receiver Complexity
We consider, for this analysis, non-backscatter based receivers
Since the uplink receiver is not located in the tag, its complexity is a lower priority for modulation selection compared with the transmitter complexity
On/Off Keying (OOK)
  Energy collection for low sensitivity (NF>25dB), or full chain RX for medium sensitivity
FSK (MSK, BFSK, 4-FSK)
  PLL for low sensitivity, or full chain RX for good sensitivity
BPSK/QPSK
  IQ full chain RX for good sensitivity
OFDM (orthogonal frequency domain modulation)
  Full chain RX with good sensitivity

## Slide 10: Summary
 | OOK | MSK/BFSK/4-FSK | BPSK | OFDM
TX complexity | Good | Good | Fair | Poor
Energy consumption | Poor [due to SNR] | Good | Poor | Poor
Link budget | Poor | Good | Good | Good
From the analysis, it appears that FSK (MSK/BFSK/4-FSK) provides a good tradeoff for AMP uplink, from an AFE perspective.
Further modem simulations are needed for a modem performance comparison before deciding on the modulation.

## Slide 11: References
[1] P. P. Mercier, S. Bandyopadhyay, A. C. Lysaght, K. M. Stankovic and A. P. Chandrakasan, "A 78 pW 1 b/s 2.4 GHz radio transmitter for near-zero-power sensing applications," 2013 Proceedings of the ESSCIRC (ESSCIRC), Bucharest, Romania, 2013, pp. 133-136, doi: 10.1109/ESSCIRC.2013.6649090.