## Slide 1: Bluetooth isochronous audio with LBT
Author:
Name | Affiliation | Address | Email
Menzo Wentink | Qualcomm | Utrecht, The Netherlands | mwentink qti qualcomm

## Slide 2: Introduction
These slides contain simulation results for Bluetooth isochronous audio in the presence of a Wi-Fi XR link
  for low and high pathloss on the Bluetooth link

## Slide 3: BT isochronous audio
left
right
1st try
2nd try
(optional)
3rd try
(optional)
4th try
(optional)

## Slide 4: Simulation settings – BLE
BLE settings
  14 dBm at central and peripheral
  360 us Tx time at central (audio), 150 us IFS, 172 us Tx time at peripheral (Ack)
  14% duty cycle (assuming no interference)
  2 MHz channel width
  Rx level on BLE link: –33 dBm
  Rx level of BLE at Wi-Fi: –50 dBm
  BLE stays on the same channel (no hopping)
  BLE uses single shot CCA, both before the audio packet and the Ack
  CCA might be extended (with reservation signal) or random backoff and floating Tx
  Isochronous audio traffic profile
  Audio is retried when CCA is busy or when no Ack received
  BLE starts at 0 s

## Slide 5: Simulation settings – Wi-Fi
Wi-Fi settings
  14 dBm at AP and STA
  160 MHz, MCS2, 2x2, 800 ns GI (432 Mbps)
  75 Mbps fixed rate (XR/VR)
  max 3 ms / A-MPDU
  14 ms average interarrival time (72 Hz)
  22% duty cycle without interference
  RTS/CTS/A-MPDU/BA frame exchange
  Rx level on Wi-Fi link: –66 dBm
  Rx level of Wi-Fi at BLE: –50 dBm
  Wi-Fi starts at 5 s

## Slide 6: Topology
-50 dBm
-50 dBm
-50 dBm
-66 dBm
-66 dBm
BLE
Wi-Fi
XR/VR
att 34 dB
(pl 80 dB)
fixed

## Slide 7: Simulation results
There are 4 groups of plots
  Bluetooth latency CDFs
  Wi-Fi latency CDFs
  Bluetooth latency in time domain
  Wif-Fi throughput in time domain
There are 5 types of experiments
  Bluetooth without Wi-Fi / Wi-Fi without Bluetooth
  Bluetooth with LBT (short CCA before Tx)
  Bluetooth with extended LBT
  Bluetooth with extended LBT and short IFS
  Bluetooth with sliding Tx (random backoff, EDCA type)

## Slide 8: Bluetooth latency CDFs

## Slide 9: Bluetooth latency without Wi-Fi
nb_r3501f1
(Latency CDF)

## Slide 10: Bluetooth / LBT latency with Wi-Fi
nb_r3603d1
There are 1.7% more Bluetooth transmissions than without LBT, due to non-transmitted Acks (caused by CCA busy at the peripheral)
Audio glitch threshold (7.5 ms)
The audio CDF stays well below the glitch threshold
(Latency CDF)
1 try
2 tries
3 tries

## Slide 11: Bluetooth / LBT with extened CCA latency with Wi-Fi
nb_r3603b1
There are 1.7% more Bluetooth transmissions than without LBT, due to non-transmitted Acks (caused by CCA busy at the peripheral)
The audio CDF stays well below the glitch threshold
Audio glitch threshold (7.5 ms)
(Latency CDF)
1 try
2 tries
3 tries

## Slide 12: Bluetooth / LBT with extended CCA and short IFS latency with Wi-Fi
nb_r3603c1
There are 1.7% more Bluetooth transmissions than without LBT, due to non-transmitted Acks (caused by CCA busy at the peripheral)
Audio glitch threshold (7.5 ms)
The audio CDF stays well below the glitch threshold
(Latency CDF)
1 try
2 tries
3 tries

## Slide 13: Bluetooth / LBT with sliding audio
nb_r3701a1
(Latency CDF)
Audio glitch threshold (7.5 ms)
The audio CDF stays well below the glitch threshold
The maximum delay is about 12% shorter than when slotted transmissions are used

## Slide 14: Bluetooth / no LBT latency with Wi-Fi
nb_r3501f1
(Latency CDF)
Audio glitch threshold (7.5 ms)

## Slide 15: Wi-Fi latency CDFs

## Slide 16: Wi-Fi latency without Bluetooth
nb_r3501c3
(Wi-Fi latency CDF)

## Slide 17: Wi-Fi latency with Bluetooth / LBT
nb_r3603d1
The Wi-Fi CDF shows only a minor deviation, caused by Wi-Fi sometimes deferring until the Bluetooth transmission has finished, while Bluetooth uses LBT to avoid collisions with Wi-Fi transmissions
(Wi-Fi latency CDF)
Minor deviation, caused by Wi-Fi deferring for Bluetooth

## Slide 18: Wi-Fi latency with Bluetooth / LBT with extended CCA
The Wi-Fi CDF shows only a minor deviation, caused by Wi-Fi sometimes deferring until the Bluetooth transmission has finished, while Bluetooth uses LBT to avoid collisions with Wi-Fi transmissions
nb_r3603b1
(Wi-Fi latency CDF)
Minor deviation, caused by Wi-Fi deferring for Bluetooth

## Slide 19: Wi-Fi latency with Bluetooth / LBT with extended CCA and short IFS
The Wi-Fi CDF shows only a minor deviation, caused by Wi-Fi sometimes deferring until the Bluetooth transmission has finished, while Bluetooth uses LBT to avoid collisions with Wi-Fi transmissions
nb_r3603c1
(Wi-Fi latency CDF)
Minor deviation, caused by Wi-Fi deferring for Bluetooth

## Slide 20: Wi-Fi latency with Bluetooth / LBT with sliding audio
The Wi-Fi CDF shows only a minor deviation, caused by Wi-Fi sometimes deferring until the Bluetooth transmission has finished, while Bluetooth uses LBT to avoid collisions with Wi-Fi transmissions
nb_r3701a1
(Wi-Fi latency CDF)
Minor deviation, caused by Wi-Fi deferring for Bluetooth

## Slide 21: Wi-Fi latency with Bluetooth / no LBT
nb_r3501e1
The tail is caused by preambles or Block Acks being hit by Bluetooth packets, and possibly also by an avalanche effect where retries are again hit by interference. When the MCS is reduced (not assumed in this simulation, which is fixed MCS), an avalanche effect is almost certain to further degrade the CDF.
(Wi-Fi latency CDF)
Significant degradation when Bluetooth uses no LBT, due to retries

## Slide 22: Bluetooth latency in time domain

## Slide 23: Bluetooth ISO latency without Wi-Fi
nb_r3501f1
1st try goes through
Audio glitch threshold (7.5 ms)
(ISO audio delay in time domain)

## Slide 24: Bluetooth / LBT ISO latency with Wi-Fi
nb_r3603d1
The audio latency stays well below the glitch threshold
2nd try goes through
1st try goes through
3rd try goes through
The latency pattern is caused by aliasing between the ISO schedule and the Wi-Fi XR arrival schedule
(ISO audio delay in time domain)
Audio glitch threshold (7.5 ms)

## Slide 25: Bluetooth / LBT with extended CCA ISO latency with Wi-Fi
The audio latency stays well below the glitch threshold
2nd try goes through
1st try goes through
3rd try goes through
The latency pattern is caused by aliasing between the ISO schedule and the Wi-Fi XR arrival schedule
nb_r3603b1
(ISO audio delay in time domain)
Audio glitch threshold (7.5 ms)

## Slide 26: Bluetooth / LBT with extended CCA and short IFS ISO latency with Wi-Fi
The audio latency stays well below the glitch threshold
2nd try goes through
1st try goes through
3rd try goes through
nb_r3603c1
(ISO audio delay in time domain)
The latency pattern is caused by aliasing between the ISO schedule and the Wi-Fi XR arrival schedule
Audio glitch threshold (7.5 ms)

## Slide 27: Bluetooth / LBT with sliding audio
nb_r3701a1
(ISO audio delay in time domain)
The audio latency stays well below the glitch threshold
The latency pattern is caused by aliasing between the ISO schedule and the Wi-Fi XR arrival schedule
Audio glitch threshold (7.5 ms)

## Slide 28: Bluetooth / no LBT ISO latency with Wi-Fi
nb_r3501f1
1st try goes through
(ISO audio delay in time domain)
Audio glitch threshold (7.5 ms)

## Slide 29: Wi-Fi throughput in time domain

## Slide 30: Wi-Fi throughput without Bluetooth
nb_r3501c3
(Time domain)
The sawtooth shape is due to the relatively short bin size

## Slide 31: Wi-Fi throughput with Bluetooth / LBT
nb_r3603d1
(Time domain)
The sawtooth shape is due to the relatively short bin size
The delays due to CCA busy are small and do not have any impact on the throughput curve

## Slide 32: Wi-Fi throughput with Bluetooth / LBT with extended CCA
nb_r3603b1
(Time domain)
The sawtooth shape is due to the relatively short bin size
The delays due to CCA busy are small and do not have any impact on the throughput curve

## Slide 33: Wi-Fi throughput with Bluetooth / LBT with extended CCA and short IFS
nb_r3603c1
(Time domain)
The sawtooth shape is due to the relatively short bin size
The delays due to CCA busy are small and do not have any impact on the throughput curve

## Slide 34: Wi-Fi throughput with Bluetooth / LBT with sliding audio
nb_r3603c1
(Time domain)
The sawtooth shape is due to the relatively short bin size
The delays due to CCA busy are small and do not have any impact on the throughput curve

## Slide 35: Wi-Fi throughput with Bluetooth / no LBT
nb_r3501e1
(Time domain)
The average throughput of 75 Mbps is maintained, but with high 'catch up' peaks and increased overhead for retries

## Slide 36: Higher pathloss on Bluetooth link

## Slide 37: Topology 2 – High pathloss on Bluetooth link
-50 dBm
-50 dBm
-50 dBm
-66 dBm
-66 dBm
BLE
Wi-Fi
XR/VR
att 34 dB
(pl 80 dB)
fixed
High pathloss
Wi-Fi interference is destructive for the Bluetooth packets

## Slide 38: Simulation results
There are 4 groups of plots
  Bluetooth latency CDFs
  Wi-Fi latency CDFs
  Bluetooth latency in time domain
  Wif-Fi throughput in time domain
There are 2 types of experiments
  Bluetooth with extended LBT and short IFS
  Bluetooth without LBT

## Slide 39: Bluetooth latency CDFs

## Slide 40: Bluetooth / LBT with extended CCA and short IFS latency with Wi-Fi
nb_r3803c1
Audio glitch threshold (7.5 ms)
The audio CDF stays well below the glitch threshold
(Latency CDF)
High pathloss on BT link
1 try
2 tries
3 tries

## Slide 41: Bluetooth / no LBT latency with Wi-Fi
nb_r3803c1
(Latency CDF)
Audio glitch threshold (7.5 ms)
High pathloss on BT link
1 try
2 tries
3 tries
4 tries
glitch

## Slide 42: Wi-Fi latency CDFs

## Slide 43: Wi-Fi latency with Bluetooth / LBT with extended CCA and short IFS
The Wi-Fi CDF shows only a minor deviation, caused by Wi-Fi sometimes deferring until the Bluetooth transmission has finished, while Bluetooth uses LBT to avoid collisions with Wi-Fi transmissions
nb_r3803c1
(Wi-Fi latency CDF)
High pathloss on BT link
Minor deviation, caused by Wi-Fi deferring for Bluetooth

## Slide 44: Wi-Fi latency with Bluetooth / no LBT
nb_r3801e1
There is no meaningful Wi-Fi latency CDF in this case because the Bluetooth retries are so numerous that the Wi-Fi throughput is only half the target throughput and therefore the delay just keeps growing.
(Wi-Fi latency CDF)
High pathloss on BT link

## Slide 45: Bluetooth latency in time domain

## Slide 46: Bluetooth / LBT with extended CCA and short IFS ISO latency with Wi-Fi
The audio latency stays well below the glitch threshold
2nd try goes through
1st try goes through
3rd try goes through
nb_r3803c1
(ISO audio delay in time domain)
The latency pattern is caused by aliasing between the ISO schedule and the Wi-Fi XR arrival schedule
High pathloss on BT link
Audio glitch threshold (7.5 ms)

## Slide 47: Bluetooth / no LBT ISO latency with Wi-Fi
Audio glitch threshold (7.5 ms)
The Buetooth audio latency exceeds the audio glitch threshold in most cases
2nd try goes through
1st try goes through
3rd try goes through
nb_r3603c1
(ISO audio delay in time domain)
High pathloss on BT link

## Slide 48: Wi-Fi throughput in time domain

## Slide 49: Wi-Fi throughput with Bluetooth / LBT with extended CCA and short IFS
nb_r3803c1
(Time domain)
The sawtooth shape is due to the relatively short bin size
The delays due to CCA busy are small and do not have any impact on the throughput curve
High pathloss on BT link

## Slide 50: Wi-Fi throughput with Bluetooth / no LBT
nb_r3801e1
(Time domain)
The Wi-Fi throughput is only about half the target throughput in this case, due to the continuous Bluetooth audio retries
High pathloss on BT link

## Slide 51: Conclusions

## Slide 52: Conclusions
Bluetooth with LBT works very well in the given scenario where Wi-Fi XR and Bluetooth ISO audio are present in the same channel
  no glitches in the Bluetooth audio
  minor deterioration of the Wi-Fi latency CDF
  extending the CCA and reducing the IFS gives some improvement
  using a random backoff and sliding Tx provides a bit more improvement
  these results are worst case for both technologies, because no hopping is assumed for Bluetooth
  when hopping is used and partly outside the Wi-Fi channel, the results will be even better

## Slide 53: References

## Slide 54: References
NBFH / NB-UWB
  11-23-1738-01-coex-bluetooth-sig-6-ghz-november-2023-update (IEEE Hawaii, November 2023)
  11-23-1259-01-coex-effect-of-no-lbt-nb-on-802-11-devices (IEEE Hawaii, November 2023)
  11-23-2081-00-coex-ble-interference-to-xr-vr-wi-fi (IEEE Hawaii, November 2023)
  BRAN(23)121013_NB_simulation_results_comparison (ETSI BRAN Nice, France, October 2023)
  11-23-1622-00-coex-nbfh-coexistence-with-wi-fi (IEEE Atlanta, September 2023)
  11-23-1503-00-coex-bluetooth-wi-fi-coexistence-channel-access-simulation-study (IEEE Atlanta, September 2023)
  11-23-1279-00-coex-nb-with-lbt (IEEE Berlin, July 2023)
  11-23-0877-00-coex-narrow-coex-studies (IEEE Orlando, May 2023)
  11-23-0455-00-coex-wi-fi-deferral-for-nb-signals (IEEE Atlanta, March 2023)
  11-23-0454-00-coex-impact-of-bt-on-wlan-performance (IEEE Atlanta, March 2023)
  11-23-0453-00-coex-nb-overview (IEEE Atlanta, March 2023)
  BT SIG Bluetooth_Wifi_coex_LBTvsEDAA_intel_aug2023
  BRAN(21)109h004r2_EN_303_687_NB_Proposals_for_DAA_Optimisation
  BRAN(21)109h007_NB_coexistence_with_WB_in_6_GHz
  ETSI EN 300 328 (2.4 GHz)
  ETSI EN 301 893 (5 GHz)
  ETSI EN 303 687 (6 GHz)