## Slide 1: Channel raster considerations for 60GHz band in IMMW
Authors:
Name | Affiliations | Address | Phone | email
Micky Mehta | Pharrowtech BV |  |  | micky.mehta@pharrowtech.com
Date: 2024-01-16

## Slide 2: Introduction
Use of 60GHz band in WLAN and WPAN technologies is not new
  802.15.3c, 802.11ad (DMG) and 802.11ay (EDMG) are well known
But unlike before, we’re now considering integrating a 60GHz front-end to existing MAC & PHY specifications operating largely in sub-7GHz [1]
  … and so how much and what aspects of the existing specs should we modify, if at all?
802.11ad,
802.11ay
802.11ac MAC & PHY, and possibly beyond to include 802.11ax, 802.11be …

## Slide 3: Existing 60GHz band channelization in 802.11
Ref: IEEE Std 802.11ay-2021; "Amendment 2: Enhanced Throughput for Operation in License-exempt Bands above 45 GHz"
EDMG channel BWs are multiples of 2.16GHz
  Spacing f in multiples of 1.08GHz is specified
  [2.16+2.16] GHz
  4.32GHz, [4.32+4.32] GHz, 6.48GHz … etc
We propose reducing f in multiples of 2n
  Where n = [0,-1,-2,-3]
  1080MHz, 540MHz, 270MHz etc
CBWs and spacing closer to sub-7GHz channel raster
  E.g., better fit for 160MHz and 320MHz CBWs, resp.
  Maintain backwards compatibility with (E)DMG
  Benefit CCA detection

## Slide 4: Sub-channelization to narrower bandwidths
48 channels, each of 270MHz CBW
24 channels, each of 540MHz CBW
12 channels, each of 1080MHz CBW
6 channels, each of 2160MHz CBW
Channel#1
Channel#6

## Slide 5: Summary
A plausible channelization scheme for 60GHz band has been proposed
  Maintain primary (legacy) channel spacing of 2.16GHz
  Support whole fractions of the primary, such that f =2n, where n=[0,-1,-2,-3]
  It retains backwards compatibility with incumbent 60GHz amendments in 802.11
Offers a relatively easier path for candidate implementation [2], [3]
  Reduced complexity and development time-scales
  In keeping with the desire to have the IMMW PAR focused and towards rapid adoption
  Offers a rapid path to realistic implementation with an upclocked 802.11ac modem
RF impairments are pronounced in mmWave band; and consensus on how to mitigate and/or circumvent will take due consideration in IMMW SG [4]
  Agreeing on likely channel raster particulars now will help IMMW SG better focus on RF impairments and related discussions

## Slide 6: References
[1] 11-23/1819r1 “Integrated mmWave Design Considerations”
[2] 11-23-2004r0, “IMMW technical scope proposal”
[3] 11-23/1905r0 “High Level Thoughts on IMMW”
[4] 11-23/1878r0 “Design Considerations on IMMW”
[5] 11-23/1968r0 “Discussion on general direction of integrated mmWave”