## Slide 1: TGbn Motions List - Part 1
Date: 2024-01-18
Authors:

## Slide 2: IEEE 802.11 TGbn: Enhancements for Ultra High Reliability (UHR) WLAN Task Group
Motions List from January 2024
Chair: Alfred Asterjadhi (Qualcomm Inc.)
Vice Chairs: Laurent Cariou (Intel), Jianhan Liu (Mediatek), Kiseon Ryu (NXP)
Secretary: Yusuke Asai (NTT)
Technical Editor: Ross Jian Yu (Huawei)
PHY Ad-hoc chairs: Dongguk Lim (LGE), Sigurd Schelstraete (MaxLinear), Tianyu Wu (Apple)
MAC Ad-hoc chairs: Srinivas Kandala (Samsung), Jeongki Kim (Ofinno), Xiaofei Wang (Interdigital)

## Slide 3: Motions on January 18th

## Slide 4: Motion 1 (PHY)
Move to add the following text to the TGbn SFD
11bn supports a distributed-tone RU (DRU) for a TB PPDU transmission
  The DRU means an RU which consists of subcarriers spreading across a certain bandwidth
Move: Eunsung Park Second: Jianhan Liu
Discussion: Some discussion.
Preliminary Result: 116Y, 6N, 48A (pass)
Result: 113Y, 6N, 47A (pass)
Note: Discussed in one of the PHY ad-hoc sessions (ref: 11-23/1919r1) during which a similar SP was run. The SP did not receive any objections.

## Slide 5: Motion 2 (MAC)
Move to add the following text to the TGbn SFD
  11bn defines a mechanism that enables a non-AP MLD to roam from one AP MLD to another AP MLD and the non-AP MLD remains in state 4 (see 11.3) during and after roaming to the other AP MLD
Move: Po-Kai Huang Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref: 23/1884r2, 23/1898r1, 23/1908r2, 23/1937r1, 23/1971r2, 23/1996r0, 23/2157r2) during which a similar SP was run. The SP result was 83Y, 22N, 22A.

## Slide 6: Motions on March 14th

## Slide 7: Motion 3 (PHY)
Move to add the following text to the TGbn SFD
  11bn will define distributed tone RU (“DRU”) transmission
Move: Bin Tian Second: Lin Yang
Discussion: Some.
Preliminary Result: 136Y, 37N, 46A.
Result: 133Y, 36N, 43A (pass).
Note: Discussed in one of the PHY ad-hoc sessions of the January Interim, (ref: 11-23/1988r2) during which a similar SP was run. The SP did not receive any objections.

## Slide 8: Motion 4 (PHY)
Move to include the following into the 11bn SFD
DRU is allowed in a punctured UHR TB transmission.
Move: Ross J. Yu Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-23/2200r3) during which a similar SP was run. The SP did not receive any objections.

## Slide 9: Motion 5 (PHY)
Move to add the following text to the TGbn SFD:
11bn supports hierarchical pilot structure for DRU
  Pilot locations of a larger DRU is a subset of pilot locations of smaller component DRUs within the same PPDU BW
Move: Lin Yang Second: Eunsung Park
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-24/0501r2) during which a similar SP was run. The SP did not receive any objection.

## Slide 10: Motion 6 (PHY)
Move to add the following text to the TGbn SFD
The number of pilot tones for the same size DRU and RRU (regular RU) is the same
  The RRU means the existing RU defined in 11ax and 11be
Move: Eunsung Park Second: Stephen Palm
Discussion: Some.
Preliminary Result: 133Y, 23N, 49A
Result: 129Y, 23N, 47A (pass)
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-24/0402r1) during which a similar SP was run. The SP did not receive any objection.

## Slide 11: Motion 7 (PHY)
Move to add the following text to the 11bn SFD:
11bn supports the hybrid mode with DRUs (Distributed tone RU) and RRUs (Regular RU as existing RU defined in 11ax/be) in UHR UL TB OFDMA transmissions
  Minimum PPDU BW for hybrid mode is TBD
Move: Shengquan Hu Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the PHY ad-hoc sessions of the March plenary, (ref: 11-24/477r2) during which a similar SP was run. The SP did not receive any objection.

## Slide 12: Motion 8 (MAC)
Move to add the following text to the TGbn SFD
11bn defines a mechanism that when a non-AP MLD roams from one AP MLD to another AP MLD, the context related to the non-AP MLD is transferred from the one AP MLD to the other AP MLD such that it preserves the data exchange context for the non-AP MLD.
  Details of the context (e.g., security association context) that can be transferred are TBD
  Framework to transfer the context is TBD.
Move: Po-Kai Huang Second: Gaurav Patwardhan
Discussion: Some.
Preliminary Result: 122Y, 71N, 34A
Result: 121Y, 71N, 34A (fails)
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref: 23/0322r0, 23/1884r2, 23/1897r0, 23/1908r2, 23/1937r1, 23/1971r2, 23/1996r0, 23/2157r2) during which a similar SP was run. SP result was 100Y, 28N, 18A.

## Slide 13: Motion 9 (MAC)
Move to add to the TGbn SFD:
TGbn defines a power save mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)
  Initial Control frame is TBD
  Whether that applies for a non-mobile AP is TBD
Move: Laurent Cariou Second: Ming Gan
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref: 23/10, 23/1875, 23/1936, 23/1965, 23/2003). SP result was: 101Y/11N/23A.

## Slide 14: Motion 10 (MAC)
Move to add to the TGbn SFD:
TGbn defines cross link power save signaling mechanism
  Allowing a non-AP MLD to indicate to its associated AP MLD that supports the mechanism, in a frame sent on one enabled link, the power management mode for one or more of its affiliated non-AP STAs
  Whether support for the mechanism is mandatory or optional is TBD
Move: Laurent Cariou Second: Rakesh Taori
Discussion: None.
Result: Approved with unanimous consent.
Note: Discussed in one of the MAC ad-hoc sessions (several submissions were discussing similar concept, ref:11-23/2003, 11-24/0602). SP result was: 122Y/23N/32A

## Slide 15: Motions on May 16th

## Slide 16: Motion 11 (MAC)
Move to add the following text to the TGbn SFD:
TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
  A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.
Move: Minyoung Park Second: Yunbo Li
Discussion: Some discussion. Recorded vote requested.
Preliminary Result: 209 (+1)Y, 7N, 31A.
Result: 199(+1)Y, 7N, 28A (pass).
Note: Discussed in several sessions and several submissions discuss similar concept, ref: [23/1911r0, 23/1913r2, 23/1935r1, 23/2005r1, 23/2023r1, 24/0070r1, 24/458r0, 24/486r0, 24/538r0, 24/670]. No objection to the SP.

## Slide 17: Motion 12 (MAC)
Move to add the following text to the TGbn SFD:
Define a way in 11bn to include in an initial control frame an intermediate FCS for UHR STA(s) that precedes padding and the FCS field
Move: Laurent Cariou Second: Ming Gan
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference documents are [11-23/1873, 11-23/2003] No objection to the SP.

## Slide 18: Motion 13 (MAC)
Move to add the following text to the TGbn SFD:
TGbn enables per-TID buffer size reporting of a larger queue in UHR
  Note: It is an optional feature.
  Note: In the baseline, the maximum approximate per-TID queue size to report is 2,147,328 octets
Move: Frank Hsu Second: Bruce Kang
Discussion: Some clarificatory discussion.
Result: Approved with unanimous consent.
Note: Reference document is 11-23/2007r2. No objection to the SP.

## Slide 19: Motion 14 (PHY)
Move to add the following text to the TGbn SFD:
DRUs tone plan design on distribution BW 20MHz and 40MHz is 26-tone RU based DRU method (using 26-tone DRUs as basic building blocks).
  DRUs tone plan design on other distribution BWs is TBD.
Move: Shengquan Hu Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/468r2. No objection to the SP.

## Slide 20: Motion 15 (PHY)
Move to add the following text to the TGbn SFD:
Global CSD is used for DRU UHR-STF transmission to solve unintentional beamforming issue
Global CSD is applied in each distribution BW
Move: Lin Yang Second: Sameer Vermani
Discussion: Some clarificatory questions.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/752r2. No objection to the SP.

## Slide 21: Motion 16 (PHY)
Move to add the following text to the TGbn SFD:
DRU transmission reuses the 8 CSD table/values in 11ax/be for global CSD allocation
Move: Lin Yang Second: Bo Gong
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/752r2. No objection to the SP.

## Slide 22: Motion 17 (PHY)
Move to add the following text to the TGbn SFD:
11bn defines frequency domain aggregation of PPDUs. A frequency domain aggregated PPDU consists of multiple PPDUs.
  The PPDU format combinations are TBD.
  The number of PPDUs is TBD.
Move: Ross J. Yu Second: Yan Xin
Discussion: Some discussion. Recorded vote requested.
Preliminary Result: 120Y, 75N, 57A.
Result: 115Y, 72N, 55A (fails).
Note: Reference document is 11-24/224r2. SP result: 68Y/20N/8A.

## Slide 23: Motion 18 (PHY)
Move to add the following text to the TGbn SFD:
The UHR-STF for DRU in a TB PPDU uses 11ax/11be trigger based STF sequences.
Move: Bo Gong Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/749r2. No objection to the SP.

## Slide 24: Motion 19 (PHY)
Move to add the following text to the TGbn SFD:
For UHR-STF corresponding to distribution bandwidth for DRU,
  STF sequence depends on PPDU BW.
  Occupied STF tones are the same as that of the largest RRU corresponding to the distribution BW within PPDU BW.
Move: Bo Gong Second: Lin Yang
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/749r2. No objection to the SP.

## Slide 25: Motion 20 (PHY)
Move to add the following text to the TGbn SFD:
In a non-punctured 80 MHz PPDU, the following distribution bandwidth modes are allowed for DRU
  80 MHz
  20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz)
Move: Eunsung Park Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Note: Reference document is 11-24/766r2. No objection to the SP.

## Slide 26: Motions on July 18th

## Slide 27: Motion 21 (PHY)
Move to add the following text to the TGbn SFD:
If a DRU for a PPDU occupies more than one 20 MHz channel, then the L-STF, L-LTF, L-SIG, and RL-SIG fields are duplicated over all the 20 MHz channels which are occupied by the DRU.
Move: Yapu Li Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference documents: [24/0736r1]. SP result: 51Y, 2N, 15A.

## Slide 28: Motion 22 (PHY)
Move to add the following text to the TGbn SFD:
“PHY version identifier” is set to 1 in U-SIG for UHR PPDUs
Move: Jianhan Liu Second: Ross J. Yu
Discussion: Some discussion.
Preliminary Result: 169Y (+5), 16N, 64A
Result: Y:167, N:16, A:59 (passes)
Reference documents: [24/0876r0]. SP result: 112Y, 4N, 17A.

## Slide 29: Motion 23 (PHY)
Move to add the following text to the TGbn SFD:
Define unequal modulation over different spatial streams
Move: Rui Cao Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Reference documents: [24/0474r2]. SP result: 116Y, 4N, 9A.

## Slide 30: Motion 24 (PHY)
Move to include the following in the 11bn SFD:
Define Enhanced Long Range (ELR) PPDU and potentially other Range Extension mechanisms.
Move: Wook Bong Lee Second: Shengquan Hu
Discussion: None.
Preliminary Result: 150Y (+27), 11N (+1), 44A
Result: 174Y, 11N, 41A (pass)
Reference documents: [24/0873r2]. SP result: 118Y, 7N, 16A.

## Slide 31: Motion 25 (PHY)
Move to include the following in the 11bn SFD:
Define LDPC codeword length larger than 1944, including 2x1944
Move: Rethna Pulikkoonattu Second: Sameer Vermani
Discussion: None.
Result: Approved with unanimous consent.
Reference documents: [23/1985r5]. SP result: 113Y, 3N, 20A.

## Slide 32: Motion 26 (MAC)
Move to add the following text to the TGbn SFD:
Define in 11bn that when a non-AP MLD is in the process of roaming from the current AP MLD to a target AP MLD, the context related to the non-AP MLD is transferred to the target AP MLD such that it preserves the data exchange context for the non-AP MLD or the context can be renegotiated with the target AP MLD
  Details on what context can be transferred and what context can be renegotiated are TBD
  How to transfer the context is TBD.
Move: Giovanni Chisci Second: Binita Gupta
Discussion: None.
Preliminary Result: 179Y (+18), 6N, 26A
Result: 193Y, 6N, 25 (passes)
Note: Reference documents:[23/1971, 23/1996, 24/0052, 24/0083, 24/0101, 24/0396, 24/0412, 24/0679]. SP result: 153Y, 22N, 37A.

## Slide 33: Motion 27 (MAC)
Move to add the following text to the TGbn SFD:
As part of the seamless roaming procedure, during roaming,
  after the request/response exchange that initiates notification of the DS mapping change from the current AP MLD to the target AP MLD,
    The current AP MLD may deliver buffered DL data frames for a TBD period of time.
    The non-AP MLD may retrieve buffered DL data frames from the current AP MLD
    The non-AP MLD may send UL data to target AP MLD.
    It is assumed that the target AP MLD is able to deliver data frames to non-AP MLD after the DS mapping change
  The current AP MLD may forward DL data to the target AP MLD.
    When and how to initiate the forwarding of DL data is TBD
Move: Po-Kai Huang Second: Jay Yang
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[23/1971, 23/1996, 24/0052, 24/0083, 24/0101, 24/0396, 24/0412, 24/0679 , 23/1884, 24/934]]. SP result: Y:136, N:11, and A:32.

## Slide 34: Motion 28 (MAC)
Move to add the following text to the TGbn SFD:
Define in 11bn that a non-AP MLD can gather information on candidate AP MLD(s) over the DS via the current AP MLD
Move: Guogang Huang Second: Jay Yang
Discussion: Some discussion.
Preliminary Result: 133 (+13)Y, 54 (4)N, 40A
Result: 143Y, 55N, 39A (fails)
Reference documents:[24/0349r3, 24/0679r1, 24/0934]. SP result: 125Y, 34N, 38A.

## Slide 35: Motion 29 (MAC)
Move to add the following text to the TGbn SFD:
• Define a multi-AP Coordinated Spatial Reuse at TxOP-level with power control
• Define multi-AP Coordinated Beamforming
• Other multi-AP coordination modes are TBD
Move: Jason Y. Guo Second: Okan Mutgan
Discussion: None. Recorded Requested (granted if possible).
Preliminary Result: 185 (+14)Y, 17N, 23 (+1)A
Result: 195Y, 17N, 22A (passes)
Reference documents:[22/1822r0, 23/0325r0, 23/0776r1, 23/1023r2, 23/1037r0, 23/1832r0, 23/1917r0, 24/0095r0, 24/0529r0, 24/0577r0, 24/0635r0, 24/0639r0, 24/0640, 24/0839r1, 24/0880r0, 24/1204r0, 24/1211r1,]. SP result: 173Y, 27N, 28A.

## Slide 36: Motion 30 (MAC)
Move to include in the 11bn SFD:
define a mechanism for a non-AP STA to report unavailability at TxOP level and define or reuse/update existing mechanism for a non-AP STA to report long term (periodic) unavailability
Move Abdel K. Ajami: Second: Yong Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference documents: [23/0816, 23/1934, 23/1964, 23/2002, 23/2078, 24/0094, 24/0420, 24/509, 24/0543, 24/0675, 24/0676, 24/0831, 24/0834, 24/0856, 24/1109, 24/1170, 24/1247]. SP result: 164Y, 24N, 33A.

## Slide 37: Motion 31 (MAC)
Move to add to the TGbn SFD the following:
11bn defines a mechanism that enables a non-AP STA to indicate that it does not have pending traffic to deliver during the current ongoing TWT SP.
  NOTE 1 – The exact signaling mechanism is TBD
  NOTE 2 – This does not propose changing the SP termination mechanism/signaling itself. As per current spec, a TWT SP may be terminated by an AP as specified in 26.8.5
  NOTE 3 – It is optional for the non-AP STA to provide such an indication
Move: Kumail Haider Second: George Cherian
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/408r0]. SP result: 147Y, 46N, 67A.

## Slide 38: Motions on September 12th

## Slide 39: Motion 32 (PHY)
Move to add to the TGbn SFD the following:
ELR PPDU starts with a legacy preamble in the PPDU for the ELR transmission
  The legacy preamble contains the L-STF, L-LTF, L-SIG, RL-SIG, and U-SIG
Move: Dongguk Lim Second: Ross J. Yu
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/1184r1]. SP result: No objection.

## Slide 40: Motion 33 (PHY)
Move to add to the TGbn SFD the following:
In the U-SIG field of a UHR ELR PPDU, the PHY Version Identifier is set to 1. And the PPDU Type And Compression Mode is used to indicate ELR PPDU.
Move: Ross J. Yu Second: Dongguk Lim
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/1410r0]. SP result: no objection.

## Slide 41: Motion 34 (PHY)
Move to add to the TGbn SFD the following:
Introduce new MCSs which are applicable to single spatial stream transmissions, as well as to equal modulation and unequal modulation cases in multiple spatial stream transmissions.
Move: Shengquan Hu Second: Stephen McCann
Discussion: Some minor clarification.
Result: Approved with unanimous consent.
Reference documents:[24/1186r1]. SP result: No objection.

## Slide 42: Motion 35 (PHY)
Move to add to the TGbn SFD the following:
Define a mode with additional pilots, located within the data portion of the PPDU, which are used for interference estimation & mitigation
  Note: zero-energy pilots alternative to be considered as well
Move: Shimi Shilo Second: Genadiy Tsodik
Discussion: Some discussion. Recorded vote requested.
Preliminary Result: 148Y, 39N, 81A (passes).
Result: 148Y, 39N, 81A (passes)*
Reference documents:[24/1264r0]. SP result: 60Y, 17N, 34A.
* The result is the same as the preliminary result as the validation data was not saved. In addition, the member that requested the recorded vote relinquished such a request.

## Slide 43: Motion 36 (PHY)
Move to add to the TGbn SFD the following:
ELR-SIG is located right after ELR-LTF in ELR PPDU
  Note that ELR-LTF is the short name of UHR-LTF for ELR PPDU
Move: Lin Yang Second: Rethna Pulikkoonattu
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/1478r2]. SP result: 64Y, 3N, 15A.

## Slide 44: Motion 37 (PHY)
Move to add to the TGbn SFD the following:
UL MU-MIMO is not applicable to DRU
Move: Lin Yang Second: Bin Tian
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/1510r0]. SP result: No objection.

## Slide 45: Motion 38 (PHY)
Move to add to the TGbn SFD the following:
DRU only supports up to 2ss
Move: Lin Yang Second: Bin Tian
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/1510r1]. SP result: No objection.

## Slide 46: Motion 39 (PHY)
Move to add to the TGbn SFD the following:
For 4 SS, the UEQM patterns only include:
  1st ss, 2nd ss, 3rd ss, 4th ss,
  [M, M, M, M-1]
  [M,M,M,M-2]
  [M,M,M-1,M-2]
  [M,M-1,M-1,M-2]
Note: M is the constellation index; M-1 refers to the constellation that is one order lower than M; M-2 refers to the constellation that is two orders lower than M.
Move: Ross J. Yu Second: Rui Cao
Discussion: No discussion but count.
Preliminary Result: 175Y, 8N, 69A
Result: 175Y, 8N, 69A (passes)*
Reference documents:[24/1409r0]. SP result: No objection.
* The result is the same as the preliminary result as the validation data was not saved.

## Slide 47: Motion 40 (PHY)
Move to add to the TGbn SFD the following:
For a (non-ELR) UHR MU PPDU, there exists a 1-bit EQM/UEQM indication in a User field for non-MU-MIMO in the UHR-SIG field.
Move: Ross J. Yu Second: Shengquan Hu
Discussion: Some discussion.
Preliminary Result: 176Y, 37N, 53A (passes)
Result: 159Y, 34N, 50A (passes)
Reference documents:[24/1411r0]. SP result: 88Y, 6N, 12A.

## Slide 48: Motion 41 (PHY)
Move to add to the TGbn SFD the following:
For a (non-ELR) UHR MU PPDU, when EQM/UEQM indicates UEQM in a User field for non-MU-MIMO, there exists a MCS field, a NSS field and a 2 bit field indicating UEQM patterns.
Move: Ross J. Yu Second: Hongyuan Zhang
Discussion: Some discussion.
Preliminary Result: 151Y, 57N, 56A
Result: 137Y, 54N, 52A (fails)
Reference documents:[24/1411r0]. SP result: 64Y, 10N, 12A.

## Slide 49: Motion 42 (PHY)
Move to add to the TGbn SFD the following:
Add the following modulation and code rate combinations as the new MCSs for 11bn:
  Modulations of {QPSK, 16QAM, 256QAM} with code rate R=2/3
  Modulation of 16QAM with code rate R=5/6
Move: Shengquan Hu Second: Jianhan Liu
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/1186r1]. SP result: No objection.

## Slide 50: Motion 43 (PHY)
Move to add to the TGbn SFD the following:
UEQM patterns for Nss=3 are limited to three:
  [M, M, M-1]
  [M, M, M-2]
  [M, M-1, M-2]
Note: M is the constellation index; M-1 refers to the constellation that is one order lower than M; M-2 refers to the constellation that is two orders lower than M.
Move: Alice Chen Second: Sameer Vermani
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/498]. SP result: 77Y, 3N, 14A.

## Slide 51: Motion 44 (MAC)
Move to add to the TGbn SFD the following:
Define a request frame sent by a non-AP MLD in state 4 to initiate the roaming procedure
The roaming procedure performs context transfer to the target AP MLD and perform the necessary changes of the DS mapping from the current AP MLD to the target AP MLD
Define a response frame sent to the non-AP MLD to indicate readiness for the non-AP MLD to send class 3 frames to the target AP MLD
TBD on data transmission from non-AP MLD to current AP MLD during the request/response frame exchange
NOTE – What context is transferred is TBD.
NOTE – TBD on which request/response frame to use
Move: Po-kai Huang Second: Giovanni Chisci
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[23/1884, 23/1971, 23/1996, 24/0052, 24/0083, 24/0101, 24/0396, 24/0412, 24/0679, 24/0830]. SP result: 77Y, 19N, 42A.

## Slide 52: Motion 45 (MAC)
Move to add to the TGbn SFD the following:
An UHR STA that uses the power save mode to transition from lower capability (LC) mode to higher capability (HC) mode, advertises the amount of padding it needs in a received initial control frame
  Padding values range between 0 and a maximum value that is TBD with a TBD resolution .
Move: Sherief Helwa Second: Abhishek Patil
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[23/1873, 23/1875, 24/450, 24/451, 24/503, 24/544, 24/671, 24/1129, 24/1227, 24/1261]. SP result: 130Y, 35N, 26A.

## Slide 53: Motion 46 (MAC)
Move to add to the TGbn SFD the following:
TGbn shall define a Coordinated TDMA (C-TDMA) procedure for an AP to share its time resources of an obtained TXOP with a set of APs.
  Set of APs is TBD.
  The set can consist of one AP.
Move: Abhishek Patil Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[23/0041, 23/249, 23/0261, 23/739, 23/1085, 23/1692, 23/1895, 23/1910, 23/1912, 24/93, 24/227, 24/382, 24/411, 24/423, 24/462, 24/842, 24/843, 24/866, 24/887, 24/941, 24/1016, 24/1017, 24/1225, 24/1250 ]. SP result: No objection.

## Slide 54: Motion 47 (MAC)
Move to add to the TGbn SFD the following:
If an initial control frame includes an intermediate FCS for UHR STA(s) that precedes padding and the FCS field, the intermediate FCS has the size of 32 bits.
Move: SunHee Baek Second: Insun Jang
Discussion: None.
Result: Approved with unanimous consent.
Reference documents: [24/1129, 23/1873, 24/485, 24/497, 24/544, 24/1227, 24/1246, 24/1256]. SP result: No objection.

## Slide 55: Motion 48 (MAC)
Move to add to the TGbn SFD the following:
Define mechanisms that enable APs to coordinate their rTWT schedule(s) and/or to ensure that one AP provides the protection of the rTWT schedule(s) of the other AP.
NOTE – TBD mechanisms including negotiation between 2 APs and advertisement.
Move: Giovanni Chisci Second: Liuming Lu
Discussion: None
Result: Approved with unanimous consent.
Reference documents:[22/1530, 23/0250, 23/860, 23/1871, 23/1887, 23/1916, 23/1932, 23/1952, 23/1962, 23/2212, 23/2022, 23/2084, 24/0160, 24/0161, 24/0388, 24/0407, 24/0678, 24/827]. SP result: 134Y, 19N, 26A.

## Slide 56: Motion 49 (MAC)
Move to add to the TGbn SFD the following:
Define a new mechanism and/or enhance existing mechanism for AP power save
Move: Laurent Cariou Second: Binita Gupta
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[11-23/10, 11-23/2002, 11-23/2040, 11-24/659, 11-24/450, 24/544, 24/671, 24/451]. SP result: 133Y, 8N, 26A.

## Slide 57: Motion 50 (Joint)
Move to add to the TGbn SFD the following:
11bn defines a common framework of a M-AP Coordination for various coordination schemes.
  Note - Coordination schemes such as (but not limited to): Co-SR (TXOP-based with power control), Co-BF, TBD Co-TDMA , TBD C-RTWT, etc.
Move: Arik Klein Second: Genadiy Tsodik
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[22/1530r1, 23/293r0, 23/1871r5, 23/1932r3, 23/2022r1, 24/0072r0, 24/453r0, 24/511r1, 24/512r0, 24/719r0, 24/842r0, 24/1217r2, 24/1220r0]. SP result: 170Y, 30N, 42A.

## Slide 58: Motion 51 (Joint)
Move to add to the TGbn SFD the following:
11bn defines a common framework of a M-AP Coordination that can enable the following procedures:
  M-AP Coordination Discovery procedure
  M-AP Coordination agreement negotiation procedure
Note: Details of the procedures and whether the above procedures are mandatory/optional - TBD
Move: Arik Klein Second: Shimi Shilo
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[22/1530r1, 23/293r0, 23/1871r5, 23/1932r3, 23/2022r1, 24/0072r0, 24/453r0, 24/511r1, 24/512r0, 24/719r0, 24/842r0, 24/1217r2, 24/1220r0]. SP result: 199Y, 8N, 46A.

## Slide 59: Motion 52 (PHY)
Move to add to the TGbn SFD the following:
UEQM patterns for Nss=2 are limited to two as:
  [M, M-1]
  [M, M-2]
Note: M is the constellation index; M-1 refers to the constellation that is one order lower than M; M-2 refers to the constellation that is two orders lower than M.
Move: Rui Cao Second: Wookbong Lee
Discussion: None
Result: Approved with unanimous consent.
Reference documents:[24/474r3]. SP result: No objection.

## Slide 60: Motion 53 (PHY)
Move to add to the TGbn SFD the following:
UHR defines unequal modulation only for LDPC
Move: Rui Cao Second: Hongyuan Zhang
Discussion: None.
Result: Approved with unanimous consent.
Reference documents:[24/474r3]. SP result: No objection.