## Slide 1: Discussion on Distributed RUs (DRUs)
Date: 2024-01-10
Authors:

## Slide 2: Situation
The core idea of DRU is a workaround to 6 GHz regulations that limit the transmit PSD per MHz to a relatively low value
DRU energize one or so subcarriers per 1 MHz instead of energizing 12.8 subcarriers on average
Gains as much as 10*log10(12.8) = 11 dB link budget
Data rate is commensurately downscaled.

## Slide 3: Problem
DRU degrades system throughput with insufficient users.
Compare achieving a 6 dB better link budget by:
  Reducing the RU BW (and data rate) by a factor of 4 (75%). Other BSSs/UL OFDMA users can use the other 75% of the bandwidth for their data, for no net loss of system throughput.
  Reducing the subcarrier density (and data rate) by a factor of 4 (75%). As currently proposed, no other BSSs can use the other 75% of the subcarriers for their data, for a 75% loss of system throughput.
At worst, throughput is degraded by 100% - 100%×1/floor(12.8) = 91.67%.

## Slide 4: Solution
Define Coordinated OFDMA for DRU (C-OFDMA-DRU)
  For both DL and triggered UL
  Recommendation: conditional mandatory. If an AP transmits a PPDU with DRU then the AP shall support C-OFDMA-DRU as a leader AP
Define:
  AP capability signaling between neighboring co-channel APs: C-OFDMA-DRU as a follower AP (and as a leader AP)
  AP frame exchanges for the C-OFDMA-DRU feature
  AP behavior: an AP that uses or triggers DRU in a PPDU and is aware of neighboring co-channel AP(s) that support C-OFDMA-DRU as follower AP(s) shall offer C-OFDMA-DRU to the neighboring AP(s).

## Slide 5: *Sidebar
DRU faces an unclear regulatory situation
  TBD if regulators will allow / disallow DRU; outcome could vary by regulatory body
  If regulators allow DRU, TBD if incumbents use their legal avenues to challenge the decision and, if so, whether incumbents succeed / fail; outcome could vary by regulatory body
Fortunately, the industry has made a considerable investment in AFC, standard power APs, dual clients and (coming) composite APs
  In regulatory domains and spectrum where Standard Power operation is allowed and Standard Power APs are available, there is no range issue nor need for DRU
  // Dual clients operate under the control of both Low Power Indoor APs & Standard Power APs
Takeaway: client vendors are urged to obtain dual certification for 6 GHz
  Following the intent of the spectrum negotiations and the regulatory rules, and
  As risk mitigation in case the outcome of DRU regulatory discussions is unhelpful

## Slide 6: Summary
To mitigate the system inefficiency of DRU, we propose that DRU should support C-OFDMA-DRU for both DL and triggered UL
The use of DRU should be conditional on enabling C-OFDMA-DRU to neighboring APs that can support C-OFDMA-DRU
In the meantime, client vendors are urged to obtain dual certification for 6 GHz since this solution is available today, invariably solves the range problem where-ever SP/Composite APs are available and does not come with regulatory risk.

## Slide 7: Strawpoll 1
Do you support the following: if 11bn defines a mechanism for DRU, then 11bn shall also define a mechanism for C-OFDMA with DRU?
Y / N/ A

## Slide 8: Strawpoll 2
Do you agree to add the following text to the 11bn SFD:
  If 11bn defines a mechanism for C-OFDMA-DRU (TBD), then an AP using DRU shall offer C-OFDMA-DRU as a leader AP to neighboring APs that support C-OFDMA-DRU as follower APs.
Y / N/ A

## Slide 9: References
23/0037r0, UHR Feature to Overcome PSD Limitations Distributed-Tone Resource Units, Jianhan Liu / Mediatek
23/0281r0, Considerations on RU / MRU Designs for UHR, Eunsung Park, LG Electronics
23/1115r0, CFO Impact and Pilot Design for dRU, Eunsung Park / LG Electronics
23/1117r0, CFO dRU Signaling for UHR, Eunsung Park / LG Electronics
23/1447r0 CFO Impact and Pilot Design for dRU Follow up, Eunsung Park, LGE
23/1448r0 Further Considerations on dRU, Eunsung Park, LGE
23/1511r0 Pilot Tone Allocation and Other Considerations of Tone-Distributed RUs for UHR, Mahmoud Kamel / Interdigital
23/1516r0 Use case for distributed RUs in Downlink, Sigurd Schelstraete (MaxLinear)