## Slide 1: Enabling Unscheduled AP PS Follow-up
Date: 2024-02-08
Authors:
Name | Affiliations | Address | Phone | Email
Guogang Huang | Huawei | Shenzhen, China |  | huangguogang1@huawei.com
Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
February 2024
Notes: September 2012

## Slide 2: Introduction
One of the goals of UHR is to reduce the AP power consumption which is more emphasized for the AP MLD.
  Since power consumption increases with the number of affiliated APs.
Some candidate AP PS mechanisms are discussed [1-2]
  Scheduled AP PS
    E.g. use the existing TWT mechanism to handle the periodic traffic
  Dynamic AP PS
    E.g. exchange initial Control frame to enable higher BW/NSS modes
  Unscheduled AP PS
    E.g. the non-AP MLD sends a wakeup request through the link on which the corresponding affiliated AP is operating in active mode to wake up other affiliated APs which are operating in PS mode
In this contribution, we will provide qualitative comparisons among these candidate AP PS mechanisms.
February 2024

## Slide 3: Recap Unscheduled AP PS [2]
In order to save AP MLD power, the simplest way is to have only one link operating in the active mode and other links operating in the PS mode if the traffic load is low.
  All APs affiliated with the AP MLD shall announce the change on the AP power management mode in advance
  No need to send Beacon frame if an AP affiliated with an UHR AP MLD is in PS mode
The ‘active’ link (which means the AP is operating in the active mode) can address the follow potential issues
  Provide access service to the pre-EHT STA
  Provide Discovery, Active Probing, Association to EHT/UHR non-AP MLD
February 2024

## Slide 4: Recap Unscheduled AP PS (Cont.) [2]
Once high throughput is needed, a non-AP MLD can send a request through the ‘active’ link to wake up one or more affiliated APs in the PS mode with the doze state
An affiliated AP in PS mode with the doze state shall enter the awake state after receiving a wakeup request for frame exchange
The affiliated AP in PS mode with the awake state can switch back to the doze state if either of the following conditions is met, e.g.
  There is no STA who operates on this link and sets the More Data subfield of the latest frame transmitted to 1
  The channel is idle for a given time
    This can address the case that the STA moves out of the AP’s coverage area
February 2024

## Slide 5: Qualitative Comparison [1]
AP PS mechanism | Status | Inactive Periods | Active Periods | Inactive/Active Duration | PS benefits | Tx Delay
Link Disablement | Baseline | In Disabled Links | In Enabled Links (At least one link) | ~ Seconds or more (order of DTIM interval) | High | High
Scheduled AP PS | UHR Candidate | Outside Wake SPs | Within Wake SPs | ~ Tens of ms. or more | Medium | Medium
Dynamic AP PS | UHR Candidate | None | All | None/All | Medium | Minimal
Unscheduled AP PS | UHR Candidate | Before received at least one wakeup request | From received at least one wake request to the time when there is no STA who operates on this link and sets the More Data subfield of the latest frame transmitted to 1. |  | High | Minimal < X < Medium
February 2024
Note all these AP PS mechanisms can be used only when all associated STAs and non-AP MLDs support them.

## Slide 6: Unscheduled AP PS
The proposed unscheduled AP PS mechanism can be used in combination with the scheduled AP PS mechanism.
For the sake of simplicity, the AP only can be operating in the dynamic AP PS mode or the unscheduled AP PS mode.
An AP affiliated with an AP MLD can announce its power management mode change through the Reconfiguration Multi-link element of the Beacon frame.
  E.g. a 2-bit AP Power Management subfield
AP Power Management subfield value | AP Power Management Mode
0 | Active mode
1 | Dynamic AP PS mode
2 | Unscheduled AP PS mode
3 | Reserved
February 2024

## Slide 7: Conclusions
We have provided qualitative comparison among different AP PS mechanisms, i.e. link disablement, scheduled AP PS, dynamic AP PS and unscheduled AP PS
  The proposed wakeup-based unscheduled AP PS mechanism can maximize power save while minimizing the transmission delay of the traffic.
February 2024

## Slide 8: References
[1] 11-23-2040-00-00bn-enabling-ap-power-save-follow-up.pptx
[2] 11-23-0225-00-0uhr-considering-unscheduled-ap-power-save.pptx
February 2024

## Slide 9: SP 1
Do you support to define a mechanism that allows an AP affiliated with an AP MLD to be in the PS mode?
  Yes:
  No:
  Abstain:
February 2024

## Slide 10: SP 2
Do you support to define a mechanism that allows the non-AP MLD to send a wakeup request through an enabled link on which the affiliated AP is operating in awake state to wake up another AP which is affiliated with the same AP MLD and operating in the doze state of the PS mode?
  Yes:
  No:
  Abstain:
February 2024