## Slide 1: Support for End-to-End QoS
Date: 2024-02-26
Authors:

## Slide 2: Introduction
UHR PAR is aiming to provide improved low latency support.
Many applications such as video collaboration, XR, immersive education/training, real-time gaming, robotics etc. require support for low end-to-end latency and jitter.
In [1] we covered that enterprise network goal is to deliver all traffic in a timely manner when enough bandwidth is available and prioritize business-critical flows to meet E2E SLA in case of network congestion.
To meet E2E SLA for applications, enterprise networks prioritize applications not only on the Wi-Fi access (AP/WLC) but also on other parts of the network (e.g. SD-WAN).
In this presentation we propose some key SCS enhancements needed to meet E2E SLA for such applications in enterprise deployments.

## Slide 3: Problem statement 1
To meet E2E SLA for business critical flows, enterprise networks apply flow specific QoS policies across the network (including AP/WLC and SD-WAN) to prioritize these flows.
TCLAS (IP tuple) information is needed to classify flows and apply flow level policy for E2E QoS boosting for SCS flows
  However, 802.11be spec does not provide TCLAS for UL SCS request with QoS Characteristics.
  There can be multiple UL flows active from a given STA for a given TID – e.g. video collaboration while a live sports stream running in the background, both flows mapped to TID 5.
  Without UL TCLAS, the UL QoS Characteristics is not associated with an UL IP flow  network cannot create any per flow policy to prioritize UL flows UL flows are treated as best effort in rest of the network  E2E SLA not met.
  Note that TCLAS is provided for DL SCS flows, and such flows can be prioritized in rest of the network for meeting E2E SLA. Leads to undesirable asymmetric E2E QoS treatment for an app (DL is prioritized E2E, but UL is not).

## Slide 4: Proposal 1: UL TCLAS in SCS Request
UL TCLAS needs to be provided for SCS Request with UL QoS Characteristics [2], then:
  AP can apply and/or create flow specific policy for UL SCS flow for E2E SLA, e.g. create a flow policy to mark an XR flow IP tuple with DSCP 46 for prioritization in the network.
  UL TCLAS allows an AP to apply flow level policy for SCS requests and allocate UL resources, e.g. trigger frequently with enough RU allocation for meeting QoS for business-critical flows.
Similar to DL, the UL TCLAS should also be provided always in the SCS request, to enable symmetric E2E QoS prioritization both for DL and UL.
  If UL TCLAS is not provided, an AP MLD can signal to non-AP MLD (e.g. using a status code) that the UL TCLAS is needed.

## Slide 5: Problem statement 2
In many cases, apps running on clients may not provide QoS KPIs to the Wi-Fi layer for business-critical flows  an SCS request with QoS Char is not sent to the AP for UL and/or DL. This could be because:
  client-side app does not implement QoS KPIs, or
  the OS platform does not provide APIs to applications for specifying QoS KPIs
In both these cases, business-critical app traffic is sent as Best Effort (AC_BE) over Wi-Fi access, leading to not meeting E2E SLA
For business-critical flows enterprise networks have the knowledge of E2E SLA/QoS KPIs (either configured or determined based on *DPI/NBAR), and have policies to prioritize these flows
*DPI: Deep Packet Inspection, NBAR: Network Based Application recognition

## Slide 6: Proposal 2: AP Initiated SCS for UL
AP should be able to install UL QoS for business-critical flows on the STA to prioritize UL traffic. For example, AP can signal UL delay bound and min data rate using QoS Characteristics.
  Option 1: AP MLD can send an AP initiated SCS Request to the non-AP MLD to provide UL QoS (per UL TCLAS), which should be installed and applied in the UL.
  Option 2: AP MLD can send an unsolicited SCS Response to the non-AP MLD to provide UL QoS (per UL TCLAS) with a new Accept SCS status code (similar to unsolicited TWT Response sent with Accept TWT). STA applies the received QoS in the UL, and (if needed) can use SCS Change/Remove for the SCS stream.
  AP MLD also applies DL QoS for business-critical flow. AP can send unsolicited SCS Response to the STA to signal DL QoS applied. STA may choose to make changes to the DL QoS applied.
  If STA is already requesting UL QoS for a flow/TCLAS, then AP would not initiate SCS for that flow. It can suggest any alternate QoS characteristics in the SCS Response.

## Slide 7: Problem Statemen 3
In enterprise networks, the QoS policy is not decided solely by the AP (it is an E2E network wide policy) and is specified based on apps/flows to meet E2E QoS/SLA for the applications.
The per flow policy verification can involve in some cases on-demand flow packets analysis including DPI/NBAR which may reside on nodes other than the AP
This means policy verification at the AP for an SCS flow may not be completed in the Wi-Fi transaction timeframe, and may need longer for DPI (e.g. DPI may take 100s of msec)
Also, if the SCS request is sent before the flow even starts, the on-demand policy verification would take much longer, because network needs to wait for the flow to start
In such scenarios AP can’t provide an accept/reject response to the SCS request right away
This may lead to STA unnecessarily retrying the SCS request, or worse incorrectly assuming that request can’t be met and change its QoS, impacting E2E QoS/SLA for business-critical flows

## Slide 8: Proposal 3: Signal Continuation of SCS Processing
While on-demand policy verification is being done for a flow, AP can send an intermediate SCS Response to STA signaling continuation of SCS request processing.
  E.g. indicated by a new “SCS Processing” status code
  Such SCS Response can also indicate (provisional) allocation of QoS resources to the SCS flow for a specified period (e.g. time taken for DPI, when possible) via an optional subelement.
Once AP has completed the flow classification and policy verification, the final SCS Response is sent indicating accept/reject for resources requested in the SCS request.

## Slide 9: Conclusion
In this presentation, we presented some key SCS enhancements which are needed to facilitate meeting E2E QoS/SLA for business-critical applications in enterprise networks
Proposed SCS enhancements include:
  Support for UL TCLAS in SCS Request, to apply flow specific prioritization for E2E QoS/SLA
  AP initiated SCS for UL (and DL), to prioritize UL traffic for E2E QoS/SLA
  Signal continuation of SCS processing, to enable DPI/NBAR for flow identification and flow specific policy verification for E2E QoS/SLA

## Slide 10: SP1
Do you agree that in 11bn an SCS Request frame that includes a QoS Characteristics element for uplink direction should support including UL TCLAS information?

## Slide 11: SP2
Do you agree that in 11bn an AP should be able to initiate SCS signaling to send an UL QoS Characteristics element for an UL flow (specified by an UL TCLAS), to a STA to prioritize the UL flow on the STA?
Do you agree that in 11bn an AP should be able to initiate SCS signaling to send a DL QoS Characteristics element for a DL flow (specified by a DL TCLAS), to a STA to notify the STA of the QoS provided by the AP for the DL flow?

## Slide 12: SP3
Do you agree that in 11bn an AP should be able to send an intermediate SCS Response frame for an SCS Request to a STA signaling continuation of the SCS Request processing, and later send an SCS Response signaling accept or reject for the SCS Request?

## Slide 13: References
[1] 11-23-2029, “Overview of Enterprise Policy and Goals”
[2] 11-23-1540-05-00be-lb275-cr-for-scs-tclas-counter-proposal