## Slide 1: Support for End-to-End QoS
Date: 2024-02-26
Authors:

## Slide 2: Introduction
UHR PAR is aiming to provide improved low latency support.
Many applications such as video collaboration, XR, immersive education/training, real-time gaming, robotics etc. require support for low end-to-end latency and jitter.
[1] Highlighted that the goal of an enterprise network is to deliver all traffic in a timely manner when enough bandwidth is available and prioritize business-critical flows to meet E2E SLA/QoS in case of network congestion.
To meet E2E SLA for applications, enterprise networks prioritize applications both on the Wi-Fi access (AP/WLC) and other parts of the network (e.g. SD-WAN).
In this presentation we propose some key SCS enhancements needed to meet E2E SLA for business-critical applications in enterprise deployments.

## Slide 3: Problem statement 1
To meet E2E SLA for business critical flows, enterprise networks apply flow specific QoS policies across the network (including AP/WLC and SD-WAN) to prioritize these flows.
TCLAS info is needed to classify flows and apply flow level policy (based on IP tuple) at network nodes (e.g. switches) for E2E QoS boosting for SCS flows
  However, 802.11be does not provide TCLAS for UL SCS request with QoS Characteristics.
  There can be multiple UL flows active from a given STA for a given TID – e.g. video collaboration while a live sports stream running in the background, both flows mapped to TID 5.
  Without UL TCLAS, the UL QoS Char. is not associated with an UL IP flow  network cannot apply per flow policy to prioritize UL flows UL flows are treated as best effort in rest of the network  E2E SLA not met.
  Note: TCLAS is provided for DL SCS flows  such flows can be prioritized in rest of the network for E2E SLA. This leads to undesirable asymmetric E2E QoS treatment for an app (DL is prioritized E2E, but UL is not).

## Slide 4: Proposal 1: UL TCLAS in SCS Request
UL TCLAS needs to be provided for SCS Request with UL QoS Characteristics [2], then:
  AP can apply and/or create flow specific policy for UL SCS flow for meeting E2E SLA, e.g. prioritize IP flow carrying XR UL pose data (to an Edge Compute) at intermediate nodes.
  UL TCLAS allows an AP to apply flow level policy for SCS requests and allocate UL resources, e.g. trigger frequently with enough RU allocation for meeting QoS for business-critical flows.
Similar to DL, the UL TCLAS should be provided always in the SCS request, to enable symmetric E2E QoS prioritization both for DL and UL.
  If UL TCLAS is not provided, an AP MLD can signal to non-AP MLD (e.g. using a status code) that the UL TCLAS is needed.

## Slide 5: Problem statement 2
In many cases, apps running on client devices (e.g. laptops, phones, IoT devices) may not provide QoS KPIs to the Wi-Fi layer for business-critical flows because:
  client-side apps do not implement QoS KPIs, or
  the OS platform does not provide APIs to applications for specifying QoS KPIs
In these cases, SCS request with QoS Char is not sent to the AP  business-critical app traffic is sent as best effort over Wi-Fi access, leading to not meeting E2E SLA
In some cases, even when a client sends an SCS request with QoS Char for a flow (DL/UL), it may not align with the network QoS policy for that flow for that specific deployment
  E.g. STA requesting TID 4 for a robotics app in IIoT, and in network policy it is configured as TID 6.
For business-critical flows enterprise networks have E2E SLA/QoS KPIs defined and apply QoS policies E2E to prioritize these flows
  In many cases network performs *DPI/NBAR for flow classification and mapping to desired QoS policy
*DPI: Deep Packet Inspection, NBAR: Network Based Application recognition

## Slide 6: Proposal 2a: AP Initiated SCS for UL
AP can provide UL QoS policy for business-critical flows to STA using AP initiated SCS with QoS Char, to enable STA to prioritize UL flows. E.g. AP can signal delay bound and desired TID for an UL TCLAS.
  Option 1: AP can send an AP initiated SCS Request to STA to provide UL QoS Char (per UL TCLAS), which should be applied in the UL.
  Option 2: AP can send an unsolicited SCS Response to STA to provide UL QoS Char (per UL TCLAS) with a new Accept SCS status. STA applies received QoS in UL, and (if needed) can use SCS Change for the SCS stream.
    Similar to unsolicited TWT Response sent with Accept TWT
  AP also applies DL QoS for business-critical flows. AP can send unsolicited SCS Response to STA to signal DL QoS applied. STA may choose to make changes to DL QoS applied.
  If STA is already requesting UL QoS for a flow/TCLAS, then AP would not initiate SCS for that flow. It can suggest any alternate QoS characteristics in SCS Response.

## Slide 7: Proposal 2b: AP Suggested TID for SCS flows
  Network QoS policy for a business-critical flow may assign a different TID (higher/lower) than the TID requested by the STA in SCS Request (for DL or UL flows)
  In such cases, it is important that an AP is able to recommend a different TID per QoS policy, to meet E2E SLA. Else, flow may be prioritized over rest of the network but not over Wi-Fi link.
802.11be allows AP to suggest revised QoS Char parameters in the SCS Response but does not allow suggesting a different TID.
SCS protocol should allow AP to suggest a different TID in QoS Char. in SCS Response as per the network policy, to meet E2E SLA
  E.g. gaming applications could be classified as business-critical in a university dorm, and AP can have a policy to use TID 5 for these apps (instead of TID 0), and would suggest that in SCS Response

## Slide 8: Problem Statemen 3
In enterprise networks, the QoS policy is not decided solely by the AP, it is an E2E network wide policy, and is specified based on apps/flows to meet E2E QoS/SLA
The per flow/app policy verification can involve in many cases on-demand flow packets analysis using DPI/NBAR which may reside on nodes other than the AP (e.g. WLC)
Policy verification at AP/WLC for an SCS flow may not be completed in the Wi-Fi transaction timeframe, and may need longer for DPI (e.g. DPI may take few 100ms)
Also, if SCS request is sent before the flow even starts, the on-demand policy verification would take much longer, because network needs to wait for the flow to start
In such scenarios AP can’t provide an accept/reject response for the SCS request right away
  This may lead to STA unnecessarily timing out and retrying SCS request, or worse AP rejecting the request because flow policy could not be verified  leading to resources not allocated for the flow  not meeting E2E SLA

## Slide 9: Proposal 3: Signal a Continuation of SCS Processing
While on-demand policy verification (DPI) is being done for a flow, AP can send an intermediate SCS Response to STA signaling continuation of SCS request processing.
  E.g. indicated by a new “SCS Processing” status code
  Such SCS Response can also indicate (provisional) allocation of QoS resources to the SCS flow for a specified period (e.g. time taken for DPI)  can ensure that initial app experience is not impacted
Once AP has completed the flow classification and policy verification, the final SCS Response is sent indicating accept/reject for resources requested in the SCS request.

## Slide 10: Proposal 4: Application Identification in SCS
Problem statement:
Enterprise network QoS policies are defined based on specific business-critical applications for a given deployment, e.g.
  autonomous robotic application in a manufacturing plant, video collab or virtual desktop apps in a carpeted office
802.11be SCS request specifies TCLAS (IP tuple) information for DL flows for flow classification, which is used for prioritization of these specific IP flows
However, IP tuple info for an application is dynamic and can change. Network QoS policies are defined based on more static identification for an application, such as a FQDN/URI or an Application ID (OS specific)
It is desired that an SCS request includes such application identification, for AP to be able to apply network policy at SCS request and prioritize business-critical flows for E2E SLA
Proposal:
Enhance SCS request to provide flow/app identification using FQDN/URI or Application ID (OS specific) when requesting resources for DL and UL
  SCS Descriptor can include a subelement to provide FQDN/URI or Application ID for the application flow

## Slide 11: Conclusion
This presentation proposed some key SCS enhancements which are needed to facilitate meeting E2E QoS/SLA for business-critical applications in enterprise networks
Proposed SCS enhancements include:
  Support for UL TCLAS in SCS Request, to apply flow level prioritization in the network
  AP initiated SCS for UL, to prioritize UL flows based on network QoS policy
  AP suggested TID for SCS flows, to allow mapping flows to TIDs per network QoS policy in DL & UL
  Signal continuation of SCS processing, to enable DPI/NBAR for flow identification and applying flow specific policy
  Application identification in SCS, to enable applying application specific policy at the AP

## Slide 12: References
[1] 11-23-2029, “Overview of Enterprise Policy and Goals”
[2] 11-23-1540-05-00be-lb275-cr-for-scs-tclas-counter-proposal