## Slide 1: Managed Networks under highly congested scenarios - Follow up
Date: 05-13-2024

## Slide 2: Goals
Follow up on the previously presented contribution about managed networks under highly congested scenarios
Discuss technical approaches for implementing mechanisms that enable an AP centric architecture under OBSS/ESS scenarios

## Slide 3: Introduction
802.11bn targets the improvement of packet delivery by reducing the transmission latency and enhancing network reliability [1]
Applications and use cases with QoS-related requirements (e.g., bounded latency and reliability) have been growing in recent times [2]
  The critical QoS services can be mainly characterized by periodic traffic patterns, and strict timing requirements for data exchange [2, 3]
  Relying on maximizing throughput is not tenable in the long term as a sole requirement for correct QoS service operation, especially under heavily congested scenarios
Several contributions presented different approaches based on the AP centric architecture or managed networks [4, 5]

## Slide 4: General Assumptions
We distinguish two types of legacy non-AP STA devices
  Legacy STA with only EDCA mechanism (pre-11ax)
    Assume these devices don’t have strict QoS requirements
    Active at 2.4GHz (IoT device) and 5GHz bands
  Legacy STA supporting Trigger-based access (post-11ax)
    Active at 5GHz (coexistence with EDCA devices) and 6GHz bands
    Assume these devices may have QoS requirements
    Strict QoS requirements are announced by sending SCS requests
AP manages at 5GHz and 6GHz bands

## Slide 5: AP QoS TXOP (1/4)
AP schedules periodic DL/UL/P2P traffic with specific QoS needs, where each service may have different requirements
These data transactions are executed within a QoS TXOP, which is limited to those services granted via an SCS request
  Non-QoS services may be scheduled in separate TXOPs
The AP needs to execute the QoS TXOP on time to meet the traffic requirements, and under congested scenarios, it becomes a real problem
  The AP needs prioritized access to the channel compared to other devices
A time structure for TXOP execution may help the AP, including the coordination with other QoS APs (OBSS or ESS scenarios)

## Slide 6: AP QoS TXOP (2/4)
The prioritized AP channel access may have different implementation options
  Leverage restricted TWT feature, creating an SP that mandates the BSS STAs to end their transmissions before the SP starts, letting the AP to get the channel
    Restricted TWT may not be implemented by all the STAs, and limited to the BSS context
  Setting EDCA parameters (MU EDCA) for non-AP STAs
    STAs might ignore the setting requests
  Highly prioritized access category for QoS TXOP.
    E.g., once the channel is idle, wait for PIFS time without back (as HCCA)
    Several additional proposals for enhancing the channel access method and reducing the collision probability [6,7,8]
    This operation needs to be limited over time, just to cover the QoS requirements and maintain the airtime fairness for other EDCA and legacy devices
Option c) seems to be the most effective way to provide QoS guarantees

## Slide 7: AP QoS TXOP (3/4)
The QoS TXOP is composed of regular MU or SU transactions, exclusively related to QoS traffic, under admission control (SCS)
QoS
Data
AP
STA1
QoS TXOP
Time
STA2
STA3
Ack
CTS to Self
Ack
QoS
Data
MU
TF
QoS
Data
Ack
QoS
Data
Ack
PIFS or other mechanism
QoS
Data
QoS
Data

## Slide 8: AP QoS TXOP (4/4)
QoS TXOP_1
QoS TXOP_2
Basic Period
QoS TXOP_1
QoS TXOP_3
Basic Period
QoS TXOP_1
Time
Basic Period 1
Basic Period 2
Basic Period 3
Basic Period 1
Basic Period 2
Basic Period 3
Basic Period 1
…
Time
Super Period
Super Period
Data services may have heterogeneous latency/throughput requirements, therefore it is not possible to cover all needs in just one QoS TXOP repeated periodically
  The AP needs to place different QoS TXOPs with a pre-calculated repetition pattern
A time structure for QoS TXOP execution may help the AP, creating a Super Period for covering the lower periodicity events, and composed of N Basic Periods that are populated of several QoS TXOPs
The AP scheduler accommodates traffic flows into different QoS TXOPs
Coordination with other QoS APs (OBSS or ESS scenarios) may leverage this time structure

## Slide 9: Legacy STAs
Gaps between QoS TXOPs allow legacy EDCA devices to access the channel
QoS TXOP_1
QoS TXOP_2
Basic Period
QoS TXOP_1
QoS TXOP_3
Basic Period
QoS TXOP_1
Time
QoS
Data
STA1
QoS TXOP
Time
STA2
STA3
Ack
CTS to Self
Ack
QoS
Data
TF
QoS
Data
Ack
Non-QoS
Data
Ack
Non-QoS exchanges
QoS
Data
QoS
Data
Non-QoS
QoS
PIFS or other mechanism

## Slide 10: OBSS Environment
Under an OBSS scenario, all the network devices are contending for the channel, while the previously shown mechanisms are valid within the BSS, a solution must be presented for this OBSS environment
The overlapped networks need a coordination mechanism so each network can guarantee its own QoS requirements, under the capacity limitations of the wireless channel
  Coordination mechanisms between APs are already being proposed, such as Coordinated TDMA or Coordinated rTWT
We can consider two possible scenarios:
  The interferer OBSS is a UHR QoS AP
  The interferer OBSS is a legacy AP or UHR non-QoS AP

## Slide 11: OBSS Environment
The interferer OBSS is a UHR QoS AP (within ED and PD range)
May occur two QoS TXOPs collide as there is no coordination between the UHR QoS APs
  Having the same high-priority channel access, the probability of collision increases
Ensuring TSF synchronization between the two APs, two possible mechanisms could avoid the collision problem
  1.a) Synchronizing the beginning of the Basic Periods, agreeing on the execution of the QoS TXOPs of each AP, not overlapping each other
  1.b) Agreeing on the Basic Period length and establishing a sharing AP that leads the QoS TXOPs in both APs by means of a Multi-AP C-TDMA mechanism
The synchronization can be done by synchronizing the TSF counters of each AP, or calculating the time offset of both free-running TSF counters

## Slide 12: OBSS Environment
1.a) Synchronizing the beginning of the Basic Periods
BSS1 QoS TXOP_1
BSS1 QoS TXOP_2
Basic Period
Basic Period
Time
BSS2 QoS TXOP_1
BSS2 QoS TXOP_2
Time
BSS1 QoS TXOP_1
BSS1 QoS TXOP_3
BSS2 QoS TXOP_1
BSS2 QoS TXOP_3
BSS1 QoS TXOP_1
Reference for the start of the super period
T1
T2
T3
T3
T1
T2
The UHR QoS APs agree on the time offsets (T1, T2, T3, etc) to execute the scheduled QoS TXOPs within each Basic Period
  The time offsets are referenced to the initial point of the basic period, which will be used to time synchronize the APs, and avoid the collisions
The agreement between the APs can be done by exchanging the QoS TXOP information through specific control/management frames
Restricted TWT could leverage the time synchronization provided by the APs
The gaps between the QoS TXOPs follow the EDCA rules

## Slide 13: OBSS Environment
1.b) Coordinated TDMA over the Basic Periods
BSS1 QoS TXOP_1
Basic Period
Basic Period
Time
BSS2 QoS TXOP_1
Time
Sharing AP
Shared AP
TXS RTS TF
CTS
Shared QoS TXOP
BSS1 QoS TXOP_2
BSS2 QoS TXOP_2
TXS RTS TF
CTS
Shared QoS TXOP
The UHR QoS APs agree on the Basic Period length and the QoS TXOPs executed along these periods
The sharing AP starts the Basic Period executing its own QoS TXOP and after finishing, shares the remaining TXOP time (i.e., C-TDMA) to the shared AP for executing its QoS TXOP
The agreement between the APs can be done by exchanging the QoS TXOP information through a Multi-AP framework
The gaps between the Basic Periods follow the EDCA rules
CF-End
CF-End

## Slide 14: OBSS Environment
The interferer OBSS is a legacy AP or UHR non-QoS AP
In this case the UHR QoS AP will have a significant advantage in contending for the channel concerning the legacy AP and UHR non-QoS AP
  Fairness must be considered, limiting the TXOP length acquired by the UHR QoS AP
Mechanisms such as C-TDMA would allow the UHR QoS AP to share the TXOP with the UHR non-QoS AP
  Legacy APs on the other hand may not have a coordination mechanism available

## Slide 15: Summary
The transmission of QoS data is organized in QoS TXOPs scheduled under a Basic Period repeated within a Super Period, covering different time requirements
Each Basic Period will serve QoS and non-QoS (legacy) data traffic, attending to the airtime fairness rules
Under OBSS or ESS, coordinated QoS TXOP scheduling may be enabled by synchronizing the AP TSF counters or agreeing on coordination based on C-TDMA

## Slide 16: Conclusion
We have presented the basic framework for scheduling high-priority accesses for QoS data exchange under an AP-centric architecture
Focusing first on a non-OBSS scenario, we have defined the mechanisms for scheduling QoS TXOPs, in coexistence with legacy EDCA traffic
Under the OBSS/ESS scenario, we have defined the mechanisms for coordinating the execution of the AP schedulers

## Slide 17: References
[1] IEEE 802.11-23/0028r6, UHR PAR discussion
[2] Inaki Val and et al. (MaxLinear), “High Criticality Use Cases and Requirements”, 23/1522r0
[3] Oliver Holland and et al. “Low Latency Communication White Paper”, P802.24-23-0010r4
[4] Salvatore Talarico and et al. (Sony), “Enhanced HCCA for Controlled UHR Scenarios”, 24/0119r0
[5] Yanchun Li and et al. (Huawei), “Discussion on UHR enhanced channel access”, 23/1973r1
[6] Laurent Cariou and et al. (Intel), “Low latency channel access”, 23/1065r0
[7] Menzo Wentink and et al. (Qualcomm), “Deterministic Backoff”, 23/0031r0
[8] Sigurd Schelstraete and et al. (MaxLinear), “CSMA with enhanced Collision Avoidance”, 24/773r0