## Slide 1: SP Based In-Device Coexistence
Date: 2024-03-04
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
In-Device Coexistence (IDC) has been discussed extensively in TGbn, due to the fact that a Wi-Fi device (e.g., smart phones) often needs to share its radio resource (e.g., RF blocks, antennas, etc.) with other technologies (Bluetooth, etc)
When one of the other technologies is using the radio resource, a Wi-Fi STA in the same device may not be able to transmit or receive, or may only be able to transmit or receive packets of certain parameters (e.g., low MCS, NSS, BW) because of the existence of in-device interference.
The STA should be able to handle the in-device interference in an appropriate way.

## Slide 3: Introduction
Some methods have been proposed in previous contributions [1-4], including:
  Reporting an unavailable period
  Reporting interfered 20MHz channels
  Starting frame exchange using ICF/ICR
  Receiving Parameters update
  TX/RX Parameters restriction
  Indicating available time in a TXOP
  Etc.
Considering that the transmissions of other technologies are often scheduled in a periodic manner, we propose an SP based IDC protocol in this contribution.

## Slide 4: SP based IDC
In the SP based coexistence mode, a series of IDC SPs will be defined, during which:
  The AP shall transmit an ICF to the STA to check its availability/capability
  The STA may transmit an ICR as a response to the ICF, where in the ICR the STA can indicate its availability duration, and maximum capability during the SP, including MAX MCS, NSS, BW, Trigger support, etc.
  If there’s no ICR received, the AP shall not transmit data to the STA during the IDC SP.
The reason for using the ICF/ICR exchange is that other technologies may or may not be using the radio resource during the IDC SPs
  When the other technology is using the radio
    If there’s strong in-device interference, then the ICF will not be received, and no ICR will be sent
    If the in-device interference is not so strong, then the ICF might be decoded successfully, and ICR can indicate receiving capabilities during the IDC SP
  When the other technology is not using the radio, then ICR can indicate: no restriction
  When the other technology is going to use the radio in the later portion of the IDC SP, then ICR can indicate the availability time during the IDC SP
Another option is that no frame exchange is allowed in the IDC SP

## Slide 5: SP based IDC
STA can exchange request/response frames with the AP to setup the SP based coexistence mode
  A TWT element (or other similar element) can be included in the request frame to indicate the IDC SPs
  Corresponding behaviors during the IDC SPs can also be specified during the setup procedure, including: ICF/ICR required, no frame exchange allowed
Multiple TWT elements can be included in the setup request frame, each of which corresponds to a service of other technologies.
……
ICF
ICR
Data
BA
IDC SP
IDC SP
IDC SP
ICF
ICR not received
No data transmission allowed

## Slide 6: Conclusion
We propose an SP based In-Device-Coexistence mode in this contribution
Several IDC SPs are reserved for other technologies, Wi-Fi STAs can use the IDC SPs cautiously (e.g., by exchanging ICF/ICR), clients have the final decision on whether an IDC SP can be used or not

## Slide 7: References
[1] 11-23/1934, In-device interference mitigation follow up, Liwen Chu
[2] 11-23/1964, Coexistence Protocols for UHR, Alfred Asterjadhi
[3] 11-23/2002, In-device coexistence and interference follow - up, Laurent Cariou
[4] 11-23/2026, Balanced Wireless In - Device, Brian Hart