## Slide 1: UEQM Benefit Analysis
Date: 4-Mar-24
Authors:

## Slide 2: Abstract
Previous submissions:
    [1] discusses the channel characteristics of MIMO WLAN channels, reviews 11n unequal modulation and shows ~2dB gain for UEQM on the 2x2 D NLOS channel over EQM with power scaling (enforcing 2 streams)
    [2] discusses unequal MCS vs. UEQM and shows UEQM gain of ~2dB on the 2x2 D NLOS channel (enforcing 2 streams)
    [3] presents performance gains on the 2x2, 4x2 and 4x4 D NLOS and B LOS channel, showing 1-5dB gain (enforcing 2 or 4 streams, respectively)
    [4] compares UEQM with all possible modulation/code rate combinations with UEQM limited to existing combinations and analyses the 4x2 D NLOS case
In this submission:
    Understanding the underlying benefit of UEQM
    Understanding performance of UEQM without BF
    Possible enhancements to Link Adaptation

## Slide 3: Effect of UEQM on BER
The ultimate goal is improving BER (or PER, …) at the decoder output
Without BF:
  Streams have similar SNR
  UEQM could lower bit errors at decoder input for one of the streams
    How much of an effect?
With BF:
  Streams have different SNR
  Modulation could be “matched” to SNR
  No need to equalize BERs of different streams at decoder input for optimal performance

## Slide 4: Analysis setup
Studying UEQM on “controlled” channels
Initial simulations on Identity channel
  With tunable difference in SNR between the streams
  Allows for controlled behavior of the channel to understand UEQM
Behavior is then verified on actual (model B) channels with similar SNR difference between streams

## Slide 5: (1) UEQM without BF
MCS 4 (16 QAM, Rate ¾), MCS 2 (QPSK, Rate ¾) vs. unequal modulation (16 QAM + QPSK, Rate ¾) tested
  Effective rates are 6 bit/carrier, 3 bit/carrier and 4.5bit/carrier respectively
No BF  No SNR difference between spatial streams
UEQM shows only a small BER improvement
  at the cost of 25% lower rate
BER improvement, but no benefit in throughput

## Slide 6: (2) UEQM for varying SNR difference
SNR difference of 6 and 12 dB between streams
  Use BF for transmission
With increasing SNR difference, BER of UEQM improves relative to EQM
  At 12 dB difference 16 QAM + QPSK outperforms QPSK + QPSK !

## Slide 7: (2) UEQM for varying SNR difference – cont.
Required SNR for the various modulations as funtion of SNR difference
  At 12 dB difference 16 QAM + QPSK outperforms QPSK + QPSK
Detailed analysis on next slides

## Slide 8: BER Analysis AWGN Channel 6dB and 12dB SNR difference
Combined BER is dominated by the spatial stream with higher BER
With a large SNR difference (e.g. 12dB), increasing the constellation size (QPSK  16 QAM) on the good spatial stream improves the overall BER
  more error-free bits on the good stream
  same errors on the bad stream
Conclusion: SNR difference between streams is an important driver for MCS selection, but decoder effects need to be considered as well
  Implications for rate adaptation

## Slide 9: WLAN Channel Example without BF
Simulation Results
  Without beamforming, the SNR difference between spatial steams is small
  The same behavior as for the AWGN channel is observed:
    BER can be lowered on one of the streams, but at significant performance penalty
    The required SNR is lowered by less then 1 dB from mcs 4 (6 bit/s/Hz) to mcs 4/2 (4.5 bit/s/Hz)
    There is no performance (throughput) advantage advantage unequal modulation

## Slide 10: WLAN Channel Example: B LOS 2x2
Simulation Results
  For 2x2 B LOS channel with beamforming, the SNR difference between spatial streams is around 12dB
  The same behavior as for the AWGN channel is observed: Unequal modulation MCS 4/2 achieves a higher rate at a lower SNR than 2SS MCS2

## Slide 11: Implications for Link Adaptation
The previous results allow us to identify possible enhancements in Link Adaptation
  Better exploit the understanding of UEQM performance
  See next three slides for proposal and comparison with existing feedback mechanisms

## Slide 12: Link Adaptation Option I – Using existing feedback
Available: PER from acknowledgements
Test all relevant constellation size/code rate settings for equal and unequal modulation
Advantage:
  No additional measurements or evaluation required
Disadvantages:
  Slow, because many options must be tested

## Slide 13: Link Adaptation Option II – Using existing feedback
Available: SNR per spatial stream from sounding, PER from acknowledgements
Use SNR difference from sounding for initial MCS pick and adjust based on PER
Advantage:
  Minimal difference to existing link adaptation
Disadvantages:
  Optimal setting is not necessarily tested
  SNR difference from sounding may not be accurate

## Slide 14: Link Adaptation Option III – Additional feedback
Available: PER from acknowledgements, SNR per spatial stream from sounding, SNR margin per spatial stream (each data packet, not available from sounding)
Pick MCS based on sounding SNR and SNR gap per spatial stream
Update SNR gap, based on PER and SNR margin feedback
Advantages:
  Fast adaptation
  Accurate decision, because of per-spatial stream feedback
Disadvantages:
  New feedback from the receiver required

## Slide 15: Link Adaptation Comparison
Unequal modulation with the modulation difference derived from sounding (Option II) achieves higher rates than equal modulation, but results in steps in the rate-reach curve (like equal modulation).
With SNR margin feedback (Option III), higher rates and a more smooth rate-vs.-reach curve is achieved. The performance is equal to a full search, but less time consuming.

## Slide 16: Conclusions
We investigated how UEQM contributes to improve BER in various situations
SNR difference between streams provides guidance on choice of UEQM, but feedback can be refined
Rate adaptation may benefit form (near-) instantaneous feedback of SNR margin

## Slide 17: References
[1] UHR MIMO RvR enhancement with unequal modulation, 24/0016
[2] Unequal Modulation in MIMO TxBF in 11bn, 24/0113
[3] Improved Tx Beamforming with UEQM, 24/0117
[4] Unequal Modulation over Spatial Streams, 24/0176