## Slide 1: Considerations on Joint Transmission
Date: 2024-03-24
Authors:

## Slide 2: Abstract
This presentation intends to discuss considerations on Joint Transmission (JT), especially focused on the way to deliver user data between APs.

## Slide 3: Introduction
Joint Transmission (JT) is a way to increase the user throughput by cooperating multiple APs ([1]-[7]).
It needs to deliver user data for JT from a Primary AP (P-AP) initiating JT to one or more Secondary APs (S-APs). This data delivery can be made in-band or through backhaul ([8]-[11]).
This presentation discusses some considerations on data delivery.

## Slide 4: Joint Transmission
Multi-AP joint transmission (JT) is a way to increase the user throughput, especially in the situation of less-scattering (LOS) environment, by transmitting different user data to an STA from multiple APs simultaneously.
AP1
(P-AP)
AP2
(S-AP)
STA
DATA 1
DATA 2
DATA 2
Simultaneous transmission
from multiple APs

## Slide 5: Ways to deliver user data
There are two ways to deliver user data from the P-AP to one or more S-APs.
  By in-band transmission
  By out-band transmission through backhaul
AP1
(P-AP)
AP2
(S-AP)
STA
DATA 1
DATA 2
DATA 2
Simultaneous transmission
from multiple APs
Through in-band or backhaul.

## Slide 6: In-band data delivery
It is easy to protect TXOP.
If the link speed between the P-AP and S-AP(s) is low, it may consume a time in delivering the user data from the P-AP to the S-AP(s)
AP1
(P-AP)
AP2
(S-AP)
STA
Time
Time
Time
Negotiation for JT
BlockAck for JT
DATA 2
DATA 1
DATA 2

## Slide 7: Data delivery through backhaul
The link speed of backhaul is higher than of the in-band one.
If the user data from the P-AP to the S-AP(s) delivered via backhaul, it can reduce the delivering time , and it can further increase the throughput.
AP1
(P-AP)
AP2
(S-AP)
STA
Time
Time
Time
Negotiation for JT
BlockAck for JT
DATA 2
DATA 1
DATA 2
Via backhaul
In-band
In-band

## Slide 8: Data delivery through backhaul (cont.)
Several issues may need to be considered as follows:
  The P-AP will need to send a frame to the S-AP(s) to inform the time to transmit DATA frame to the STA.
  It may also need a way to protect TXOP during for delivering the user data from the P-AP to the S-AP(s).
AP1
(P-AP)
AP2
(S-AP)
STA
Time
Time
Time
Negotiation for JT
BlockAck for JT
Notify
T
DATA 1
DATA 2
Time for delivery
over backhaul
Time to start JT (T)
(It may need a way to protect TXOP here.)

## Slide 9: Summary
This contribution discusses the ways to deliver user data for joint transmission from the P-AP to the S-APs.
In-band delivery will easily protect TXOP, however, it may consume time in delivering the user data from the P-AP to the S-AP(s) if the link speed between these APs is low.
Data delivery through backhaul can further increase the throughput due to a higher backhaul link speed for the data delivery compared to the in-band one.
It may need to be considered further several issues, such as a way to send a frame to the S-AP(s) to inform them of the time to transmit DATA frame to the STA, and a way to protect TXOP during for delivering the user data from the P-AP to the S-AP(s).

## Slide 10: References
[1] “Multi-AP Joint Transmission Simulations with Impairments”, IEEE 802.11-23/1843r0
[2] “Multi-AP Simulations: framework and Joint Transmission results”, IEEE 802.11-23/1176r1
[3] “Joint Transmission for UHR – Additional Results”, IEEE 802.11-23/0243r0
[4] “System Level Simulation of Co-BF and Joint Tx”, IEEE 802.11-22/1821r1
[5] “Joint Transmission for 11be”,IEEE 802.11-20/0071r1
[6] “Consideration on Joint Transmission”, IEEE 802.11-19x/1595r0
[7] “Multi-AP for reliability with Coherent and Non-coherent transmissions”, IEEE 802.11-23/2009r0
[8] “Joint Transmission for UHR – A Refresher and New Results”, IEEE 802.11-22/2188r0
[9] “Joint Transmissions: Backhaul and Gain State Issues”, IEEE 802.11-19/1089r0
[10] “Multi-AP backhaul analysis ”, IEEE 802.11-19/1588r0
[11] “WLAN Backhaul Options”, IEEE 802.11-23/0677r0