## Slide 1: Multi-AP Coordination and Roaming
Date: 2024-04-15
Authors:

## Slide 2
Abstract
In this contribution we share some thoughts on the approaches for defining multi-AP operations in 11bn, including various coordination operations as well as seamless roaming.

## Slide 3: Introduction
Multi-AP has been proposed as a UHR feature, including many variants of coordinated operations
Numerous contributions have been presented for each of the topics in EHT, 11be, UHR and in 11bn
In this contribution, we share our thoughts on the approaches of defining multi-AP operations
We also discuss potential impacts of the approaches of defining multi-AP operations on defining seamless roaming procedures

## Slide 4: Proposed Multi-AP Operations
There have been many contributions presented on the multi-AP topic in EHT, 11be, UHR and 11bn including the following:
  Coordinated TDMA
  Coordinated rTWT/TWT
  Coordinated OFDMA
  Coordinated spatial reuse
  Coordinated Beamforming
  Joint transmission
Clearly there has been a lot of interests
Majority of the contributions on multi-AP operations have been on one of these multi-AP operations

## Slide 5: Analysis of Multi-AP Operations (1)
These proposed multi-AP operations are very different
  They require different knowledge of the network topology
  They require different knowledge of the channel state information
    C-TDMA requires APs to be within range, while C-BF requires much more details
  They require sharing of different information for the correspodning coordination
    Tx/Rx timing/scheduling, Tx power, Tx/Rx RU allocation
  They have different timing requirements
    C-OFDMA, C-BF and JT require synchronization
  They have different data sharing requirements
    JT requires data sharing among the transmitting APs

## Slide 6: Analysis of Multi-AP Operations (2)
These proposed multi-AP operations also have a lot in common
  They require to identify a set of APs prior to the multi-AP operations
    E.g., a set of two APs may be sufficient for C-TDMA, but that set of APs is likely larger for other multi-AP operations such as C-rTWT, C-SR
  They require sharing of coordination information
    E.g., Tx/Rx timing/scheduling, Tx power, Tx/Rx RU allocation
  They require decisions in coordination (Arbitrations)
    E.g., if multiple APs want to use an overlapping time, who gets it?

## Slide 7: Approaches to Define Multi-AP Operations (1)
Based on the analysis, there may be two approaches defining multi-AP operations in 11bn
  Approach 1: study and define each multi-AP operation proposed
    Pro:
      Organic growth of each feature
      May leverage existing features
    Con:
      Cannot leverage commonality among different multi-AP operations
      May define overlapping signaling used for the same purpose for different operations
      May only be limited to one or two multi-AP operations
      Lack of possibility of easy expansion for future similar features

## Slide 8: Approaches to Define Multi-AP Operations (2)
Approach 2: study multi-AP operations as a whole and define a common framework
  Pro:
    Easily leverage commonality among different multi-AP operations
    May support a higher number of multi-AP operations
    Possibility of easy expansion for future similar features
  Con:
    May consume longer time to consider multiple multi-AP operations before defining a common framework
  In addition, if a common framework for multi-AP operations is defined, likely an arbitration/coordination entity needs to be defined to facilitate decisions in case of more than 2 participating APs
    E.g., a coordination/information sharing virtual entity

## Slide 9: Multi-AP Operations and Seamless roaming
Seamless roaming support has also been proposed for UHR [1][2][3][4]
  Seamless roaming also involves APs that are not co-located
  Seamless roaming also requires coordinating among multiple APs and information sharing among APs
  Seamless roaming can be easily viewed as a coordinated multi-AP operation
If a common framework and/or coordinating/information sharing entity can be defined for multi-AP operations, the same framework and coordinating/information sharing entity can be leveraged to support seamless roaming

## Slide 10: Conclusions
  Two approaches for defining multi-AP operations in 11bn has been discussed
    Approach 1: piece-wise study and define each multi-AP operation proposed
    Approach 2: study multi-AP operations as a whole and define a common framework and maybe a coordinating/information sharing entity for the case there are more than 2 participating APs
  We looked at the pros and cons for both Approaches
  Approach 2 likely will provide a better design and provide better expansion support for similar features in the future, even though it may consume a bit more time
  Defining a common framework and a coordinating/information sharing entity for multi-AP operations may benefit seamless roaming design as well

## Slide 11
References
[1] 11-22/1910r3, Seamless Roaming for UHR, Duncan Ho
[2] 11-23/237, Considerations on Seamless Roaming, Insun Jang
[3] 11-23/0170, Smooth Roaming, Liwen Chu
[4] 11-23/231, Thoughts on Seamless Roaming Under Non-collocated AP MLD Architecture, Guoguang Huang
[5] 11-23/295r1, Discussion on Multi-AP Coordination, Xiaofei Wang

## Slide 12: SP #1
Which approach for 11bn to define multi-AP operations do you prefer?
  Approach 1: piece-wise approach for each individual multi-AP operations
  Approach 2: define a unified framework for multi-AP operations
  Abs:

## Slide 13: SP #2
Do you agree that a coordinating entity should be defined to enable multi-AP operation coordination?