## Slide 1: Vendor Specific PHY Options With Minimal PHY Changes
Apr 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Motivation for Standardized PHY-level Vendor Specific Signaling Mostly a repeat from [1]
Goals:
  Signal the presence of proprietary PHY-layer features in PPDUs to devices in the transmitter’s eco-system
  Avoid confusing devices outside their eco-system by conforming to the 802.11 standard
Stakes are raised with U-SIG
  This needs to support many generations of 802.11 MAC/PHY amendments and many vendors/eco-systems
  Any misuse of reserved fields or VS-redefinition of standardized fields runs the risk that the misuse/redefinition will be exposed in future amendments
The MAC has rich and mature mechanisms for safe feature experimentation, prototyping and deployment
  Vendor Specific (sub)elements, and (Public) Action frames
  Some of these proprietary features didn’t work out, and did not burden the 802.11 standard
  Some of these proprietary features created high value and were returned to 802.11 and have been proposed/accepted as standardized features
    i.e., vendor specific extensions support a rich and healthy 802.11 eco-system
Let’s create a safe environment for PHY experimentation, prototyping and deployment too
  And can we do this with minimal PHY changes?

## Slide 3: Part A: High-level Requirements for UHR TB PPDU (Recap)
No identify confusion
  Use upper layer signaling to enable
No easy SIG field to use: needs something after user separation
  Which is limiting but apparently unavoidable
Option A:
  A new SIG field after the training for the Data field akin to the VHTSIGB field
Option B:
  Bits 11-15 of Service field
Service field already exists and suffices
Recommendation:
  Option B, unless and until 802.11 unreserves too many bits of the Service field
  To allow implementers enable VS development while remaining in compliance with 802.11, SFD should define that the 11bn amendment permits negotiated vendor specific upper layer Signaling between AP and non-AP using bits 11-15 of the Service field in a UHR TB PPDU sent by the non-AP STA to its AP.
  All such vendor specific signaling shall operate so that it never precludes standardized use of the same signaling resources.

## Slide 4: Part B: UHR (SU)/MU PPDU Perfect Identification of Vendor-Specific PPDUs is Not Required
Axiom:
  If a) a STA attempts to receive a PPDU not intended for the STA, and the STA fails to successfully receive the PSDU due to vendor specific PHY functionality and b) the PHY still sets CCA as usual, then there is near-zero cost and this situation does not need to be avoided by design.

## Slide 5: Vendor Specific Signaling Requirements when seeking minimization of PHY changes – Top Level
A STA may negotiate vendor specific behavior as a recipient with a peer using upper layer signaling (e.g., MAC-level vendor-specific signaling)
The vendor specific behavior must not affect information for third party STAs:
    PPDUs containing RTS, CTS, CF-End (and likely MU-RTS, Ack, BA) must be unchanged
    LSTF + LLTF + LSIG + RLSIG + version independent fields of the USIG must be unchanged
If the VS behavior is static
  One of the following conditions must be true:
    The STA is receiving intended PPDUs from one peer only
    The STA is receiving intended PPDUs from two or more peers, and an agreement is achieved for all peers
      However, almost always there is a window of communication before an VS agreement is established, so almost always this requirement cannot be perfectly met for non-initial peers.
    The STA is receiving intended PPDUs from two or more peers, an agreement is achieved with a subset of the peers, and the agreement includes a way for transmitting peers in the subset to identify PPDUs intended for the STA uniquely wrt PPDUs sent by peers not in the subset
If the VS behavior is dynamic (i.e., can change per PPDU)
  The “static” requirements are still needed
  As well, there needs to be a way to signal the dynamic parameters (i.e., via per-PPDU signaling)
Corner cases for APs and clients with infrastructure & P2P associations

## Slide 6: Options to identify received PPDUs with different VS behavior, while minimizing PHY changes: STA-ID is most promising
Option | Position* in PPDU | Analysis (see next slides for more detail)
BSS Color | Very early |  Not unambiguous, not adequate (see [2])
Reserved USIG bit(s) | Very early |  Needs “6”-24 bits (assuming support for up to 64+ silicon vendors or use the OUI)
New VS SIG field (see 24/0461) | Very early |  Greater PHY changes; some test complexity concerns (see [2])
STA-ID | Early | () Reliable, unless device has virtual APs/STAs in different BSSs, and there is an STA-ID collision or there is the broadcast RU
Pad bits in UHRSIG | Middling | (~) Lighter PHY changes
Waveform, such as transmitting information in the UHTLTF null subcarriers | Middling-Late |  Greater PHY changes; needs “6”-24 bits (ditto)
Service field | Late | (~) Needs “6”-24 bits (ditto)
PHY Pad bits in the Data field | Very late |  Too late to be useful
 | *The earlier in the PPDU the better | 

## Slide 7: To ensure STA-ID can unambiguously identify each transmitting peer for all conditions, we recommend a new AID Veto element
A device wishing to negotiate VS behavior as a recipient with a peer shall ensure that the AID connected* with the peer is different from the AID connected with other peers not using that VS behavior
To achieve this, if the device contains non-AP STAs in two or more BSSs (i.e., an AID taker), it needs to send a new “AID Veto element” in its (Re)Association Request for the subsequent associations for which different VS behavior is planned
  * i.e., AID assigned by peer if peer is an AP; else AID assigned to peer if peer is a non-AP STA
AID List lists the AIDs that the STA does not wish to have assigned as an AID, and is either:
  N * 2 octets, where each 2 octets contains the AID
  N * 1.5 octets + 0/0.5 octets of Pad bits, where each 1.5 octets contains 11 LSBs of the AID + 1 reserved bit
For TIM compactness, the AP wishes to allocate low AIDs, so the AP might be disinclined to accept association from a STA that vetoes too many low AIDs
NOTE – using STA-ID to unlock VS behavior means that unassociated STAs cannot use VS behavior
  Since it is hard to negotiate VS behavior pre-association, this is a tolerable constraint
Element ID | Length | Element ID Extension | AID List
1 octet | 1 octet | 1 octet | variable

## Slide 8: Options to include per-PPDU signaling for dynamic VS behavior, while minimizing PHY changes: several reasonable choices
Option | Position* in PPDU | Common / Per-User | Analysis (see next slides for more detail)
Reserved USIG bit(s) | Very early | Common | (?) Need 11bn draft to allow this for negotiated exceptions
New VS SIG field (see 24/0461) | Very early | Common |  Greater PHY changes; some test complexity concerns
Redefined bit(s) or redefined values in the User field | Early | Per-User | () Need 11bn draft to allow this for negotiated exceptions (and no change in number of bits)
Pad bits in UHRSIG | Middling | Common & Per-User |  These bits are already uncontrolled; format can be entirely VS once connected STA-IDs are unique
Waveform | Middling-Late |  |  PHY changes; receivers might depend on unexpected features of the waveform.
Service field | Late | (Common &) Per-User | () Need 11bn draft to allow this for negotiated exceptions
PHY Pad bits in the Data field | Very late | (Common &) Per-User |  Too late to be useful
 | *The earlier in the PPDU the better |  | 

## Slide 9: Risks and Concerns with These Modes
802.11be specifically created Disregard bits so that minor or per-user features could be added to the EHT PPDU PHY format (e.g., finer MCSs) without any change to the PHY Version Identifier field
  So UHR/Wi-Fi9/Wi-Fi10 APs could use EHT MU PPDUs across the client mix (EHT+UHR[+Wi-Fi9[+Wi-Fi10]])
And Validate bits/values allowed for disruptive changes, but again without any need to change the PHY Version Identifier field
Here using a Reserved bit/value in the USIG carries risks:
  A future draft amendment could assign the Reserved bit/value
  For PPDUs intended for STAs that understand the newly standardized feature (i.e., a broadcast RU or the STA’s STA-ID is listed), the Vendor Specific behavior for other STAs cannot be unambiguously signaled
    Typically requires the Vendor Specific behavior to be torn down
    Or the AP needs to find an alternative method to signal the Vendor Specific behavior
      But best to use this method from the beginning, rather than retrospectively, due to the difficulty of firmware updates!
  Worst case: implementations process such VS signaling without requiring upper layer negotiation first!?
These risks could be lowered or zeroed if UHR allocated some Reserved bits to VS signaling
  E.g., using EHTSIG in EHT MU PPDU as a hypothetical starting point, wherein B20-24 are Disregard, 802.11 could change B23-24 to be designated as Vendor Specific.
  But this denies the bits to the UHR and future amendments, so few/no such bits should be allocated

## Slide 10: Summary
802.11 has certain PHY resources (USIG fields, User fields, UHTSIG pad field, Service field etc)
Each time a vendor uses one of these PHY resources without proper guardrails, practically the PHY resources become unavailable to future amendments
Proper guardrails for PHY VS signaling include:
  All PHY VS behaviors shall be first negotiated with a peer using upper layer signaling (e.g., MAC-level vendor-specific signaling)
  A STA shall not negotiate, and shall tear down any successful negotiations for, VS behaviors whenever the STA as a recipient cannot distinguish between intended PPDUs with a VS behavior different to other intended PPDUs
    For instance, for UHR (SU)/MU PPDUs, the recipient device of VS behavior with a peer shall ensure that the AID connected* with the peer is different from the AID connected with other peers not using that VS behavior
      * i.e., AID assigned by peer if peer is an AP; else AID assigned to peer if peer is a non-AP STA
    Via AID allocation and/or the proposed AID Veto element
  For UHR TB PPDUs, VS dynamic signaling may occur in the Service field
  For UHR (SU)/MU PPDUs, VS dynamic signaling may occur in the User field and UHTSIG field
    TBD if VS dynamic signaling may occur in the USIG field; TBD if any USIG bits are allocated for VS purposes
  All such vendor specific signaling shall operate so that it never precludes standardized use of the same signaling resources.

## Slide 11: References
[1] 23/1099, “Vendor Specific SIG field”, Brian Hart (Cisco Systems)
[2] 24/0461, “Vendor Specific Signaling”, Brian Hart (Cisco Systems)

## Slide 12: Strawpoll 1a
Do you agree to add the following text to the 11bn SFD:
  11bn shall define guardrails to enable PHY-level vendor specific extensions that are safe:
    Not ambiguous to an intended recipient
    Does not introduce interoperability issues if use of the same signaling resources is standardized.
Y / N / A

## Slide 13: Strawpoll 1b
Do you agree that the problem defined in 24/461 and the proposed direction (in the same document) are promising and should be presented to a wider audience (MAC/Joint) as the next step
Y / N / A