## Slide 1: Low latency channel access Legacy impact
Date: 2024-03-06
Authors:

## Slide 2: Recap from 11-23/2126r0: problem
High Priority EDCA (HiP EDCA) mechanism based on transmission of a dedicated signal prior to general EDCA contention allow to improve tail latency :
  90-95-99th percentiles in both isolated BSS case and multi-BSS setup
  In situations with and without hidden nodes
The repetition of DS signal (i.e. an AP reply with same DS signal) has limited affect on tail latency improvement
In terms of design, it is better to have “Unique” DS signal rather than “Common” one, i.e. DS signal to be specific to a BSS
Rules to send DS signal need to be discussed
  Frequency of transmission
  AIFSN boundary for transmission

## Slide 3: Recap from 11-23/1065r0: solution
Proposal would be to isolate STAs with prioritized access from the rest of the STAs at the beginning of a contention period
  Achieve this by allowing these STAs to transmit a Defer Signal at the beginning of a contention period to force all STAs that are not sending the Defer Signal to have CCA busy and not participate in the contention period
  If multiple of these STAs have prioritized access, they will transmit the same Defer Signal at the same time with the same result on other STAs (CCA busy)
And then to allow for a contention only between the STAs with prioritized access
  Only STAs that have sent a Defer Signal can participate in this immediately following contention
  More degrees of freedom for the contention parameters setting to avoid collisions without loosing priority
    don’t necessarily need to be too aggressive in order to scale to a larger number of STAs while ensuring low collision rates (contrary to AC_VO)
Example:
  A device with the traffic in AC_VO use legacy EDCA to transmit data.
  Device is eligible to send DS signal if it experience a failure after using legacy EDCA and doubled its contention window
    After successfully attempting transmission using DS STA fall back to normal EDCA operations

## Slide 4: New material: Impact on legacy devices
What is the effect on legacy devices when UHR device use DS
  If in a BSS set of STAs is using DS for LL frame transmission and other – don’t
  What if one BSS use DS and others don’t
  A mix of above

## Slide 5: Simulation configuration
Enterprise-like layout
  1, 2 or 3 BSSes with variable number of STAs: 5,6,..,15, 16
  Out of which 2, 3 or 4 are ULL STAs
  Other STA has bidirectional full buffer BE traffic.
2x2x20Mhz @ MCS3
TXOP limit = uniform (1.5ms; 5ms)
  New TXOP limit is selected each time when STA/AP won contention
  Randomization is only to introduce “burstiness” and extra randomness into channel occupancy time
  STA Cw = 15/1023; AP Cw=15/63
  TxPower: STA = 17dBm; AP=23dBm
Location
  STAs assigned on a grid across four 4x4 cube islands, AP in the middle of the island
  Overall area size is 80x80meters
80meters
80meters
28m
31m
50m
D=9
1
2
3
4
# STAs | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
# of VO STAs | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4
% of VO STA | 40 | 33 | 29 | 25 | 33 | 30 | 27 | 25 | 31 | 29 | 27 | 25

## Slide 6: HiP EDCA for AC VO Multi-BSS setup in 80x80 and 20x20 area
ULL traffic use AC_VO access category
A STA / AP use HiP EDCA after first failure in AC_VO category
  VO traffic is bi-directional 160 bytes every average 16ms =uniform (10ms, 22ms)
  BE are legacy with bi-directional full buffer traffic, TXOP = uniform (1.5ms, 5ms)
Three cases:
  1 BSS case with
    ULL use AC_VO
    ULL use DS
    Half of streams in a BSS use VO and the other one use DS
  2 and 4 BSS case
    All BSSes use AC_VO for ULL
    All BSSes use DS for ULL
    Half of BSSes use AC_VO and the other half - DS
    Half of streams in each BSS use VO and the other one use DS
Statistic of interest:
    ETE delay

## Slide 7: 1 BSS case
VO – all ULL use legacy EDCA Half VO – half of ULL use VO
DS – all ULL use DS Half DS – half of ULL use DS
Chart: 1 BSS case, 8 STAs in BSS, 2 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0024122 | 0.0044449 | 0.005862 | 0.0099489 | 0.012174
DS | 0.0020167 | 0.0037092 | 0.0042231 | 0.0046312 | 0.0048523
Half DS | 0.001999 | 0.0037362 | 0.0042263 | 0.0045479 | 0.0046855
Halfs VO | 0.0023377 | 0.0042788 | 0.0056681 | 0.0088838 | 0.011546
Chart: 1 BSS case, 9 STAs in BSS, 3 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0029029 | 0.0063681 | 0.0090815 | 0.011655 | 0.01437
DS | 0.0020745 | 0.0038562 | 0.0043037 | 0.0046961 | 0.0049493
Half DS | 0.0020442 | 0.0038765 | 0.0042478 | 0.0047587 | 0.0051255
Halfs VO | 0.0029349 | 0.006188 | 0.0086241 | 0.012087 | 0.013776
Chart: 1 BSS case, 12 STAs in BSS, 3 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0031672 | 0.0073209 | 0.010102 | 0.014038 | 0.016563
DS | 0.0020829 | 0.0037916 | 0.0043122 | 0.0047853 | 0.0051285
Half DS | 0.0020451 | 0.0038723 | 0.004318 | 0.0047949 | 0.0053695
Halfs VO | 0.0032273 | 0.0072493 | 0.010008 | 0.015015 | 0.017733
Chart: 1 BSS case, 13 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0035338 | 0.0081388 | 0.011891 | 0.015585 | 0.018725
DS | 0.0020635 | 0.0039026 | 0.0044382 | 0.0049499 | 0.0053151
Half DS | 0.0020589 | 0.0039188 | 0.0044635 | 0.0051419 | 0.0057035
Halfs VO | 0.0032747 | 0.0074549 | 0.01015 | 0.013843 | 0.016754
Chart: 1 BSS case, 16 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0035314 | 0.0087631 | 0.011152 | 0.014561 | 0.016741
DS | 0.0020647 | 0.0039056 | 0.0044477 | 0.0050327 | 0.0054896
Half DS | 0.0020505 | 0.0038417 | 0.0043539 | 0.0048325 | 0.0053032
Halfs VO | 0.0034549 | 0.0081083 | 0.011147 | 0.014105 | 0.017101
Chart: 1 BSS case, 5 STAs in BSS, 2 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.002234 | 0.0042061 | 0.0051508 | 0.0076859 | 0.0084733
DS | 0.0019719 | 0.0035785 | 0.0041563 | 0.0045326 | 0.004674
Half DS | 0.0019224 | 0.0036102 | 0.0040787 | 0.0045722 | 0.0047167
Halfs VO | 0.0022233 | 0.0041835 | 0.004977 | 0.0074926 | 0.0089577

## Slide 8: 2 BSS case
VO – all ULL use legacy EDCA Half VO – half of ULL use VO BSS VO – half of BSS use VO
DS – all ULL use DS Half DS – half of ULL use DS BSS DS – half of BSS use DS
Chart: 2 BSS case, 5 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0029565 | 0.0067172 | 0.0092994 | 0.012298 | 0.013878
DS | 0.002094 | 0.0039468 | 0.0045109 | 0.0053097 | 0.0060466
BSS DS | 0.0019962 | 0.0037899 | 0.0043627 | 0.0049248 | 0.0053728
BSS VO | 0.0028254 | 0.0060216 | 0.0085676 | 0.01185 | 0.014509
Half DS | 0.0020818 | 0.0038126 | 0.0043469 | 0.0050082 | 0.0058946
Halfs VO | 0.0027564 | 0.0059525 | 0.0085144 | 0.010956 | 0.013102
Chart: 2 BSS case, 8 STAs in BSS, 4 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0032456 | 0.0077709 | 0.010988 | 0.014218 | 0.017399
DS | 0.002127 | 0.0040605 | 0.0045758 | 0.0052111 | 0.0058299
BSS DS | 0.0020497 | 0.0038767 | 0.0044814 | 0.0050506 | 0.0056945
BSS VO | 0.0030164 | 0.0067768 | 0.0096275 | 0.012952 | 0.016068
Half DS | 0.0020492 | 0.0038704 | 0.0044467 | 0.0051925 | 0.006027
Halfs VO | 0.0030678 | 0.007474 | 0.0098093 | 0.0139 | 0.017477
Chart: 2 BSS case, 9 STAs in BSS, 6 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0039837 | 0.0097057 | 0.012618 | 0.017175 | 0.019819
DS | 0.0021525 | 0.0040606 | 0.0046751 | 0.0054548 | 0.0066072
BSS DS | 0.0021573 | 0.0041088 | 0.0046944 | 0.005437 | 0.0059742
BSS VO | 0.003599 | 0.0087078 | 0.011534 | 0.015407 | 0.019655
Half DS | 0.0021366 | 0.0040034 | 0.0046827 | 0.0056733 | 0.0064368
Halfs VO | 0.0038153 | 0.0090346 | 0.012363 | 0.01688 | 0.020734
Chart: 2 BSS case, 12 STAs in BSS, 6 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0040187 | 0.0098508 | 0.012662 | 0.017146 | 0.019816
DS | 0.0022356 | 0.0042066 | 0.0048676 | 0.0064017 | 0.0073891
BSS DS | 0.0021857 | 0.0041693 | 0.004772 | 0.0058657 | 0.0068018
BSS VO | 0.0038068 | 0.00942 | 0.012688 | 0.017109 | 0.020361
Half DS | 0.0021628 | 0.0041708 | 0.0048694 | 0.0057324 | 0.0067636
Halfs VO | 0.0037825 | 0.0092183 | 0.011841 | 0.015802 | 0.018899
Chart: 2 BSS case, 13 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0045467 | 0.011278 | 0.014577 | 0.019471 | 0.022838
DS | 0.0022049 | 0.0042577 | 0.0049712 | 0.0061653 | 0.0070266
BSS DS | 0.0022276 | 0.0043886 | 0.0050601 | 0.0064872 | 0.0075305
BSS VO | 0.0040379 | 0.009631 | 0.013158 | 0.017034 | 0.020298
Half DS | 0.0021765 | 0.0041724 | 0.0049344 | 0.0063671 | 0.0078178
Halfs VO | 0.0042341 | 0.010125 | 0.013549 | 0.017355 | 0.020813
Chart: 2 BSS case, 16 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0047933 | 0.011752 | 0.015977 | 0.021025 | 0.024816
DS | 0.0022076 | 0.0043184 | 0.0051239 | 0.0063911 | 0.0072899
BSS DS | 0.0022466 | 0.0043784 | 0.0051812 | 0.0060752 | 0.0072039
BSS VO | 0.0041658 | 0.010557 | 0.014063 | 0.019169 | 0.022277
Half DS | 0.002189 | 0.0042818 | 0.0051841 | 0.0068189 | 0.0082426
Halfs VO | 0.0041839 | 0.010303 | 0.013235 | 0.017081 | 0.019663

## Slide 9: 4 BSS case
VO – all ULL use legacy EDCA Half VO – half of ULL use VO BSS VO – half of BSS use VO
DS – all ULL use DS Half DS – half of ULL use DS BSS DS – half of BSS use DS
Chart: 4 BSS case, 5 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0037378 | 0.0089397 | 0.012215 | 0.016514 | 0.019281
DS | 0.0024208 | 0.0047329 | 0.0060946 | 0.0083567 | 0.010527
BSS DS | 0.0022741 | 0.0044894 | 0.0055051 | 0.0072917 | 0.0085124
BSS VO | 0.0036584 | 0.0087768 | 0.011898 | 0.016031 | 0.019016
Half DS | 0.0023358 | 0.0045789 | 0.0058928 | 0.0078005 | 0.0094901
Halfs VO | 0.0033942 | 0.0080891 | 0.010873 | 0.014787 | 0.017414
Chart: 4 BSS case, 9 STAs in BSS, 12 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.004618 | 0.011404 | 0.014828 | 0.019401 | 0.022852
DS | 0.002632 | 0.0055039 | 0.0070464 | 0.0093039 | 0.011348
BSS DS | 0.002514 | 0.0052168 | 0.0065373 | 0.0082171 | 0.0096282
BSS VO | 0.0044753 | 0.01109 | 0.014782 | 0.019932 | 0.023389
Half DS | 0.0025462 | 0.005152 | 0.0068554 | 0.0094409 | 0.011206
Halfs VO | 0.0045683 | 0.010985 | 0.01446 | 0.019752 | 0.02297
Chart: 4 BSS case, 8 STAs in BSS, 8 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0041162 | 0.0098462 | 0.013213 | 0.018038 | 0.022401
DS | 0.0025542 | 0.0050293 | 0.0064688 | 0.0089624 | 0.011112
BSS DS | 0.002409 | 0.0046903 | 0.0059387 | 0.0079304 | 0.0093213
BSS VO | 0.0039846 | 0.010078 | 0.013387 | 0.017762 | 0.021365
Half DS | 0.0025208 | 0.0050094 | 0.0066577 | 0.009243 | 0.010818
Halfs VO | 0.0036715 | 0.0087992 | 0.012242 | 0.016564 | 0.019461
Chart: 4 BSS case, 12 STAs in BSS, 12 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.004962 | 0.012184 | 0.016007 | 0.021361 | 0.02611
DS | 0.0027006 | 0.0055246 | 0.0071018 | 0.0096506 | 0.011657
BSS DS | 0.0026546 | 0.005623 | 0.0073885 | 0.0094386 | 0.011303
BSS VO | 0.0047937 | 0.011969 | 0.016377 | 0.021791 | 0.025822
Half DS | 0.0027066 | 0.005651 | 0.0073584 | 0.0095351 | 0.011534
Halfs VO | 0.0047331 | 0.011758 | 0.015588 | 0.020433 | 0.024383
Chart: 4 BSS case, 13 STAs in BSS, 16 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0050732 | 0.012287 | 0.01631 | 0.02165 | 0.026135
DS | 0.0028472 | 0.0061299 | 0.0080833 | 0.01024 | 0.012376
BSS DS | 0.0028033 | 0.0060402 | 0.007979 | 0.010718 | 0.012697
BSS VO | 0.0051969 | 0.012826 | 0.016915 | 0.022348 | 0.025466
Half DS | 0.0028603 | 0.0063412 | 0.0082093 | 0.011135 | 0.013372
Halfs VO | 0.0052018 | 0.012876 | 0.017175 | 0.022632 | 0.026581
Chart: 4 BSS case, 16 STAs in BSS, 16 ULL flows
| mean | 90 | 95 | 98 | 99
VO | 0.0051569 | 0.012749 | 0.016999 | 0.02216 | 0.027012
DS | 0.0028706 | 0.0061538 | 0.0081113 | 0.010612 | 0.012603
BSS DS | 0.0028561 | 0.006205 | 0.0082216 | 0.010674 | 0.013063
BSS VO | 0.0054591 | 0.013387 | 0.018353 | 0.024122 | 0.028709
Half DS | 0.0028834 | 0.006508 | 0.0086981 | 0.011602 | 0.01404
Halfs VO | 0.005322 | 0.012861 | 0.017588 | 0.024083 | 0.028586

## Slide 10: Conclusion
There is no negative impact on LL stream using legacy EDCA mechanism in presence of devices using HiP EDCA mechanism