## Slide 1: Follow Up on High Level Thoughts on DRU Design
Date: 2024-03-xx
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Qifan Chen |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Distributed transmission shows significant power gain to mitigate PSD limit, as such it was adopted as 11bn feature in the last IEEE meeting
Before discussing the detailed design options, it is better to first converge on high level directions
In this presentation we will refresh our thoughts and recommendations

## Slide 3: dRU Spreading BW and RU Sizes
For 20/40/80MHz PPDU BW, it is reasonable for all dRUs to spread to PPDU BW
For PPDU BW>80MHz, still recommend to limit dRU spreading BW to 80MHz to balance gain vs complexity
  Leave spreading BW > 80MHz to future generation
Prefer BW dependent dRU size support to maximize BW and power efficiency
  Due to marginal gain, recommend not to support MRU to reduce dRU tone plan design /implementation/testing complexity
  20MHz: RU26, RU52, RU106
  40MHz: RU26, RU52, RU106, RU242
  80MHz: RU52, RU106, RU242, RU484

## Slide 4: Mixture of dRU and rRU
For 20/40/80MHz PPDU, mixture of dRU + rRU is not preferred
  More complicated in scheduling, tone plan, signaling and AP receive processing
  dRU can spread over entire PPDU BW to max Tx power
For 160/320MHz PPDU, hybrid mode can be supported with limited flexibility to reduce scheduling and signaling complexity
  Propose per 80MHz decision: each 80MHz segment can use either dRU or rRU but no mixture

## Slide 5: Supporting STA in wide BW OFDMA
Mainly the following two cases
  20MHz operation STA in 80, 160, 320MHz
  80/160MHz operation STA in 160, 320MHz
80/160MHz operation STAs fit well with the 80MHz spreading BW limit
For 20MHz operation STA in wide bandwidth OFDMA, open to more discussions on the supported use cases and dRU configurations
  Mixing different spreading bandwidth in the same frequency range brings challenges to the tone plan design and adds implementation complexity
  If there is strong need for supporting 20MHz operation STA in an 80MHz dRU segment, we can potentially consider OFDMA dRUs with different spreading bandwidth (e.g. dRU20+dRU20+dRU40)
    Note that this will reduce the spreading gain for non 20MHz operation STAs

## Slide 6: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  11bn supports dRU transmission with spreading BWs of 20MHz, 40MHz and 80MHz

## Slide 7: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  11bn supports the following BW dependent dRU size support to maximize BW and power efficiency
    No MRU in distributed transmission
    20MHz: RU26, RU52, RU106
    40MHz: RU26, RU52, RU106, RU242
    80MHz: RU52, RU106, RU242, RU484

## Slide 8: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  11bn supports per 80MHz dRU/rRU switch if PPDU BW >80MHz and no hybrid dRU and rRU mode for up to 80MHz
    dRU (distributed tone RU)
    rRU (regular RU)

## Slide 9: Straw Poll #4
Do you agree to add the following text to the TGbn SFD?
  In a punctured 80MHz subblock, 11bn only supports the spreading BWs of 20MHz and 40MHz with dRU transmission