## Slide 1: Control Frame Protection Follow Up
Date: 2024-03-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: MAC Header Protection
Currently all unicast Data/Management frames between a STA supporting MAC header protection and its associated AP supporting MAC header protection have their MAC headers being protected.
The following fields are added in the unicast Data/Management frames for the MAC header protection:
  KID, PN MIC.
The assumption for protecting the unicast Data/Management frames is that a third-party STA/AP will not decode the unicast Data/Management frames that are not addressed to it.

## Slide 3: Analysis of Active Scanning Rules
The following is part of Active scanning rules:
This means that a unicast Probe Response frame may be received by a third-party STA.

## Slide 4: Observation of Various Management Frames
Observation 1: most likely the management frame generated by hardware will not carry the critical information in MAC header.
Observation 2: if the frame body of a unicast management frame is not protected, the MAC header will not carry the critical update.

## Slide 5: Protected Unicast Management Frame Clarification (1)
Proposal option 1:
  The MAC header of the unicast Data/Management frame between the peer AP and STA in State 4 is protected with the following exception
    The MAC header of the Probe Response is not protected.

## Slide 6: Protected Unicast Management Frame Clarification (2)
Proposal option 2:
  The MAC header of the unicast Data/Management frame between the peer AP and STA in State 4 is protected with the following exception
    The MAC header of the Probe Response is not protected.
    The MAC header of the unicast frame for measurement is not protected. The Power Management, More Data of such frame are ignored by the recipient, and the frame is not allowed to carry HTC field
      Frame for sounding report (CSI frame, Compressed/Uncompressed Beamforming frame , VHT Compressed Beamforming frame, HE/EHT/UHR Compressed Beamforming/CQI frame)
      LMR
      FTM frame
      Fine Measurement frame.
  A variant to option 2 is that the MAC header of an unprotected unicast frame for measurement is not protected.

## Slide 7: Protected Unicast Management Frame Clarification (3)
Proposal option 3:
  The MAC header of the unicast Data/Management frame between the peer AP and STA in State 4 is protected with the following exception
    The MAC header of the Probe Response is not protected.
    The MAC header of the unicast frame that is not robust Management frame is not protected. The Power Management, More Data of such frame are ignored by the recipient, and the frame is not allowed to carry HTC field

## Slide 8: Explicit Indication of MAC Header Protection
A unicast Data/Management frame carry the indication about whether the MAC header of the unicast Data/Management frame is protected or not.
  Such indication can be carried as follows:
    Option 1: the reserved bit in the MPDU Delimiter of an A-MPDU subframe is used to indicate whether the MPDU has protected MAC header.
    Option 2: the PHY header is used to indicate whether the MPDU has protected MAC header.
    Option 3: one of the reserved bits in CCMP/GCMP header is used to indicate whether the MPDU has protected MAC header. The Header Protection field with Key ID, PN and MIC is immediately after GCMP Header.
      The Header Protection field is not encrypted.
      This option is not suitable for MAC header protection of a Management frame that is not a robust management frame (a management frame that is eligible for protection).