## Slide 1: Considerations of A Unified Initial Control Frame Design
Date: 2024-06-08
Authors:

## Slide 2
Abstract
Initial control frame (ICF) and initial control response (ICR) frame exchanges were discussed in different scenarios, e.g., [2-3].
Different procedures may be needed for different scenarios.
  However, they share some commonalities if we consider them as the dynamic change from one mode to another.
In this contribution, we review ICF design considerations for below scenarios:
  Non-Primary Channel Access (passed motion [1])
  Dynamic subchannel operation
  Power saving (passed motion [1])
  In-device coexistence
  Dynamic puncturing for Secondary Channel
Further, we summarize the design considerations and discuss whether a unified design for ICF should be considered.

## Slide 3
Non-Primary Channel Access
Change of mode: Primary channel mode vs non-primary channel mode
General procedure:
  An AP announces a preselected anchor channel.
  When the primary channel is occupied by OBSS transmissions, the AP and its associated non-AP STAs switch to monitor the anchor channel.
  The AP/STAs perform channel access on the anchor channel.
  First frames exchanged are ICF/ICR.
ICF design considerations:
  Support one-to-one transmissions and one-to-multiple transmissions
  Support both DL/UL transmissions.
    ICF could be initiated by an AP or a non-AP STA.
Existing Trigger frame, e.g., MU-RTS/BSRP, may be reused.
  We need to extend them to allow uplink transmissions of the ICF.

## Slide 4
Dynamic Subchannel Operation
Change of mode: Static subchannel mode vs dynamic subchannel mode
General procedure :
  An AP acquires a wideband channel. The AP asks one or more STAs to park on a secondary subchannel by transmitting an ICF.
  The intended STA switches to the secondary subchannel and respond with an ICR.
ICF design considerations:
  Including padding so the intended STAs have time to switch.
  Support both one-to-one and one-to-multiple transmissions.
  The ICF is transmitted in DL by the AP.
Existing Trigger frame may be reused to convey minimum necessary information.
  If the ICR is carried by non-HT Dup PPDU which are not transmitted on the primary channel, modifications to the existing TF are needed.
  Receiving STAs need to distinguish whether it is a legacy Trigger frame or a Trigger frame for DSO (so that it could park on the secondary channel till the end of the TXOP).

## Slide 5
Power Saving
Change of mode: Power save mode vs full operation mode.
General procedure:
  STAs are in the power save mode with low Rx Nss, narrow Rx bandwidth, low MCS, etc.
  A STA switches to the operation mode indicated in the ICF frame.
ICF design considerations:
  Extra padding is needed for the STA to switch mode.
  Both one-to-one and one-to-multiple communications should be considered.
  The ICF is transmitted in DL by the AP.
    If AP power saving is considered, then the ICF could be initiated by a non-AP STA.
  Operation related parameters, such as the maximum Tx bandwidth, maximum Tx Nss, maximum Tx MCS in the upcoming TXOP could be indicated in the ICF.
No existing frame can be used without modification.

## Slide 6
Coexistence
Change of mode: Interference-free mode vs interference mode
General procedure:
  If a STA foresees an interference (e.g., in-device) may happen, it may transmit an ICF/ICR to report its unavailable time and subchannels.
ICF design considerations:
  Should allow both AP and non-AP STA to initiate the transmission of the ICF.
  If the ICF is initiated by an AP, we may consider to allow one-to-multiple solicitation.
  Unavailable time, unavailable subchannel(s) could be carried in the ICF if the ICF is transmitted by a non-AP STA in an unsolicited way.
  Mode change may not always happen immediately after the ICF/ICR exchange.
Some contributions (e.g.,[4-8]) suggest reusing (MU)RTS/CTS frame exchanges for the solicited case.
  Unavailable time is possible to be signaled this way with modified rules.
Solicited
Unsolicited

## Slide 7
Dynamic Puncturing
Change of mode: Static puncturing mode vs dynamic puncturing mode.
General procedure:
  The ICF/ICR exchange indicates the dynamic puncturing is allowed in the TXOP.
  Method 1: dynamic puncturing information is carried in the ICF/ICR (Pros: STAs could exchange puncturing patterns; Cons: hard to support multi-cast if the ICR needs to carry user specific information.
  Method 2: dynamic puncturing pattern is carried in the USIG on each 80MHz subblock in the UHR PPDU. The responding STAs may use the full Rx bandwidth to acquire the puncturing pattern. (Pros: support one to multiple. Cons: STA1 may not know the punctured channel of STA2).
ICF design considerations:
  Both one-to-one and one-to-multiple communications should be considered.
  The ICF could be initiated by an AP or a non-AP STA.
No existing frame can be used without modification.
  At least one field to indicate the dynamic puncturing may happen in the TXOP.

## Slide 8
General Design Considerations for ICF
ICF | NPCA | DSO | Power Saving | Coexistence | Dynamic Puncturing | Highlighed Design Consideration
Transmitted before Mode Change | No | Yes | Yes | Yes | No | 
ICF/ICR in the same Mode | Yes | Maybe | Maybe | Yes | Yes | If with diff modes, padding is needed
Padding (e.g., FCS2) | No | Yes | Yes | No | No | 
Carried in non-HT Dup PPDU | Maybe | Maybe | Maybe | Maybe | Maybe | To support lagecy NAV setting, better to use non-HT Dup PPDU
Support multicast transmission (one-to-multiple) | Yes | Yes | Yes | Maybe | Yes | Could reuse TF. Need to design whether ICR is carried in TB PPDU
Initiated by an AP | Yes | Yes | Yes | Yes | Yes | 
Initiated by a non AP STA | Yes | No | Maybe | Yes | Yes | TF is DL only now. Either using TF with modification or a new type, or a new frame.
Contains Max BW | Maybe | Maybe | Yes | Yes | Maybe | With unified design, we could define different types/variants for different use cases/scenarios
Contains Max Tx/Rx Nss | Maybe | Maybe | Yes | Yes | Maybe | 
Contains Max MCS/Rx MCS | Maybe | Maybe | Yes | Yes | Maybe | 
Contains Dynamic puncturing | Maybe | Maybe | Maybe | Yes | Yes | 
Contains unavailable time | No | No | No | Yes | No | 
Contains QoS | Maybe | Maybe | Maybe | Maybe | Maybe | Good to have in all cases

## Slide 9
Why a Unified Design is Desirable?
With a unified frame design, it is easier to consider all the requirements below:
  Efficiency: one design goal should be the shortest transmission and reception time of the ICF. A unified frame with a mode change type indication may be designed for the purpose.
  Flexibility: a well-defined frame structure should allow the ICF transmitted in DL/UL, with unicast transmissions/multicast transmissions.
  Extendibility: by defining different mode change types, it is easier to extend the use of the ICF to any future scenarios.
  Backward compatibility: to support legacy devices to set NAV correctly, some types of the ICF should be carried by non-HT or non-HT Dup PPDU.
    We don’t expect legacy STAs to perform dynamic mode change and thus they don’t need to decode all the fields carried by the ICF.
Options:
  Reusing Trigger frame with exiting types (modifications are needed, e.g., needs to know at least the purpose of the ICF).
  Reusing Trigger frame with a new type.
  A new frame.

## Slide 10
Summary
Reviewed NPCA, DSO, Power saving, in-device coexistence and dynamic puncturing procedures.
Although they are different procedures to achieve different purposes, they share some commonalities.
A unified design of initial control frame for dynamic mode change is preferred.
3 options are proposed for the ICF design.

## Slide 11
Reference
IEEE 802.11-24/0209r3, Specification Framework for TGbn
IEEE 802.11-24/0042r1, Flexible Control frames
IEEE 802.11-24/299r1, Initial control frame for bandwidth-switching modes
IEEE 802.11-24/0094r0, Probe-Before-Talk and Unsolicited Unavailability Announcement for Co-ex Management
IEEE 802.11-23/1964r1, Coexistence Protocols for UHR
IEEE 802.11-23/2026r0, Balanced Wireless In-Device
IEEE 802.11-23/2002r2, In-device Coexistence and P2P – follow-up
IEEE 802.11-24/1934r0, in-device interference mitigation follow up

## Slide 12
Straw Poll 1
Do you agree to define a new mechanism in 802.11bn that enables an UHR STA to switch from one mode to another mode dynamically.
  NOTE 1 – Dynamic mode switching may include
    Primary channel mode vs non-primary channel mode
    Static subchannel mode vs dynamic subchannel mode
    Power save mode vs full operation mode
    Interference-free mode vs interference mode
    Static puncturing mode vs dynamic puncturing mode
  NOTE 2 – The exact types of dynamic mode switching are TBD

## Slide 13
Straw Poll 2
Do you agree to define a unified initial control frame in 802.11bn that enables an UHR STA to switch from one mode to another mode dynamically.
  NOTE 1 – The exact types of dynamic mode switching are TBD