## Slide 1: MAC header/data integrity with relaxed receiver requirement
Authors:
Name | Affiliations | Address | Phone | email
Li-Hsiang Sun | MediaTek | 13480 Evening Creek Drive North, Suite 600, San Diego, CA 92128 |  | li-hsiang.sun@mediatek.com
Gabor Bajko |  |  |  | 
Frank Hsu |  |  |  | 
James Yee |  |  |  | 
Yonggang Fang |  |  |  | 
Kaiying Lu |  |  |  | 
Date: 2024-03-xx

## Slide 2: Background
[1] proposed header protection for individually addressed Data and Management frames
  A new MIC is generated for the header fields each time an MPDU is (re)transmitted
It is generally assumed that the recipient of unicast data/management frames would verify header MIC before sending Ack/BA
Considerations at receiver side for MIC verification before BA/Ack:
  Recipient may have processing/cost constraints/performance degradation for processing all the MICs received in a high rate AMPDU before sending immediate ack/BA
  Extra padding/delimiters in an AMPDU reduces throughput
  Header MIC check does not guarantee the data integrity
[2] illustrates an issue of a jam/record/replay attack
  proposed to use portion of the TSF as PN in the header MIC
  Verifying MIC and TSF before sending ACK comes at an even higher cost to receiver

## Slide 3: Alternatives to MIC check before sending ack
Recipient would not need to check the MIC before sending protected ACK
Originator would check that the ACK is genuine and solicited before removing PPDUs from the retransmit buffer and confirming the MAC state change
Originator would verify the MIC of the Ack
  Even if the Ack is unsolicited
    Preform replay check. Update of replay counter if Ack is fresh
    Discard the Ack if unsolicited
To prevent the ack being replayed by an attacker at a later time, a TSF/signature protected Ack may be needed
  Transmitter would check the ACK with TSF/signature and MIC before accepting the ACK
  Including a TSF/signature into the MIC of the ACK is FFS
Consequences of an attack at both side are still prevented.

## Slide 4
A
Data frame [H_MIC, D_MIC]
B
Protected ack [MIC]
Data frame [H_MIC, D_MIC]
A
B
Protected ack [MIC]
Check H_MIC before sending ACK
Check D_MIC after sending ACK
Check MIC before taking any action
Check both H_MIC and D_MIC after sending ACK
BAR
Protected ack
Check MIC before taking any action
Check both H_MIC and D_MIC before sending ACK
The below 2 scenarios provide same level of protection
Only FCS check before sending ACK

## Slide 5
Attack scenarios which can be prevented without TSF/signature in the protected ack:
  Attacker modifies data frame, does not replay ACK
  Recipient protects the ack instead of checking the header MIC of the soliciting frame before Ack

## Slide 6: scenario I.1
MITM sends modified MPDUs without header change
Instead of being detected by time-based header MIC check at recipient side, originator can detect because of unsolicited ack
SN=1,2,3,4
A
B
MITM
Protected ack SN=1,2
Modified data SN=1,2
A verifies the protected ack, updates replay counter for the ctrl frame protection (if not replay)
A then drops the ack b/c
it’s unsolicited
Expecting solicited ack

## Slide 7: scenario I.1 extension
MITM sends modified MPDUs with both data and header change for SN=1,2
B sends first protected ack for SN=1,2,3,4 after FCS check only
A detects an unsolicited ack and does not update its tx buffer/MAC states
B verifies header and body MICs of SN=1,2,3,4, only SN=3,4 pass
After detecting attack, A sends a protected standalone protected BAR to check the receiver status
B sends protected ack for SN=3,4
A verifies the ack and removes SN=3,4 from TX buffer
SN=1,2,3,4
A
B
MITM
Protected ack SN=1,2,3,4
BAR
SN=1,2,3,4, modified data and header for SN=1,2
Protected ack for SN=3,4
A verifies the protected ack, updates replay counter for the ctrl frame protection (if not replay)
A then drops the ack b/c it’s unsolicited
Expecting solicited ack

## Slide 8: scenario I.2
MITM sends fakes data
Instead of being detected by header MIC check at recipient side, it can be detected by originator because of unsolicited ack
Fake SN=1,2
A
B
MITM
Protected ack SN=1,2
A verifies the protected ack, updates replay counter for the ctrl frame protection (if not replay)
A then drops the ack b/c it’s
unsolicited

## Slide 9
Verifying header MIC before ack as per [2] | Check only FCS before ack as proposed in this doc
B checks FCS | B checks FCS
B verifies header MIC | B sends protected Ack (w or w/o TSF/signature) using a per-PPDU partial state scoreboard
B verifies TSF in header close to the current TSF | A verifies the MIC of the ack and its freshness, performs replay check of the Ack
B updates MAC states, performs duplicate detection, updates scoreboard | A removes ack’ed MSDU from TX buffer, updates MAC states
B sends protected ack | B verifies header and body MICs* and checks replay of both,
A verifies the MIC of the ack, performs replay check of the Ack | B updates MAC states, performs duplicate detection
A removes ack’ed MSDU from TX buffer, updates MAC states | B buffers and re-orders
B verifies body MIC*, buffers, re-orders, and checks replay | 
*both mechanisms cannot handle the body MIC check failure after ack

## Slide 10: Conclusion
For the scenarios in which the Ack is not replayed by attacker, checking the header MIC at the receiver side before sending the ACK does not provide additional protection vs the case when the header MIC is checked at the receiver side after sending protected ACK
  Assuming the protected ACK is verified at the sender side before updating its TX buffer, MAC layer states
Shifting the freshness-checking burden to the originator side, which is simpler to implement
  Originator does not have a SIFS deadline of MIC processing. The MIC check, and the follow-up actions can happen in parallel with the transmission of other MPDUs in the TXOP
  Originator only verifies a single response frame from each recipient
  Recipient does not need to have a SIFS deadline for TSF protected header MIC checking. Recipient checks header/data MIC after sending ack. It won’t change state/act based on the MPDUs yet be verified.

## Slide 11
Attack scenarios which can only be protected with TSF/signature in the protected ack
  II.1 Attacker modifies the data frame and jams sender to prevent it from receiving the ACK
  II.2 Attacker injects data frame to replay ACK later
  III.3 Attacker jams sender to prevent it from receiving ACK, then jams recipient to prevent it from receiving the resent data with modified header and replays ACK

## Slide 12
A
Data frame [H_MIC, TSF, D_MIC]
B
Protected ack [MIC]
Data frame [H_MIC, no TSF, D_MIC]
A
B
Protected ack [MIC, TSF/sig]
Check H_MICand TSF before sending ACK
Check D_MIC after sending ACK
Check MIC before taking any action
Check both H_MIC and D_MIC after sending ACK
BAR
Protected ack
Check MIC and TSF/sig before taking any action
Check both H_MIC and D_MIC before sending ACK
The below 2 scenarios provide same level of protection for scenarios II.1 and II.2
Only TSF/sig in ACK (lower figure) can protect against scenario II.3
Only FCS check before sending ACK

## Slide 13: scenario II.1
MITM sends modified MPDUs with both data and header change
Instead of being detected by time-based header MIC check at recipient side, it can be detected by time-based protected ack
SN=1,2,3,4, PM=1
A
B
MITM
Protected ack SN=1,2
Replayed Protected ack SN=1,2
BAR, PM=1
Modified data SN=1,2, PM=0
A verifies the protected ack, updates replay counter for the ctrl frame protection (if not replay)
A then drops the ack b/c
time/sig-based protected ack not fresh
Expecting solicited ack

## Slide 14: scenario II.2
MITM sends fakes data
MITM buffers and replays protected ack
Instead of being detected by header MIC check at recipient side, it can be detected by time-based protected ack at originator side
Fake SN=1,2
A
B
MITM
Protected ack SN=1,2
Replayed Protected ack SN=1,2
Genuine SN=1,2,3,4
A verifies the protected ack, updates replay counter for the ctrl frame protection (if not replay)
A then drops the ack b/c
time/sig-based protected ack not fresh

## Slide 15: scenario II.3 (can only be protected if TSF/sig is in ACK)
A reTX data with a newer header, then MITM relays the ack
Cannot be detected by header MIC check at recipient side, but it can be detected at originator side by time-based protected ack at originator side
Genuine SN=1,2, PM=0 (same as previous pkts)
A
B
MITM
Protected ack SN=1,2
Replayed Protected ack SN=1,2
Genuine SN=1,2, PM=1 (change)
A verifies the protected ack, updates replay counter for the ctrl frame protection (if not replay)
A then drops the ack b/c
time/sig-based protected ack MIC check not fresh
Expecting solicited ack

## Slide 16: Preventing attack scenarios II
Feasibility of using TSF for Ack protection needs to be evaluated
Need to resolve several additional issues before we can make use of TSF:
  TSF is currently not protected in Beacon
  Even if TSF would be protected in Beacon
    It was protected by a group key which is less secure, but it is used later in unicast frame exchange
    Protected beacon itself can be replayed causing STA to be unsynchronized with AP
Adding TSF protection in TGbn timeframe may be difficult, instead, we may
  Only handle attacks in type I scenarios (cases in which originator receives the ack), or
  Instead of making use of TSF, handle attacks in type I and II scenarios by introducing some linkage between soliciting frame and ack to ensure the timeliness of the ack
    See next slide

## Slide 17: linkage between soliciting frame and ack
Inputs to Ack/BA MIC may include additional data which contains info of the soliciting PPDU
  e.g. some bits in soliciting MPDUs, with bit locations known by originator and recipient
    Difficult for attacker to selectively replace some bits while not changing others
  e.g. header MIC, # of symbols between the MIC and the ack
    Difficult for attacker to send unpredictable bits (header MIC) and altered bits (altered header fields) in the same symbol at the correct time
  e.g. soliciting PPDU length and one or more of the corrected received header MIC
preamble
MPDU1√
MPDU3 √
MPDU2
x
MPDU4
√
ACK
MIC
Some bits from soliciting PPDU as input of Ack MIC
SIFS

## Slide 18: Reference
[1] 11-23/1888r1 “MAC header protection – follow-up”
[2] 11-23/1960 “Enhanced replay detection for header protection”

## Slide 19: SP1
Do you agree to define a mode that a recipient only checks the FCS of the soliciting individually addressed data and management frame with MAC header protection before sending protected immediate acknowledgement, and the sender checks the MIC in the acknowledgement?

## Slide 20: SP2
Do you agree that if a recipient only checks the FCS of the soliciting individually addressed data and management frame with MAC header protection before sending immediate acknowledgement, then the recipient shall check the PN and MIC of the MAC header protection while processing the solicited frame after sending the acknowledgement?