## Slide 1: Trigger, BA, and BAR Protection Follow Up
Date: 2024-09-24
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Ido Ouzieli |  |  |  | 
Danny Alexander |  |  |  | 
Daniel F Bravo |  |  |  | 
Laurent Cariou |  |  |  | 
Robert Stacey |  |  |  | 
Ehud Reshef |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Trigger, BA, BAR protection has been discussed in [1-9]
In this presentation,
  We elaborate why Trigger, BA, BAR protection are essential for UHR from security perspective
  We illustrate design consideration to show that protection is feasible

## Slide 3: Motivation for Trigger protection
Trigger frame has been used by many important functionalities and there is a trend to load it with even more functionalities in UHR as initial control frame
Each functionality has an attack vector and Trigger frame protection prevents the attack vector
Functionality | Attack
transitioning from low capability mode to high capability mode | Force one or more STAs in BSS to be in high capability mode and lose benefits of staying in low capability mode. Enable other attacks at any time. Similar attack on mobile AP.
Solicit data/management | Force one or more STAs in BSS to transmit data/management to the void (due to TB) and drop frames when retry limit hits
Move window of Rx buffer | Force one or more STAs in BSS to move window of Rx buffer
DSO | Force one or more STAs in BSS to be in unexpected channels and guarantee missing important BSS information

## Slide 4: Motivation for BA/BAR protection
BA traditionally only indicates acknowledgement, but there is a trend to include other feedbacks (ex unavailability [10]) in Multi-STA BA frame as ICR.
  Fake acknowledgement drops the frame in the transmitter queue
  Fake unavailability denies operation for a long period of time since peer will not even attempt to transmit any frame
  Other attack depends on the feedbacks that we add
Proposal: focus protection on only Multi-STA BA for its flexible format and potential importance for including various feedback. Hence, we protect both ICF and ICR for UHR.
BAR is used to solicit the BA. It has its useful functionalities to move window as well.
  Disabling the moving functionality is not ideal
  Fake BAR also randomly requests client to send useless stuff
Proposal: focus protection on compressed BAR and multi-TID BAR

## Slide 5: Mode of Protection
For backward compatibility, authentication only is the only direction
To simplify protocol design, can mandate GMAC-256, which is supported by all 11be STAs due to support of GCMP-256, is anyhow the best cipher we get, and works even for Quantum attack
Separate keys for individually addressed and group addressed control frame like today
  Group key per BSS like today and delivered with similar approach of other group keys
  Individual key per MLD like today and can have per link PN, per link replay counter and per link TA as Nonce to have independent PN assignment among links

## Slide 6: MIC calculation
Can follow similar operation of GMAC-256 used in BIP with tweak
AAD includes Frame Control field, Duration field, RA field, and TA field, which is common for all 3 frames
  No need to mask out since there is no retransmission of control frame
MIC calculation includes AAD, nonce, and contents after TA field and before MIC field
  Do not include MIC field and fields after MIC fields (likely padding) to save time

## Slide 7: Padding consideration
Processing delay for verifying MIC can be addressed by padding after MIC which is feasible in Trigger frame (already there), Multi-STA BA (flexible format), BAR (only individually addressed)
Processing delay for preparing MIC in solicited frame can be addressed by padding in soliciting frame
  Padding in Data (can be done already with MPDU delimiter with zero length) to solicit protected Multi-STA BA
  Padding in BAR or Trigger (can be done already due to above consideration) to solicit protected Multi-STA BA

## Slide 8: Format Feasibility
We will need key ID, PN and MIC in the frame that can be backward compatible for group addressed version
For Trigger frame,
  Key ID needs to be early, and we have spaces in common info field or special user info field.
  PN and MIC can be inserted in a similar way of intermediate FCS
For BA/BAR,
  Key ID needs to be early, and we have spaces in BAR control and BA control.
  PN and MIC can be inserted using flexible format of Multi-STA BA and the fact that we only need to protect individually addressed BAR

## Slide 9: Conclusion
We discuss protection of Trigger frame, BA, and BAR
  Propose to focus on Trigger, Multi-STA BA, compressed BAR and multi-TID BAR
We propose to mandate GMAC-256 for MIC only protection
We explain that design of individual key, group key, AAD and MIC calculation can follow existing principle
We elaborate padding consideration and why format is also feasible to be backward compatible for group addressed frame

## Slide 10: Straw Poll #1
Do you support the following in 802.11bn?
  Define Trigger frame protection
  Define BAR frame protection for Compressed BAR and Multi-TID BAR variants
  Define BA frame protection for Multi-STA BA variants

## Slide 11: Straw Poll #2
Do you support to use GMAC-256 to protect group addressed control frame and individually addressed control frame that are defined to be protected?

## Slide 12: Straw Poll #3
Do you support the following?
  Have a pairwise key between an AP MLD and a non-AP MLD with per link PN and replay counter to protect individually addressed control frames between them that are defined to be protected
  Have one additional group key per BSS to protect the group addressed control frames that are defined to be protected.

## Slide 13: Straw Poll #4
Do you support that GCM nonce construction for the control frame that are defined to be protected will use Address 2 field from the MAC header?

## Slide 14: Straw Poll #5
Do you support the following?
  the AAD construction for protected Trigger/BA/BAR includes at least Frame Control field, Duration field, RA field, and TA field without mask out
  the MIC calculation for protected Trigger/BA/BAR includes AAD, nonce, and contents after TA field and before MIC field

## Slide 15: Reference
[1] 11-23-286 Trigger frame protection
[2] 11-23-0312 Thoughts on Secure Control frames
[3] 11-23-1914 Enhanced Security Considerations in UHR
[4] 11-23-1915 Enhanced Security for Control frame in 11bn
[5] 11-23-1933 security enhancement follow up
[6] 11-23-2001 Secure Control frames - Follow up
[7] 11-24-0151 Establishment of Security Key for Control Frame
[8] 11-24-497 security enhancement (control frame protection) follow up
[9] 11-24-547 Secure Control frames - Follow Up
[10] 11-24-1226 ICF-ICR design