## Slide 1: SP-based Non-Primary Channel Access
Date: 2024-02-17
Authors:

## Slide 2: Motivation
To meet throughput and latency requirements mentioned in the UHR PAR [1], non-primary channel access (NPCA) was proposed as a potential method
Existing Techs: Many contributions [2] focus on TXOP-based NPCA
  To switch to a non-primary channel when OBSS TXOP is detected on the primary channel
  To switch back to the primary channel when OBSS TXOP on the primary channel ends
Reality: OBSSs often use the same primary channel, if the operating channels overlap
  Heavy traffic is anticipated during TWT SPs => Primary channel becomes very busy during an OBSS TWT SP
  Frequent switching is anticipated during OBSS TWT SPs
    Wherein durations on the primary channel might be too shattered to be used
=> SP-based NPCA is introduced

## Slide 3: Recap: TXOP-based NPCA
With a wider operating channel width and a denser network deployment, channel efficiency is low when only the primary channel access is used
  With only primary channel access, a STA has to do backoff for transmission if the primary channel is busy, even when non-primary channels are idle.
With TXOP-based NPCA, when the primary channel is occupied by an OBSS TXOP, STAs switch to a non-primary channel to contend for the channel, using idle non-primary channels to access the medium, and switch back to the primary channel when the OBSS TXOP ends.
OBSS TXOP
BSS TXOP
Primary
channel
Non-primary
channel
Switch to a non-primary channel
Switch back to the primary channel

## Slide 4: Concept: SP-based NPCA
With SP-based NPCA, a BSS switches to a non-primary channel to access the medium during an OBSS TWT SP and switches back when SP ends, because
  It is anticipated that there would be heavy traffic during the TWT SPs
  OBSSs with staggered parking channels reduce collisions [3]
Non-primary channel | BSS parking |  | BSS parking | 
Primary channel | OBSS TWT SP | BSS parking | OBSS TWT SP | BSS parking
time
frequency
OBSS TWT SP
BSS parking
Primary
channel
Non-primary
channel

## Slide 5: Proposal
Negotiation Phase: AP and non-AP STAs negotiate parameters used in SP-based NPCA phase
  Parked non-primary channel, etc.
SP-based NPCA Phase: AP and non-AP STAs park on the non-primary channel during OBSS TWT SPs, and park on the primary channel outside OBSS TWT SPs
Primary
channel
Non-primary
channel
Negotiation
Negotiation Phase
AP announces OBSS TWT Info
SP-based NPCA Phase
OBSS TWT SP
BSS parks
OBSS TWT SP
BSS parks
…
Note: Not parked on the subchannel

## Slide 6: Detail 1. SP-based NPCA Phase
For each OBSS TWT Info detected by AP
  Step 1. AP announces an OBSS TWT Info
  Step 2. AP and non-AP STAs in a BSS, park on a non-primary channel instead of the primary channel only during OBSS TWT SPs
    AP and non-AP STAs in a BSS automatically switch to the non-primary channel when an SP starts and automatically switch back to the primary channel when an SP ends
AP announces OBSS TWT Info
Primary
channel
Non-primary
channel
BSS switches to a non-primary channel
Switches back to the primary channel
OBSS TWT SP
BSS parking
BSS parking
BSS parking

## Slide 7: Detail 1-1. AP’s Announcement of OBSS TWT
AP collects OBSS TWT Info via, e.g.,
  Listening to OBSS’s beacon, or
  Information exchange among multiple APs (Multi-AP co-operation)
OBSS TWT Info is announced/broadcasted by AP via, e.g.,
  Modified current TWT element, or
  Defined OBSS TWT element

## Slide 8: Discussion
Non-supporting UHR non-APs compatibility
  Option 1: the feature can be enabled only when there is no non-supporting UHR non-Aps
  Option 2: need additional rules to regularize behaviour for UHR STAs when not supporting the feature
Legacy compatibility
  Option 1 [Preferred]: the feature can be enabled only when there is no pre-UHR associated non-APs
    Simple on AP’s scheduling implementation
  Option 2: for particular pre-UHR features, e.g., trigger-enabled TWT, quite procedure, the proposed feature can be enabled only when all pre-UHR associated non-APs support those particular pre-UHR features

## Slide 9: Discussion (Cont.)
Location of NPCA operating channel
  Case 1: Bandwidth of MyBSS is larger than the Bandwidth of OBSS
    Option 1 [Preferred]: MyBSS uses secondary channels which do not overlap with the OBSS operating channel
    Option 2: MyBSS uses the whole operating channel but the NPCA (temporary) primary channel is a secondary channel which do not overlap with the OBSS operating channel
  Case 2: Bandwidth of MyBSS is less than or equal to the Bandwidth of OBSS
    Option 1 [Preferred]: MyBSS switches to a temporary operating channel outside of current operating channel, and the temporary operating channel does not overlap with the OBSS operating channel
    Option 2: MyBSS uses the current operating channel but the NPCA (temporary) primary channel is a secondary channel
  Preference is to minimize the impact (e.g., interference, bandwidth changing) on OBSS.

## Slide 10: Discussion (Case 1)
OBSS
BSS
Primary X MHz
Secondary X MHz
OBSS
BSS
Primary X MHz
Secondary X MHz
Option 1 [Preferred]
OBSS
BSS
Primary X MHz
Secondary X MHz
OBSS
BSS
Primary X MHz
Secondary X MHz
Option 2
NPC
NPC
PC
PC
PC
PC
During SP
During SP

## Slide 11: Discussion (Case 2)
OBSS
BSS
Primary X MHz
Secondary X MHz
OBSS
BSS
Primary X MHz
Secondary X MHz
Option 1 [Preferred]
OBSS
BSS
Primary X MHz
Secondary X MHz
OBSS
BSS
Primary X MHz
Secondary X MHz
Option 2
NPC
NPC
PC
PC
PC
PC
During SP
During SP

## Slide 12: Discussion (Cont.)
During “respected” r-TWT SP
  OBSS: following base line
  BSS: regular EDCA

## Slide 13: Discussion (Cont.)
Negotiation necessity between MyBSS and OBSS
  Option 1: MyBSS respects (switches to non-primary channel) without notice of OBSS
  Option 2 [Preferred]: Negotiation is needed to determine which OBSS TWT is to be respected and which is not
    OBSS sends a request to be “respected” during an OBSS r-TWT schedule and BSS responds
    Necessary r-TWT and SP-based NPCA related parameters are exchanged during negotiation
    BSS is allowed to reject

## Slide 14: Summary
The idea of SP-based NPCA is introduced: A BSS parks on a non-primary channel during OBSS TWT SPs
  AP and non-AP STAs in the BSS
    switch to the non-primary channel when an OBSS TWT SP starts, and
    switch back to the primary channel when the OBSS TWT SP ends

## Slide 15: Straw Poll
Do you support to include SP-based NPCA where a BSS parks on a non-primary channel during OBSS TWT SPs in 11bn SFD?
Do you agree that UHR APs may negotiate r-TWT schedule(s) that enable one AP and its associated STAs switch from the BSS operating channel to a different channel during the r-TWT schedule(s) of the other AP?

## Slide 16: References
[1] 11-23/0480r3, “UHR proposed PAR,” Laurent Cariou
[2] 11-23/2005r1, “Non-primary channel access (NPCA),” Minyoung Park
[3] 11-23/2022r1, “R-TWT for multi-AP (follow-up),” Laurent Cariou