## Slide 1: TX Power Randomization
Date: 2024-03-08
Authors:

## Slide 2: Abstract
Introduction to PHY Layer parameter randomization to increase CPE client privacy.

## Slide 3: Background
- CPE clients otaMAC rotation is being adopted (whether individual, group or mass rotation)
- MAC Header parameters encryption is being discussed
- Layer 1 parameters are not being addressed so far

## Slide 4: RSSI and otaMAC Rotation
- A simple capture on the air with a sniffer gives Radio Information for each frame. Among this information, there is an RSSI value at which the frame is received by the sniffing device.
- Rotating the otaMAC but maintaining the same Tx Power gives a non negligeable hint to an eavesdropper to connect the previous otaMAC to the next.
MAC1, -62 dBm
MAC1, -62 dBm
MAC8, -62 dBm
MAC2: -56 dBm, MAC3: -68 dBm,…
Then, MAC1 stops:
Most likely, MAC8=MAC1

## Slide 5: RSSI Relates to Tx Power
- If the STA changes its TxPower, the STA’s frames RSSI change at the AP, and for all observers.
- TxPower changing is already allowed in 802.11ax (BSS coloring):
- AP uses different mechanisms to influence in-BSS and OBSS STAs Tx power
e.g. by informing OBSS PD thresholds, leading the STAs to transmit low enough over OBSS that it would not disrupt the OBSS operations
e.g. by informing OBSS STAs on the PSR (AP’s tolerance to OBSS transmissions over UL scheduled transmissions)

## Slide 6: Proposal
CPE STA rotates otaMAC and adjusts its Tx Power at the same time to increase its anonymity
Possible methods:
  CPE STA operates independently
  CPE STA coordinates with the AP on the new Tx Power to be applied at the next rotation
    CPE STA and AP agree on Tx Power range not harming transmissions and the CPE STA variates it autonomously (‘a-la 802.11ax spirit’)
    Long-term algorithm to calculate a pseudo-random variation periodically (every few or at each epoch)
    When the CPE STA communicates next otaMAC, it also communicates next Tx Power.

## Slide 7: Other Considerations
Other PHY parameters could reduce the anonymity of a CPE STA and are worth considering:
  MCS index
  Number of spatial streams
  Bandwidth
  Assigned RUs set
A change of some of these parameters at each epoch are also beneficial to maintain anonymity.

## Slide 8: Straw Poll 1
Do you agree that PHY parameters of a CEP STA should also be protected at an epoch edge?
  Yes
  No
  Abstain

## Slide 9: Straw Poll 2
Should 802.11bi consider a CPE STA-AP coordination mechanism for variating Tx Power at an epoch edge?
  Yes
  No
  Abstain