## Slide 1: Future Light Communications Requirements
Date: 2024-03-15
Authors:

## Slide 2: Abstract
This presentation proposes the technical requirements for the development/enhancement of Light Communications to be market relevant for 2028 as a next step after 802.11bb.

## Slide 3: Current status
  802.11bb has been well received with significant interest in the standard from the market
  802.11bb is limited to 11n, 11ac and 11ax capabilities
  Future evolution of Light Communications is required to ensure market relevance

## Slide 4: Market requirements for future LC
  Customer discussions have provided feedback on key improvements required in the 2027+ timeline to include:
    Support of “the latest Wi-Fi standard”
    “Higher speed”
    “Additional wavelengths for operations”
    “Better MIMO”
  Each of these requirements can be defined as specific technical consequences

## Slide 5: Technical requirements for LC
  Evolution to use “the latest Wi-Fi standard”
    Next LC update should include support for 11be (ideally 11bn if possible?)
  “Higher speed”
    Greater electrical bandwidth for the opto-electrical front end (e.g., Light Antenna)
      Light Antennas can easily accommodate 320 MHz continuous bandwidth or higher
  “Additional wavelengths for operations”
    Current definition of 800-1000 nm is sufficient for a start
    New wavelengths should be included to allow greater optical power output (better range, data rates, etc.)
  “Better MIMO”
    Practical implementations of 11bb struggle to use more than 2 wavelengths in the 800-1000 nm range

## Slide 6: Proposed scope of work for LC
  Add integration with the 11be/bn PHYs
    Same goal as IMMW
    No changes in the MAC (same as 11bb)
    No impact on anything else for IMMW
  Add support for use of 1200 – 1550 nm spectrum
    The spectrum to be used is additive to the current spectrum requirement
  Update the LC MIMO (wavelength division multiplexing) clause for 11bb
    Better definition of the WDM spectrum utilization
    Confine the effective field-of-view to ensure interoperability

## Slide 7: Proposed path forward
Integrate LC as part of the IMMW TG
LC will introduce no additional requirements to the group beyond:
  Expand the scope of the PAR to include the light spectrum
  Augment the 11bb MIMO clause to include additional parts of the light spectrum and define the spectrums of relevance

## Slide 8: Straw poll
  Would you support including LC in the IMMW PAR?
    Yes
    No
    Abstain