## Slide 1: Balancing Wideband & Narrowband Frequency Hopping Channel Access Mechanisms for Operation in 6GHz
Date: 2024-03-13
Authors:

## Slide 2: Assumptions 1: Spectrum
Narrowband Frequency-Hopping system sharing the spectrum
  Represented by a Bluetooth system
  1 MHz channels with 0.5MHz guard band left & right
  3 advertisement channels, 233 data channels
Wideband system operating according to ETSI EN 303 687
  Represented by a Wi-Fi system
  3 ⨯ 160MHz channels (channel number 15, 47, 79) with primary 20MHz channels

## Slide 3: Assumptions 2: Scenario
Scenario B
Increase distance of Bluetooth to reduce received signal strength
  More susceptible to interference
  Modelling “body blockage” loss between central and peripheral device
Scenario A
Three separate Wi-Fi links on three 160MHz channels
  23dBm transmit power
  Energy detection threshold -72dBm/20MHz
(Up to) six Bluetooth links
  10dBm transmit power
  Energy detection threshold -85dBm/1MHz

## Slide 4: Assumption 3: Traffic & KPIs
Bluetooth
Constant bitrate traffic (CBR)
  1280B every 20ms (≙512kb/s)
  KPI: Packet delay
Connection interval 10ms
  Channel hopping frequency 10ms
Total channel activity ~57%
Wi-Fi
FTP 10MB file downloads
  Back-to-back
  Channel activity ~100%
  Access category BE
  KPI: File download duration
FTP 10MB file downloads with pauses
  Pause duration between downloads [50...150]ms
  Channel activity ~50%
  Access category BE
  KPI: File download duration

## Slide 5: Results (Wi-Fi: FTP / Bluetooth: CBR; solid = mean / dashed = 95-percentile)
Scenario A: Bluetooth operates undisturbed
Scenario B: Bluetooth is completely disturbed
Wi-Fi FTP download operation is completely disturbed by Bluetooth
Wi-Fi requires a Bluetooth coexistence mechanism
Introduce LBT before every connection event

## Slide 6: Results (introduce LBT for Bluetooth) (Wi-Fi: FTP / Bluetooth: CBR; solid = mean / dashed = 95-percentile)
Bluetooth does not get sufficient reliable access to the channel to deliver the data
Growth rate of queues is larger than successful delivery rate
Queues build up during the simulation & delay just keeps growing
Wi-Fi FTP download durations are close to performance without interference
Bluetooth needs to be more persistent
Introduce Secondary Channel Deferral (SCD) LBT before every connection event
No meaningful
packet delays.

## Slide 7: Secondary Channel Deferral (SCD) LBT
Basic idea:
  When initial LBT is busy, try to transmit on another channel as quickly as possible
Secondary hop performed independent of regular hopping scheme
  Receiver follows if no packet start is detected
Regular hopping pattern resumed at next connection event
Secondary hop frequency separation chosen to match Wi-Fi channel bandwidth (79 channels, ~160MHz)
LBT
SCD-LBT

## Slide 8: Results (Enhance LBT by Secondary Channel Deferral) (Wi-Fi: FTP / Bluetooth: CBR; solid = mean / dashed = 95-percentile)
Bluetooth operation is significantly improved for the Wi-Fi 50%-load
  Still significant chance for high delay
Wi-Fi’s 100%-load still blocks Bluetooth
Bluetooth links support each other
50%-load: Close to undisturbed
100%-load: Slightly disturbed
Promising approach
Mitigate impact to delay of Bluetooth in the presence of high Wi-Fi load

## Slide 9: High-Load Mitigation for Bluetooth: SCD-LBT with EDT Ramp-Up
Allow up to 5 deferrals, ending at EDT = -65dBm/MHz
  Bluetooth slowly raises EDT, becomes less sensitive & increases chance of observing an idle channel
Initial LBT done with -80dBm/MHz Energy Detection Threshold (EDT)
  Idle: Transmit
  Busy: Start Secondary Channel Deferral procedure
    Deferral channel is ~160MHz separated from original channel
    Increase EDT by 3dB

## Slide 10: Results (Enhance Bluetooth SCD-LBT with EDT Ramp-Up) (Wi-Fi: FTP / Bluetooth: CBR; solid = mean / dashed = 95-percentile)
Significant decrease of 95-percentile unless Bluetooth is heavily interfered
Bluetooth’s power backoff increases delays in 100%-load case, but only slightly in 50%-load case
Mitigate impact to delay of Bluetooth in the presence of high Wi-Fi load: Stepwise increase of Energy Detection Threshold in case of blocked channel

## Slide 11: Assumption 3b: Traffic & KPIs
Bluetooth
Constant bitrate traffic (CBR)
  1280B every 20ms (≙512kb/s)
  KPI: Packet delay
Connection interval 10ms
  Channel hopping frequency 10ms
Total channel activity ~57%
Wi-Fi
Cloud Gaming
  30Mb/s downlink video & uplink control
  Channel activity ~15%
  Access category VI & VO
  KPI: gaming delay

## Slide 12: Results (Bluetooth with LBT + SCD + ED Ramp-Up) (Wi-Fi: Cloud Gaming / Bluetooth: CBR; solid = mean / dashed = 95-percentile)
Bluetooth delay close to performance without interference due to low Wi-Fi channel occupancy
SCD / ED Ramp-Up barely active
Cloud gaming traffic delay: Significant increase by Bluetooth interference
Decrease Wi-Fi delay in the presence of narrowband interference

## Slide 13: Wi-Fi Channel Access Procedure & Delay
Wi-Fi uses “Option 2” according to EN 303 687 for channel bonding:
  Initially, channel access only listens on the “primary” 20MHz channel
  Count down backoff while the channel remains idle
  25µs before the transmission energy detection is performed on the full channel
  Data transmission starts if primary 20MHz channel & full bonded channel remains idle
t
f [MHz]
160
primary 20MHz channel
Data
Ack

## Slide 14: Order of Events on the Channel
Wi-Fi before Bluetooth
Clear Channel Assessment (CCA) result is idle on all 20 MHz subchannels
Wi-Fi transmission starts
Bluetooth hops on channel, LBT detects transmission and defers
  Mitigation by secondary channel deferral
No delay increase
Bluetooth before Wi-Fi
Bluetooth hops on channel, LBT detects an idle channel
Bluetooth transmission starts
Wi-Fi CCA detects Bluetooth transmission and defers
  Bluetooth is on primary channel: anytime during backoff
  Bluetooth is on secondary channel: during the last 25 µs of the backoff
Wi-Fi continues to observe until the channel is idle and re-starts backoff
Increase of channel access delay
t
f [MHz]
160
t
f [MHz]
160
p20
Data
Ack
Bluetooth LBT fails
p20
Wi-Fi backoff on secondary channel fails
Data

## Slide 15: Wi-Fi Bandwidth Adaptation
Dynamic Backoff Bandwidth
Fully Dynamic Puncturing
Puncturing allows 20 MHz-sized “holes” in the spectrum
Primary 20 MHz must be idle
Fully dynamic in
  Time: Puncturing is instantaneously, backoff simply continues
  Frequency: Puncture arbitrary 20 MHz-channel holes
This corresponds to “Option 1” in EN 303 687
Dynamic Backoff allows adapting the channel bandwidth during countdown
Primary 20MHz must be idle
Only available bandwidths are 80MHz, 40MHz, and 20MHz

## Slide 16: Results (Enhance Wi-Fi by Bandwidth Adaptation) (Wi-Fi: Cloud Gaming / Bluetooth: CBR; solid = mean / dashed = 95-percentile)
No significant change for Bluetooth links
Flexible Puncturing gives the best delay
Significant simpler dynamic backoff bandwidth is not much worse
Wi-Fi is able to adapt to narrowband interference
Can we do better?

## Slide 17: Results (Bluetooth avoids Wi-Fi’s primary-20 channels) (Wi-Fi: Cloud Gaming / Bluetooth: CBR; solid = mean / dashed = 95-percentile)
No significant change for Bluetooth links
Flexible Puncturing reaches optimum gaming delay
Always idle primary 20MHz channel combined with Dynamic Backoff still provides significant delay improvements
Decrease Wi-Fi delay in the presence of narrowband interference: Dynamic channel bandwidth + guaranteed idle primary-20 channels

## Slide 18: Conclusions
Further Thoughts:
  Narrowband may detect spectrum occupied and avoid channels
    Separation in frequency should give best results if feasible
    Learning might be supported by external information, agreements, LBT results
    Has its own challenges, known from Adaptive Frequency Hopping in 2.4GHz
  Define a ”simpler” mode of operation, governed by restrictions
    Inspired by Short Control Signalling, but adapted for narrowband frequency hopping
Dynamic sharing of 480MHz frequency spectrum between wideband and narrowband frequency-hopping systems is feasible
Coexistence & performance of both systems can be achieved by
  (Short) LBT in narrowband
  plus
  Mitigation of channel access delay in narrowband by
    Quickly trying a different channel and
    Ramp-up of the energy detection threshold in case of retries
    plus
  Mitigation of channel access delay in wideband by
    Dynamic bandwidth adaptation or
    Puncturing
    (plus
  Leaving the primary 20 MHz idle for wideband.)

## Slide 19: Annex: Cloud Gaming Traffic Model & KPI
Slide 19

## Slide 20
KPI:
(Mean & 95-percentile) Gaming Delay
Cloud Gaming Traffic Model & KPI
Uplink: Control Messages over UDP
  Mean size 468 B with 90 B standard deviation
  Mean inter-frame interval 15 ms with 6 ms standard deviation
  Access category voice
  Measure frame delivery delay
Downlink: XR Video Model over RTP
  Mean load 30 Mb/s with 10 Mb/s standard deviation
  60 frames/s, every 120th frame is an I-frame (2⨯size)
  Access category video
  Measure frame delivery delay

## Slide 21: Single Simulation
Single simulation results in CDFs for the downlink video packet delay & uplink control packet delay

## Slide 22: 99-percentiles of 100 simulations
DL Video 99-percentiles
UL Control 99-percentiles
Run 100 simulations
  100 CDFs
  100 UL Control 99-percentiles
  100 DL Video 99-percentiles
Define ”gaming delay”: sum of UL & DL 99-percentiles
  100 gaming delays
KPI: Mean / 95-percentile of gaming delay
Sebastian Max, Ericsson
Mar 2024