## Slide 1: ARC Closing Report
Date: 2024-03-14
Authors:

## Slide 2: Abstract
This document is the closing report for ARC SC,
March 2024 Session

## Slide 3: Work Completed - 1
Agenda is here: 11-24/0263r4
IEEE Std 802 revision:
  Completed comment resolution of WG LB (802.1 “hosting”).
  The last significant open issue is what to do to better describe EPD/LPD. In P802REVc meeting, continued/finished review of a proposal for replacement text, which will remove the EPD and LPD terminology, and instead refer to/describe how the LLC does protocol discrimination with a protocol identifier (EtherType, LSAP addresses/SNAP, etc.) and how it formats the protocol identifier in LPDUs (2 styles). Made some edits from suggestions for improvement of the draft.
  Will recirc out of March, and likely again from an April telecon. Expect to start SA ballot out of May.

## Slide 4: Work Completed - 2
Considered follow-on architecture work, from the IEEE Std 802 results, and discussed 802.11be architecture fit
Annex G:
  Agreed we could probably use 3 Annexes, all informative, on:
    Frame Exchange and Frame Exchange Sequence explanation
    Overview/introduction/index to specific frame usage/order, with references into the body text subclauses
    Discussion of how “real-world” implementation designs relate/map to the architecture in 802.11
WBA E2E QoS presentation
  Deferred to May.

## Slide 5: Monitoring/future activities
    Other items being tracked (but not actively worked unless/until contributions):
    Related to IEEE Std 802 updates (slide 20):
      802.1AC mapping from ISS to 802.11 MAC SAP interface
      Consider any changes to remove 802.2/LLC terms?
      802.11’s “Portal”, and mapping to/usage of IEEE Std 802 terminology
      Access Domains: “802 Access Domains”? In 802.11, an ESS? TGbe implications?
      Is the DS a bridge (small ‘b’)?
      Clarify EPD/LPD within 802.11: 11-20/0174r0
        Follow the lead from 802REVc?
    MLME-RESET, versus MLME-JOIN, MLME-START, MLME-SCAN and MLME-END
      One aspect is how MAC address is set/controlled – related to IEEE 1609/TGbd activities

## Slide 6: Plans
Ongoing work:
Monitor results of IEEE P802REVc recirculation ballot(s)
Annex G replacement phase 2, continued
WBA E2E QoS coordination, continued
Monitoring/future activities, or other relevant topics, if any contributions
Teleconferences – None expected. If needed, will schedule with 10-days notice.
Two meeting slots requested in May