## Slide 1: Coex SC Closing Report
Date: 2024-05-16
Authors:

## Slide 2: Abstract
Closing report for IEEE 802.11 Coex SC (Coexistence Standing Committee) for May 2024.

## Slide 3: Coex SC’s week at a glance
Met three times
Two Coex SC (only) slots
One Joint session with 15.4.ab

## Slide 4: ETSI BRAN Update to 802.11 (1/2)
EN 303 687 (Wireless Access System/Radio Local Area Network (WAS/RLAN) in the license-exempt 6 GHz band)
Version 1.1.1 published by ETSI and reviewed by European Commission (EC)
EC criticizes normative reference to IEEE 802.11ax-2021 because EC does not recognize IEEE as SDO
Reference need for the definition of one signal used to conduct an Energy Detection Threshold (EDT) level related test
ETSI TC BRAN developed response to EC
Waiting for feedback by regarding the use of IEEE 802.11ax-2021 as normative reference

## Slide 5: ETST BRAN Update to 802.11 (2/2)
EN 301 893 (Wireless Access System/Radio Local Area Network (WAS/RLAN) in the license-exempt 5 GHz band)
First national vote (Standardisation Request deliverables Approval Process, SRdAP) completed (note: SRdAP replacing ENAP)
All SRdAP comments resolved
Since draft uses IEEE 802.11-2020 as normative reference, TC BRAN expects similar issues with the EC.

## Slide 6: Update from Bluetooth SIG Work
Recent actions
Participating in and contributing to the ETSI BRAN
 Proposed channel access scheme to ETSI BRAN (BRAN(24)123a003)
Next steps
Exploring enhanced sharing mechanisms for the 5725 – 5850 MHz band

## Slide 7: Technical Submissions & Discussion Items (1/2)
NB Status Update (11-24/907r0)
Summary of current activities, including discussion between .11 and .15.4ab
Review of channel access proposal introduced by BT SIG to ETSI BRAN (BRAN(24)123a003)
Impact of non-listing of EN 303 687 in the OJEU (11-24/922r0)
IEEE staff and LMSC Chair attended to provide feedback
IEEE open to evaluate request to grant copyright for citing / copying relevant parts of the standard

## Slide 8: Technical Submissions & Discussion Items (2/2)
Joint Session Coex SC with 802.15.4ab
Continued discussion on CCA modes
CCA Modes in 802.15.4 (11-24/360r3)
Response to CoexSC 11-24 360r3 (15-24/212r5)
Addition information item
FCC Filing for for PNT and 5G in 900 MHz (15-24/280r0)

## Slide 9: Plans for July
Coex slots:
One joint 802.11 Coex SC – 802.15.4ab – Tuesday EVE
Two dot11 Coex (only) slot (one before and one after the joint session with .15.4ab)
Joint dot11 dot15.4ab slot:
Continue discussion on channel access schemes
Coex (only):
Update on ETSI BRAN
Update on Bluetooth SIG
Technical submissions (tba)
Note: coexistence-related topics are welcome. Please contact the Chair

## Slide 10: Telcos
No telco scheduled.

## Slide 11: References for this week
Agenda for this week: 11-24/0620
Snapshot Slide: 11-24/0621
Meeting / Chair’s Slide Deck: 11-24/0622
Closing report: 11-24/0623
Meeting minutes: 11-24/0932

## Slide 12: Coex Submissions
Bluetooth SG update | 11-24/717
ETSI TC BRAN update | 11-24/910
Impact of non-listing of EN 303 687 in the OJEU | 11-24/922
NB Status Update | 11-24/907
FCC Filing for for PNT and 5G in 900 MHz | 15-24/0280r0
CCA Modes in 802.15.4 | 11-24/0360r4
Bluetooth channel access proposal | BRAN(24)123a003
Response to CoexSC | 15-24/212r5