## Slide 1: UL Low Latency Traffic Indication
Date: 2024-04-15
Authors:

## Slide 2
Abstract
In this contribution we share some thoughts on the necessity for UL low latency traffic indication as well as how to provide low latency traffic indication.

## Slide 3: Introduction
802.11bn targets to support stringent latency requirements for a variety of traffic [1]
  Augmented, virtual and mixed reality
  Robotics
  Industrial automation
A number of features have been proposed related to low latency traffic, including
  Preemption
  Defer Signals/4us signals
  Deterministic backoff
  Coordination and protection of rTWT
Some proposed features are distributed, however, it is beneficial for the AP to know which STAs currently have UL low latency traffic
  Better utilization of UL MU transmissions for higher spectrum and medium efficiency
  Better management of low latency SP such as rTWT
It is desirable to have an efficient UL low latency traffic indication

## Slide 4: UL Low Latency Traffic Indication
  Mechanisms to indicate UL low latency traffic need to satisfy a number of requirements
    Can provide/obtain information on/from a reasonable number of STAs within a short period of time
    Have low overhead
    Provide sufficient information
  NDP Feedback Report (NFR) defined in 802.11ax is a good candidate for this purpose
    Each 20 MHz wide channel can support the reporting of 18 STAs using OFDMA alone, hence enabling concurrent reporting by a reasonable number of STAs
    NDP does not have MAC frame body and is efficient
    However, NFR only reports 1 bit of data
      Currently just report whether buffered traffic exceeds a threshold

## Slide 5: Improvements needed for the NFR design (1)
  Traffic priority information needs to be added
    Currently NFR only provides feedback about PS mode and whether buffered traffic exceeds a threshold
    In order to enable low latency traffic indication, at least, low latency traffic information is specifically needed
  Can also consider adding latency related information for low latency traffic

## Slide 6: Improvements needed for the NFR design (2)
  Three options may be available to add traffic priority information to the NFR mechanism
    Option 1: Traffic priority information may be added to the NDP Feedback Report Poll (NFRP) frame
      Use one or more reserved bits to indicate that only feedback is solicited for low latency traffic
    Option 2: Add more bits to the NFR NDP PPDU
      Expand the number of HE-LTFs to provide a more detailed breakdown for buffered traffic
        E.g., one bit information on traffic of priority Low Latency, VO+VI, BE+BK, etc.
      Needs to consider added overhead; trade-off between efficiency and detailed information
    Option 1 & Option 2

## Slide 7: Improvements needed for the NFR design (3)
  In addition, currently STAs are scheduled to respond with NFR by a range of AIDs indicated in NFRP
    Indication of Starting AID for a total number of Nsta
    Nsta is based on bandwidth and multiplexing
  If the AIDs of STAs with low latency traffic are far apart, this may reduce the efficiency of the NFR procedure
    AP may need to do multiple rounds of NFRP to obtain the low latency needs in its BSS

## Slide 8: Improvements needed for the NFR design (4)
  Two options could improve the NFR mechanism efficiency for UL low latency traffic indication
    Option 1: assign AIDs of STAs with low latency traffic close to each other, or within a specific range
      May have more implication due to MLD AID assignment rules
    Option 2: Modify NFRP frame format to enable individual STA polling

## Slide 9: Conclusions
It is desirable to have an efficient UL low latency traffic indication mechanism for 802.11bn
  Better utilization of UL MU transmissions for higher spectrum and medium efficiency
  Better management of low latency SP such as rTWT
The NDP Feedback Report (NFR) mechanism defined in 802.11ax is a good candidate for this purpose
  Allow the concurrent reporting of a reasonable number of STAs
  NDP frame format is very efficient
Improvements to the NFR mechanisms are needed to make it suitable for UL low latency traffic indication in 802.11bn
  Traffic priority information need to be added
  Modification is needed to enable highly efficient polling in case AIDs are not assigned close to each other to STAs with low latency traffic
Discussed a number of options of improvement for the NFR design

## Slide 10
References
[1] 11-23/480r3, UHR Proposed PAR, Laurent Cariou

## Slide 11: SP #1
Do you agree that the NDP Feedback Report mechanism should be considered for UL low latency traffic indication in 802.11bn?
Y/N/Abs: