## Slide 1: Optimizing Roaming Scan
Date: 2024-11-06
Authors:

## Slide 2: Introduction
Before seamless roaming procedure is initiated, the non-AP MLD needs to discover neighboring AP MLDs for roaming candidate selection
In this presentation, we define enhancements to optimize overall roaming scan and discovery procedure for discovering neighboring AP MLDs for seamless roaming

## Slide 3: SMD Association and Seamless Roaming Flow
Before SMD association, non-AP MLD performs baseline active/passive scan to discover AP MLDs (e.g. using 11be ML probe). It then performs auth+assoc procedure with the SMD through an AP MLD.
Post SMD association, a non-AP MLD needs to discover one or more neighboring AP MLDs and then select candidate target AP MLDs for seamless roaming.
Neighbor discovery + candidate selection can involve:
  Non-AP MLD initiated neighbor discovery and/or unsolicited neighbor info push by serving AP MLD.
  Non-AP MLD selecting one or more candidate target AP MLDs for roaming, serving AP MLD can provide recommendation for specific roaming candidates.
  Non-AP MLD may fetch detailed info about selected candidate AP MLDs through serving AP.
Then roaming preparation and roaming execution steps are performed

## Slide 4: Problem Statement
For seamless roaming, a non-AP MLD needs to first discover info for neighboring AP MLDs
Below, we summarize some existing ways for a non-AP MLD to discover candidate neighboring AP MLDs, but each have some limitations:
  Roaming scan: Passive (listen for beacons) or active (Probe Request/Response) scan by the client, however scan is time consuming (and drains power) and is disruptive to ongoing transmissions
  11k Neighbor Report: Client can send a 11k Neighbor Report Request & receive a Neighbor Report Response, however these frames have not been enhanced for MLD in 11be
  BTM: Client can send a BTM Query to request BSS transition candidates in BTM Request
    BTM Request has been enhanced for MLD in 11be and is more widely supported. However, BTM Request does not provide all the elements as provided in Probe Response.
  RNR: Client can discover neighboring APs in RNR (from Beacon) and then fetch detailed information for selected APs using targeted roaming scan, but this also requires client to perform off-channel roaming scan
We need ways to discover information about neighboring AP MLDs through serving AP MLD to minimize off-channel scan and discovery overhead
Here we propose enhancements to optimize roaming scan and discovery for seamless roaming

## Slide 5: Neighbor Discovery for Seamless Roaming
Neighbor discovery for seamless roaming through serving AP can include:
  Client discovering some basic information for several neighboring AP MLDs
  Client then down selects to one or few neighboring AP MLDs as seamless roaming candidate and discovers full set of information for those neighboring AP MLDs
RNR can provide some basic set of information for neighboring APs
  RNR can provide info for collocated & non-collocated APs - RNR in beacon may or may not provide non-collocated APs to address any beacon bloating concerns (see next slide for extensions to RNR)
Step 1 can be accomplished by:
  Extending BTM Query to request for RNR and/or selected elements (e.g. BSS Load, RSNE) in Neighbor Report elements in the BTM Request. Provide limited info for Neighbor AP MLDs to minimize discovery overhead.
Step 2 can be accomplished by:
  Client performing neighbor Probe Request/Response to retrieve detailed/full set of information for few selected neighboring AP MLDs, through the current AP
Client implementations may choose to perform step 1 or step 2 or both for neighbor discovery.

## Slide 6: Extend RNR for Seamless Roaming
Add SMD parameters
  Indicate ‘Same SMD’ flag in BSS parameters
  SMD parameters specify SMD Identifier - only included if different SMD
Add some extended BSS parameters (2/3 octets?) (to assist in AP selection):
  BSS Operating BW
  PHY Type
  Max Nss Supported
  Max MCS Supported
  IP Address Continuity Support
  Capabilities?
    Signal few TBD selected capabilities, that can be useful in candidate selection
To avoid Beacon bloating concerns, Extended BSS parameters may not be included in RNR in Beacon, but included in other places where RNR can be provided (BTM Request, Probe Response)

## Slide 7: Extend BTM Query and BTM Request (1)
BTM Query: Add Request element and Extended Request element, to allow requesting for RNR and other specific elements to be sent in BTM Request.
  Define new BSS Transition Query Reason values to signal ‘Neighbor Discovery’ or ‘Neighbor Discovery within SMD’
BTM Request: Enhance to provide RNR element + security related elements (RSNE, RSNXE) in Optional Subelements of the NR element
  Serving AP returns set of Neighboring APs per Query Reason (e.g. only APs in the SMD vs all APs)
  Serving AP can return additional APs if needed
  Propose to apply inheritance across NR elements for reducing size, e.g. if all reported APs have same RSNE, RSNXE then include these only once

## Slide 8: Extend BTM Query and BTM Request (2)
Unsolicited BTM Request by Serving AP:
  Today an AP can send unsolicited BTM Request to recommend BSS transition to specific AP MLDs (e.g. for load balancing purpose)
  For seamless roaming, enable serving AP to provide neighbor APs info w/o specifically asking to perform BSS transition (e.g. to provide set of APs to consider for seamless roaming)
  Propose to add a Reason Code to BTM Request to signal a reason for BTM Request (e.g. ‘Neighbor Info Push’).
    Presence of Reason Code signaled in Request Mode
    Note: BTM Query includes a ‘Query Reason’ today, it makes sense to enhance BTM Request also to provide a reason for the purpose of BTM Request
  When Serving AP is recommending specific candidates to perform seamless roaming, then it uses a different Reason code (e.g. ‘Recommend to Perform Seamless Roaming’)

## Slide 9: Neighbor Probe Req/Resp through Serving AP (1)
A client may need to fetch detailed/complete set of info (as obtained in Probe Resp) to perform seamless roaming to a candidate target AP MLD
Proposal: Define Neighbor Probe Request/Response as extension to 11be ML probe request/resp to probe for detailed info for one or more neighboring AP MLDs through serving AP MLD
  Extend Probe Req ML element to signal probing for a neighboring AP (aka neighbor Probe Req ML element)
  A Probe Request frame that includes neighbor Probe Req ML element(s) is a Neighbor Probe Request
  A Neighbor Probe Request can include (Extended) Request element(s) to indicate specific elements being requested for neighboring AP MLDs (similar to ML probe in 11be)
  Neighbor Probe Request can include one or more neighbor Probe Req ML elements, one for each neighbor AP MLD being probed
  A Neighbor Probe Response is a Probe Response frame that includes one or more Basic ML element that carries complete or partial profile(s) for neighboring AP MLDs
Neighbor Probe Request/Response frames are exchanged as PMF protected with serving AP MLD

## Slide 10: Neighbor Probe Req/Resp through Current AP (2)
After receiving a Neighbor Probe Request, serving AP MLD can use any of the following methods to generate a response
  Fetch neighbor information directly from each of the requested neighboring AP MLDs over-the-DS, or
  Fetch neighbor information for requested neighboring AP MLDs from a controller/WLC, or
  Use recent cached info for requested neighboring AP MLDs
Serving AP MLD will return a Neighbor Probe Response that provides information in one or more Basic ML element(s) for neighboring AP MLDs
  Multiple neighbor Probe Responses can also be returned, one for each neighbor AP MLD, each providing information in one Basic ML element

## Slide 11: Neighbor Probe Request
Neighbor Probe Request
  A Probe Request frame that includes one or more neighbor Probe Request ML elements(s)
    Address 1 and Address 3 are set to BSSID of an affiliated AP of the serving AP MLD
  Indicate in Presence Bitmap a ‘Neighbor AP Probe Indication’ to signal probing for neighbor AP MLD. AP MLD ID indicates identifier for the neighbor AP MLD.
  Apply inheritance across STA Profiles within and across different neighbor Probe Request ML elements.
    If same Request element and Extended Request element values are applicable for all Neighboring APs, then include these only once (same as in 11be ML probe)

## Slide 12: Neighbor Probe Response
Neighbor Probe Response
  A Probe Response frame that Includes one or more Basic ML element for neighbor AP MLDs
  MLD MAC Address is set to the Neighbor AP MLD MAC Address. Per-STA Profiles provides affiliated APs information of neighbor AP MLD.
  Apply inheritance across STA Profiles within and across different Basic ML elements
    Elements included in the first Per-STA Profile of first Basic ML element can also apply to other Per-STA Profiles in the same and other Basic ML elements included in response frame.
    Use Non-Inheritance element when inheritance should not apply

## Slide 13: Conclusion
Roaming scan is expensive, causes disruption and adds delay to roaming.
For seamless roaming it is desired to define enhancements to optimize roaming scan and minimize discovery overhead
We propose following enhancements to optimize roaming scan through serving AP MLD:
  Extend RNR with SMD parameters + some extended BSS parameters (to assist in candidate selection)
  Extend BTM Query to request for RNR and/or selected elements (e.g. BSS Load, RSNE) in NR elements in the BTM Request (to learn basic information for neighboring APs)
  Define Neighbor Probe Request/Response as extension of 11be ML probe, to enable a non-AP MLD to fetch detailed/full set of information for neighboring AP MLDs through the serving AP MLD
These enhancements aim to reuse and extend existing mechanisms (RNR, BTM Query/BTM Request, 11be ML probe req/resp)
These enhancements minimize disruptions due to roaming scan and discovery, since all exchanges are performed with serving AP MLD

## Slide 14: Straw Poll 1
Do you agree that 11bn uses the BTM Query and BTM Request for a non-AP MLD to query and discover necessary information about the neighboring AP MLDs of the serving AP MLD, to assist in selection of candidate target AP MLD(s) for seamless roaming?
Neighboring AP MLDs may belong to the same SMD (as the serving AP MLD) or may belong to a different SMD
Serving AP MLD can use the BTM Request mechanism to provide information about the neighboring AP MLDs in an unsolicited manner

## Slide 15: Straw Poll 2
Do you agree that 11bn defines a mechanism for a non-AP MLD to discover probe response information for neighboring AP MLDs of the serving AP MLD, through the serving AP MLD?
Neighboring AP MLDs may belong to the same SMD (as the serving AP MLD) or may belong to a different SMD

## Slide 16: Straw Poll 3
Do you agree to enhance RNR element to provide a ‘Same SMD’ indication for a reported neighboring AP, to signal whether the reported neighboring AP is part of the same SMD as the reporting AP?