## Slide 1: Peer-to-Peer TWT for Handling Coex and P2P
Date: 07-01-2024
Authors:

## Slide 2: Abstract
In this contribution, we provide some of the potential enhancements to 802.11 to better support periodic/deterministic in-device coexistence for WLAN devices.

## Slide 3: Introduction
Coex/P2P events for a STA can be scheduled or planned ahead of time.
  In such cases, the coex events can occur in a periodic manner with known periodicity parameters such as coex/P2P start time, duration, and interval.
During the coex/P2P events, the STA maybe unavailable for communication with some other STAs.
  For instance, during the coex/P2P window, a non-AP STA may not be available for infrastructure operation with the AP

## Slide 4: Peer-to-Peer TWT
Peer-to-peer TWT was introduced in the baseline to indicate to the AP the periodic unavailability of the STA due to coex/P2P communication.
The baseline channel usage procedure was extended to facilitate peer-to-peer TWT.
  The non-AP STA sends a Channel Usage Request frame and includes a TWT element to request to set up a peer-to-peer TWT schedule with the AP
Once, a peer-to-peer TWT schedule is set up with the non-AP STA, the AP does not send any downlink frame to the non-AP STA and does not solicit uplink frame from the non-AP STA.

## Slide 5: Need for Enhancements(1)
For TWT operation--due to the lack of granularity in the TWT interval units, once the TWT has been setup, over time, it is expected that there would be a mismatch between traffic arrival time and the TWT SP start time. The divergence would increase as time progresses.
Also, if the STA has a P2P link, the AP clock and the P2P group’s clock may get unsynchronized over time, we may need to re-align the TWT SP start time.
For Peer-to-peer TWT to handle coex events, there needs to be a mechanism to update/revise the peer-to-peer TWT SP start time so that it is aligned with the coex/P2P start time.

## Slide 6: Flexible Peer-to-peer TWT
We need a mechanism to flexibly change the subsequent peer-to-peer TWT SP start time
The change in the start time should compensate in difference in actual coex event start time and unavailability schedule previously set up with the AP.

## Slide 7: Flexible Peer-to-peer TWT: Example

## Slide 8: TWT Information Frame Usage
TWT Information frame can be used to suspend or resume peer-to-peer TWT SPs or unavailability SPs.
Currently supports—
  Unavailability SP suspension/resumption
Can be extended to support flexible peer-to-peer TWT—
  Indication of arbitrary start time for Next SP
  Indication of the k-th SP from which the new/modified start time would take into effect.
    May also indicate in changes in other parameters: SP duration and interval

## Slide 9: Need for Enhancements (2)
Unavailability information can be coupled with channel recommendation. This can be useful for P2P operation.
Using gratuitous channel usage procedure, an AP can suggest a set of channel for P2P.
  But timing info is not factored in.
STA indicating unavailability pattern and AP provides the most suitable channels
  The non-AP STA can indicate the coex/P2P unavailability schedule or peer-to-peer TWT schedule
  The AP may recommend/suggest the best off-channel or a set of preferred off-channels that best suited for such P2P schedule
  Example: The STA may have already decided the P2P group operation schedule/cadence, and now want to know the best channel to establish the P2P cadence.
  Serves dual purpose: unavailability indication for AP + finding best channels for P2P
  Can reuse/extension of existing tools: (Peer-to-peer TWT + Channel Usage element) in the Channel Usage Req/Resp.

## Slide 10: Summary
Peer-to-peer TWT is important for handling coex events
For effective unavailability indication using peer-to-peer TWT, it would be essential to devise a mechanism to update the start time of the subsequent SPs in a sequence of peer-to-peer TWT SPs.
For effective handling of P2P related coex, unavailability timing information can be coupled with the recommendation for preferred channels.

## Slide 11: References
[1] Liwen Chu, et.al., IEEE 802.11-23/1934r0, “In-device interference mitigation follow up”.
[2] Alfred Asterjadhi, et.al., IEEE 802.11-23/1964r0, “Coexistence Protocols for UHR”.
[3] Laurent Cariou, et.al., IEEE 802.11-23/2002r1, “In-device coexistence and interference follow – up”.
[4] Brian Hart, et.al., IEEE 802.11-23/2026r0, “Balanced In-Device Coexistence”.
[5] Rubayet Shafin, et.al., IEEE 802.11-24/509r1, “Thoughts on in-device coexistence and P2P for 11bn”