## Slide 1: Further considerations on coordinated TWT
Date: 01-18-2024
Authors:

## Slide 2: Abstract
  Multi-AP (MAP) Coordination is one of the key features considered for UHR SG and IEEE 802.11bn.
    TWT-based multi-AP coordination is considered one of the candidate technologies for UHR[1-9].
    Different modes of TWT coordination were discussed.
    In this contribution, we follow up specifically on the R-TWT version of the TWT-based MAP coordination.

## Slide 3: Coordinated R-TWT (C-R-TWT)
  In the end-to-end C-R-TWT operation, some phases can be part of the generalized MAP framework, while others would be R-TWT-specific procedures.
  For the generalized segments (Discovery and Param neogitation), all the MAP coordination techniques can use the same vehicle/ information container.

## Slide 4: MAP Discovery for C-R-TWT
  Discovery for C-RTWT:
    In this phase, the C-R-TWT initiating AP advertises/announces its intent for R-TWT-based MAP coordination to other APs.
      Basic C-R-TWT-related capabilities and other coordination information can be included in the advertisement
      Schedule information can optionally be shared during the discovery phase.
    An AP that receives the C-R-TWT announcement from the initiating AP and is willing to participate in the C-R-TWT coordination should respond to the announcement.
      The responder AP should include its C-R-TWT capability information in its response.
    Capability information may include support for different modes of C-R-TWT

## Slide 5: MAP Negotiation for C-R-TWT
  Negotiation for C-RTWT:
    In this phase, the C-R-TWT initiating AP gets into explicit parameter negotiation with an AP that responded to the initiating AP’s C-R-TWT advertisement.
      1-to-1 Request-response based approach
      Responding AP also suggest alternative param set it can support
      The responding AP can also be referred to as a coordinated AP.
    Negotiating parameters (minimum set):
      Schedule timing information: TWT, wake duration, and interval mantissa and exponent
      Schedule persistence
      Mode of C-R-TWT (see slide 7)
      Schedule identifier (can be different than B-TWT ID used for intra-BSS operation)
    Can either repurpose the existing TWT element or come up with a new container

## Slide 6: Example frame exchange for Disc. and Negotiation
  For C-R-TWT
    The MAP Announcement and MAP Preparedness frame can include an indication of R-TWT-based coordination and the corresponding capability information.
    The MAP Request and Response frames may include exact C-R-TWT negotiation parameters.

## Slide 7: Modes of C-R-TWT
  When a C-R-TWT initiating AP negotiates with a coordinated AP for a C-R-TWT schedule, based on the protection level expected from the coordinated AP, modes of the C-R-TWT schedule can be determined.
  Mode-1: Only AP ending TXOP
    In this mode, only the coordinated AP ends its TXOP before the C-R-TWT SP starts. The associated STAs in coordinated AP’s BSS do not need to end their TXOP.
  Mode-2: Both the AP and STAs ending TXOP
    In this mode, both the coordinated AP and its associated STAs end their TXOP before the C-R-TWT SP starts.
  Mode-3: QoS-aware TXOP ending
    In this mode, the coordinated AP or its associated STAs end their TXOPs before the C-R-TWT SP starts if certain QoS requirements are not violated; otherwise, the TXOPs are not ended.
      For example, a STA in the coordinated AP’s BSS may end its TXOP only if the C-R-TWT SP does not overlap with any of its own high-priority QoS delivery windows.

## Slide 8: Intra-BSS C-R-TWT Announcement (1)
  This step is from the baseline. Some enhancements are needed.
  Announcement by C-R-TWT initiating AP:
    For the C-R-TWT initiating AP, the intra-BSS announcement procedure for the C-R-TWT initiating AP can be the same as the baseline R-TWT announcement procedure.
      The C-R-TWT initiating AP advertises the schedule in its BSS as a regular R-TWT
      The STAs associated with the initiating AP can be agnostic of whether the advertised R-TWT schedule is coordinated or not.
  Announcement by the C-R-TWT coordinated AP:
    For the C-R-TWT coordinated AP, the intra-BSS announcement procedure requires some enhancement.
      If needed, the C-R-TWT coordinated AP, in its schedule announcement, should be able to make a distinction between an R-TWT schedule originating in its BSS and a schedule originating in the C-R-TWT initiating AP’s BSS.

## Slide 9: Intra-BSS C-R-TWT Announcement (2)
  OBSS Schedule vs QoS Prioritization
    When a coordinated AP announces an R-TWT schedule in its BSS, making a distinction between an R-TWT schedule of its own and a schedule that is being coordinated on may be necessary at some times.
      This would allow some control on the prioritization of other factors over the C-R-TWT SP.
    Some kind of marker needs to be placed schedule container making such distinction.
      Accordingly, the coordinated AP can dictate the behavior of its associated STAs on how to treat the two types of schedules.
      For instance, if the C-R-TWT coordinated AP has negotiated a mode-3 type of C-R-TWT schedule with the initiating AP, then the coordinated AP can dictate QoS-aware OBSS schedule prioritization rules for its own BSS. [see next slide]

## Slide 10: Intra-BSS R-TWT Negotiation (1)
  This step is also from the baseline. Some enhancements are needed.
  Negotiation by C-R-TWT initiating AP:
    For the C-R-TWT initiating AP, the intra-BSS negotiation procedure for the C-R-TWT initiating AP can be the same as the baseline R-TWT announcement procedure.
      The C-R-TWT initiating AP advertises the schedule in its BSS as a regular R-TWT
      The STAs associated with the initiating AP can be agnostic of whether the advertised R-TWT schedule is coordinated or not.
      The B-TWT ID used for intra-BSS schedule identification can be independent of the C-R-TWT schedule identifier used to identify the schedule for MAP coordination.

## Slide 11: Intra-BSS R-TWT Negotiation (2)
  Negotiation by C-R-TWT initiating AP:
    Opening up an OBSS schedule for membership
      The C-R-TWT coordinated AP, in its intra-BSS schedule advertisement, can potentially indicate that the schedule is open for membership
        For instance, it has one or more associated STAs that have QoS delivery window that overlaps with the C-R-TWT schedule.
        The coordinated AP can indicate this condition (when it happens) to the C-R-TWT initiating AP (instead of tearing down the coordination).
      Otherwise, the coordinated AP, in its intra-BSS schedule advertisement, can indicate that the advertised schedule is not open for membership (i.e. schedule full)

## Slide 12: Intra-BSS R-TWT Maintenance
  When an R-T-TWT initiating AP successfully negotiates an R-T-TWT schedule with a coordinated AP, any changes to the schedule parameter can be made by the initiating AP.
  However, the initiating AP needs to propagate the corresponding changes to the coordinated AP.
    If changes in timing param (flexible) have been requested, the coordinated AP may enter into another round of negotiation with the initiating AP.
    This is in contrast to the baseline param change procedure
  If the coordinated AP accepts the changes, then it will propagate the changes to the its own BSS through advertisement
  Note: schedule suspension/resumption request should be accepted by the coordinated AP.

## Slide 13: C-R-TWT coordination termination
  Termination of a C-R-TWT coordination agreement can be made by either the initiating AP or the coordinated AP.
    Unsolicited response for a schedule with a REJECT indication would result in the termination of the schedule.
  Any modification in the coordination terms (e.g. changes in the modes) should go through a negotiation
    The same Req-resp based approach used in the initial C-R-TWT setup can be used.
    Either the initiating AP or the coordinated AP can request for changes in the coordination terms.

## Slide 14: SP1
Do you agree to define in 11bn a multiple AP coordination mechanism based on target wake time (TWT) information exchanged between the participating APs?
Such a mechanism would be referred to as coordinated TWT (C-TWT)

## Slide 15: SP2
Do you agree to define in 11bn a variant of TWT-based multi-AP coordination where the participating APs coordinate with each other exchanging restricted TWT schedule information?
Such a mechanism would be referred to as coordinated restricted TWT (C-R-TWT)

## Slide 16: SP3
Do you agree to define in 11bn different modes of coordinated R-T-TWT schedule?
Different modes can correspond to different levels of protection offered by the C-R-TWT coordinated AP for the C-R-TWT initiating AP.

## Slide 17: SP4
Do you agree to define in 11bn a mechanism to allow a C-R-TWT coordinated AP to make a distinction, during the intra-BSS schedule advertisement, between a schedule originated in the C-R-TWT coordinated AP’s BSS and a schedule originated in the C-R-TWT initiating AP’s BSS?

## Slide 18: References
[1] IEEE 802.11-21/1046r0, “Multi-AP: TWT Information Sharing”, Rubayet Shafin, et.al., July 2021.
[2] IEEE 802.11-22/1530r1, “Multi-AP coordination for next-generation Wi-Fi”, Rubayet Shafin, et.al., Sept 2022.
[3] IEEE 802.11-23/932r0, “Follow-up on TWT-based Multi-AP Coordination”, Rubayet Shafin, et.al., May 2023.
[4] IEEE 802.11-23/226r1, “Coordination of R-TWT for Multi-AP Deployment”, Abdel Karim Ajami, et.al., April 2023
[5] IEEE 802.11-23/250r0, “AP coordination with R-TWT”, Liwen Chu, et.al., April 2023
[6] IEEE 802.11-23/291r0, “R-TWT Multi-AP Coordination”, Muhammad Kumail Haider, et.al., May 2023.
[7] IEEE 802.11-23/297r0, “r-TWT for Multi-AP”, Laurent Cariou, et.al., April 2023
[8] IEEE 802.11-23/355r0, “Enhanced rTWT and MAP operation”, Hanqing Lou, et.al., May 2023
[9] IEEE 802.11-23/771r0, “Coordinated R-TWT Protection in Multi-BSS”, SunHee Baek, et.al., June 2023.