## Slide 1: Cross-link power save state indication
Date: 2024-04-03
Authors:

## Slide 2: Abstract
This document proposes cross-link indication of a transition from doze state to awake state by a non-AP MLD for the affiliated STAs operating in power save mode.

## Slide 3: Power Save Mode - Recap
A STA operating in power save (PS) mode operates in two possible states:
  Doze state
  Awake state.
A non-AP STA operating in PS mode indicates a transition from doze state to awake state by transmitting a PS poll frame.
A non-AP STA operating in U-APSD PS mode, indicates the start of an APSD service period by transmitting a trigger frame.
  Trigger frame can be a QoS Null frame, or a QoS data frame corresponding to a trigger-enabled access category.
As per baseline, for a non-AP MLD, the transitions of PS states (doze  awake, awake  doze) are indicated on a per-link basis.
A mechanism to indicate a transition from doze  awake state for one STA in PS mode, via another STA affiliated with the same MLD can improve efficiency.
  Some similar ideas were also discussed in early days of 802.11be [1-3].

## Slide 4: Illustration of cross-link PS state signaling
STA2
AP2
Beacon
AP MLD
non-AP MLD
STA1
AP1
Beacon
Awake
Doze
Doze
TIM in beacon indicates BU(s) for non-AP MLD.
PS poll
ACK
Awake
Doze
STA2
AP2
Beacon
AP MLD
non-AP MLD
STA1
AP1
Beacon
Awake
Doze
Doze
TIM in beacon indicates BU(s) for non-AP MLD.
ACK
Awake
Doze
Cross-link PS poll
Per-link signaling
Cross-link signaling

## Slide 5: Why cross-link PS state signaling?
Why not transmit the indication on link 2?
  A STA transitioning from doze to awake state has to follow the NAVSynch recovery procedure, which can cause significant delay before it can transmit. This adds latency to signaling.
  If multiple STAs of the non-AP MLD are transitioning from doze to awake state, separate signaling adds overhead.
Why not receive the BUs on link 1?
  This provides more flexibility for non-AP MLD implementation. For e.g., best link for receiving beacon frames (link 1), may be different from the best link to retrieve BUs (link 2).
  When TID-to-link Mapping Negotiation Support = 3 is used, certain BUs can only be retrieved from specific links.
Why not use cross-link power management mode change?
  A STA retrieving BUs while remaining in PS mode can implicitly transition back from awake  doze state.
  A STA retrieving BUs by changing from PS mode to active mode would require an explicit indication of transition back to PS mode by transmitting a frame that solicits a response. This is an unnecessary overhead.
  The use cases of both are different.

## Slide 6: Why now in 802.11bn?
MLO will become mature by the time 802.11bn is implemented. Use of Type 3 non-default TID-to-link mapping may become common in 802.11bn.
  802.11be already allows negotiation of Type 3 TID-to-link mapping.
In Denver meeting (Mar 2024), the 802.11bn group agreed [1] to define a mechanism to: “allow a non-AP MLD to indicate to its associated AP MLD that supports the mechanism in a frame sent on one enabled link, the power management mode for one or more affiliated non-AP STAs”. A joint design of cross-link PM mode and cross-link PS state signaling is recommended.
With progress being made to include mm-wave band into MLO framework, cross-link PS state indication will become more relevant due to the disparities in the link capabilities and parameters.

## Slide 7: Details to be considered
An 11bn AP/non-AP MLD should indicate capability of supporting cross-link PS state indication.
An 11bn AP MLD should indicate the expected delay in cross-link information transfer at the AP MLD.
The cross-link signaling can be captured in a new variant of the A-control subfield of a U-APSD trigger frame or PS poll frame transmitted by the non-AP MLD.
  For control frames, e.g., PS Poll, the A-control can be included by using a Control wrapper frame. An alternative is new mechanisms as discussed in 802.11bn [2] .
  The new A-control variant can be used for both cross-link PM mode and PS state signaling, both cases being differentiated via a Subtype subfield.
Control ID Value | Meaning | Length of the Control Information subfield (bits) | Content of the Control Information subfield
9 | AP assistance request (AAR) | 20 | See 9.2.4.7.10 (AAR Control)
10 | Link Indication (LI) | 20 | 
11-14 | Reserved |  | 
Subtype | Reserved | Link ID Bitmap
Bits: 3 1 16

## Slide 8: Conclusion
Cross-link signalling of change in the PS state by a non-AP MLD can improve efficiency and also reduce latency of retrieving buffered data.
Cross-link indication of change in PS state and PM mode should be jointly designed.
Use of A-control subfield is a good candidate for the cross-link indication.
The expected delay that an AP MLD may experience in the cross-STA information transfer should be indicated.

## Slide 9: References
11-19-1544-03-00be-multi-link-power-save-operation.pptx
11-19-1857-01-00be-multilink-power-save-followup.pptx
11-20-0085-01-00be-multi-link-power-save-link-bitmap.pptx
11-24-0171-06-00bn-tgbn-motions-list-part-1.pptx
11-24-0042-01-00bn-thoughts-on-flexible-control-frames.pptx

## Slide 10: Straw polls
SP 1: Do you agree to allow a non-AP MLD to indicate to its associated AP MLD that supports the mechanism in a frame sent on one enabled link, a change in the power save state for other affiliated non-AP STAs operating in PS mode?
  Whether the support for the mechanism is mandatory is TBD.
  Yes
  No
  Abstain

## Slide 11: Straw polls
SP 2: Do you agree to define an A-control subfield variant for cross-link power save state indication ?
  Yes
  No
  Abstain

## Slide 12: Straw polls
SP 3: Do you agree to allow an AP MLD to indicate the expected delay for the transfer of power-save state information between affiliated STAs?
  Yes
  No
  Abstain

## Slide 13: Backup slides