## Slide 1: Multi-Link SM Power Save Mode Follow Up
Date: 2024-04-08
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Ross Jian Yu |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
The following motion has passed for the power save of single-link operation:
TGbn defines a power save mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)
  Initial Control frame is TBD
  Whether that applies for a non-mobile AP is TBD
Multi-Link operation (MLO) is widely used since Wi-Fi 7, it is strongly required to define power save schemes for MLDs in TGbn.

## Slide 3: Introduction
Multi-Link SM power save (MLSMPS) mode has been proposed in TGbe [1-2] and TGbn [3], which aims to reduce the power consumption for MLDs.
Under the MLSMPS mode, a non-AP MLD uses a single link for listening, and becomes active on multiple links when it receives an initial control frame (ICF). After the frame exchange sequence, the non-AP MLD is available on only one link.
Several terminologies are proposed:
  MLSM Primary Link: the link that the non-AP MLD uses to monitor the ICF the AP MLD
  MLSM Links: a subset of the enabled links that is used by the non-AP MLD in the MLSM power save mode
The ICF shall be transmitted using non-HT (dup) PPDU, with one spatial stream, and low MCS (e.g., MCS 0~3).
The ICF shall also indicate the links that the AP MLD intends to use to transmit to the non-AP MLD.

## Slide 4: Link status under MLSMPS mode
MLSM Primary link:
  Initial status: listen for ICF using low capability
  After receiving ICF: transition to high capability to receive data frame
  After frame exchange: transition to low capability to listen for ICF
MLSM Non-Primary link:
  Initial status: unavailable
  After receiving ICF on the MLSM primary link: become available, able to receive data frame using high capability
  After frame exchange: become unavailable
  If no frame exchange: become unavailable after a timeout period

## Slide 5: How to determine MLSM Links
Step 1: during setup procedure, the non-AP MLD will indicate a set of setup links as the candidate set of links (Set 1) for the AP MLD to choose to transmit to the non-AP MLD under the MLSMPS mode
Step 2: in the ICF transmitted by the AP MLD on the MLSM primary link, the AP MLD can indicate the links (Set 2) that the AP MLD intends to use to transmit data frames to the non-AP MLD
  Set 2 is a subset of Set 1
  Note: AP MLD can determine Set 2 based on the scheduling (which links to use to transmit data to the non-AP MLD)
Step 3: in the ICR transmitted by the non-AP MLD on the MLSM primary link (as the response to the ICF), the non-AP MLD can further indicate the links (Set 3) that the non-AP MLD is ready to receive the data from the AP MLD
  Set 3 is a subset of Set 2
  Note: the non-AP MLD may not be able to receive on all the indicated MLSM links during the setup procedure due to in-device coexistence issue, hence the non-AP MLD can choose a subset of links to receive

## Slide 6: ICF & ICR details
There are many schemes that require ICF/ICR exchange, e.g., dynamic power save, IDC protocol, DSO, etc
We can use similar design for the ICF/ICR as proposed in those schemes, e.g.,
  Reuse MU-RTS/BSRP (with some modifications)
  Use a new type of trigger frame
  Define new A-Control fields
  Reuse Multi-STA BA
  Define new control frames
The information needed to be carried in the ICF/ICR is:
  The link(s) that the AP MLD intends to use
  The link(s) that the non-AP MLD is ready to use

## Slide 7: Conclusion
We propose a MLSMPS mode for the non-AP MLD to save power under the MLO framework
The non-AP MLD uses one link for listening, and becomes available on multiple links after receiving ICF.
The AP MLD can indicate the links that it intends to use to transmit data frames to the non-AP MLD in the ICF
The non-AP MLD can indicate the links that the non-AP MLD is ready to receive the data from the AP MLD in the ICR

## Slide 8: Straw Poll
Do you agree to define a MLSMPS mode in TGbn as follows:
    A non-AP MLD that is in MLSM PS mode can use only one link and one active receive chain for receiving and responding to an initial frame sent by the AP, and addressed to it
    The non-AP MLD becomes available on other links after responding to the initial frame
    The non-AP MLD may become unavailable on any of the “other links” if The TXOP on the “other link” has ended, or the non-AP MLD does not receive any frame addressed to it on the “other links” within a timeout period

## Slide 9: References
[1] 11-20-0760-05-00be-multi-link-sm-power-save-mode
[2] 11-22-1250-05-00be-lb266-cr-for-ml-sm-power-save-mode
[3] 11-23-1922-00-00bn-Multi-Link-SM-Power-Save-Mode