## Slide 1
MAP Co-CAC follow up

## Slide 2: Introduction
In reference[2], we have a high-level discuss on MAP co-CAC(check available check) mechanism with the following benefits:
  Address Wi-Fi service interruption issue caused by all RF chains switching to a target DFS channel
  Reduce Wi-Fi chipset cost caused by a dedicated RF chain design for CAC operation
  Avoid throughput drop issue caused by partial RF chain switching to a DFS channel
MAP (DFS) co-CAC is a mature feature
  Already standardized by other Wi-Fi group,(e.g. Wi-Fi Alliance Easy Mesh Specification)
In this contribution, we would like to see whether we can leverage MAP scheme to extend co-CAC feature to a more general MAP scenarios

## Slide 3: Recap MAP (DFS) co-CAC
What’s CAC?
  CAC（Channel Available Check）: Ensure that there are no radars operating on any selected channel for 1 min or 10 mins. e.g. no predefined radar pulse signal detected.
The basic mechanism of Coordinated DFS CAC in Easy Mesh network
  Controller sends a CAC request to an Agent AP(e.g. Agent AP1.)
  Agent AP1 reports the CAC status on the target DFS channel(assume no radar signal found)
  Another Agent AP(e.g. AP2) can switch into that DFS channel without
  CAC operation based on AP1’s CAC report results.
Multi-AP controller
Agent AP1
Agent AP2

## Slide 4: Regulatory rule(EN-301-893-ETSI)
Master devices:
  The master device shall use a Radar Interference Detection function in order to detect radar signals.
  The master device may rely on another device, associated with the master, to implement the Radar
  Interference Detection function. In such a case, the combination shall comply with the requirements applicable to a master.
  An RLAN network always has at least one RLAN device operating in master mode when operating in the bands 5 250 MHz to 5 350 MHz and 5 470 MHz to 5 725 MHz.

## Slide 5: The illustration of co-CAC in MAP coordination network
Assume MAP/multi-BSS consist a RLAN(Radio Local Area Networks)
  One AP(AP1) may rely on another AP(AP2), which will perform CAC on the target DFS channel
  If no radar detected on the target DFS channel, that channel be marked as “Available Channels”
  AP(1) can operate on an “Available Channels” based on the report results from AP2
  The worst case, if AP2 may reject the (new) CAC request, AP1 may perform CAC operation by itself.
AP1
STA12
STA13
STA14
STA11
AP2
STA22
STA23
STA24
STA21
AP3
STA32
STA33
STA31

## Slide 6: Regulatory certification concern
For individual AP certification test, each AP should operates in Master mode as they did today.
For AP group certification test, the certification test should be based on the combination based on ETSI regulatory rule.
  mobile AP can not operate in master mode(no radar signal detection function)

## Slide 7: The proposed signaling
AP1
AP2
CAC request
CAC report

## Slide 8: Summary
Recap the machinist of MAP co-CAC in Easy mesh network
Analyze the possible approach of 11bn MAP co-CAC under ETSI Regulatory rule
Propose a simple signaling exchange to implement MAP co-CAC

## Slide 9
THANK YOU 

## Slide 10: Reference
[1] 802.11bn PAR
[2] 23/2186r0 MAP coordination for DFS channel
[3] ETSI EN 301 893 V2.1.1 (2017-05)
[4] Wi-Fi EasyMesh® Specification Version DRAFT 6.0

## Slide 11: SP1
Do you agree 11bn should define a co-CAC procedure under MAP coordination scheme?