## Slide 1: Sensing and Ranging in IMMW
Date: 2024-05-13
Author:
Name | Affiliation | Address | Phone | Email
Tony Xiao Han | Huawei Technologies Co., Ltd. | F3, Huawei Base, Shenzhen, China |  | Tony.hanxiao@huawei.com
Rui Du | Huawei Technologies Co., Ltd. |  |  | 
Narengerile | Huawei Technologies Co., Ltd. |  |  | 
Zhuqing Tang | Huawei Technologies Co., Ltd. |  |  | 
Mengshi Hu | Huawei Technologies Co., Ltd. |  |  | 
Yiyan Zhang | Huawei Technologies Co., Ltd. |  |  | 
Claudio Da Silva | Meta Platforms |  |  | 

## Slide 2
Overview
In this contribution, we would like to consider Sensing and Ranging in IMMW.
Some general design consideration are given.

## Slide 3
Definition
A Station to identify its absolute and relative position to another station or stations it’s either associated or unassociated with.
  Better accuracy with respect to the Fine Timing Measurement (FTM) protocol.
  For Sub 7GHz (11n/ac/ax), and 60GHz (11ad/ay)
WLAN Ranging (802.11az/bk) [2, 3]
WLAN Sensing (802.11bf) [1]
WLAN sensing is the use of received WLAN signals to detect feature(s) of an intended target(s) in a given environment.
  Features = Range, velocity, angular, motion, presence or proximity, gesture, etc.
  Target = Object, human, animal, etc.
  Environment = Room, house, car, enterprise, etc.
  For Sub 7GHz (11ac/ax), and 60GHz (11ad/ay)
IMMW [4]

## Slide 4
Motivation
Sensing and Ranging for IMMW
  Feature: Similar as 802.11bf/az/bk for WLAN, Sensing and Ranging also could be the unique/highlight features in IMMW
  Market: Based on the addressable market for WLAN Sensing [8], Sensing and Ranging could further enable the commercialization of IMMW
IMMW for Sensing and Ranging
  Requirement: Some use cases may need mmWave, e.g.,
    For Sensing: Audio with user tracking, fine-grained gesture recognition, etc. [7, 8]
    For Ranging: Device Proximity Detection, Nano Location in store, etc. [9]
  Current: standardized mmWave Sensing and Ranging is based on 11ad/ay
  Potential: IMMW may be a good candidate (Unified baseband for sub-7GHz and mmWave) to supplement the mmWave part, with higher commercialization possibility.
Sub7GHz
mmWave
802.11bf
Sub7GHz
mmWave
802.11az
Supplement
May not be implemented
IMMW
  Pre-standard (2024-2025)
  It is anticipated that there will be a rapid increase in the number of WLAN Sensing compatible devices.
  Because of the arrival of pre-standardization 802.11bf chipsets
  Official 802.11bf standardization (2025-2026)
  Additional growth is expected following the official 802.11bf Standard releases
  Well-defined requirements and market demand encourage more chipset vendors to adopt 802.11bf for their chipsets
Notes: Mutual beneficial

## Slide 5
Procedure & Technology in 802.11bf [5]
802.11bf have well defined protocol for Sensing, no need to completely redesign
Minimize redesign according to IMMW architecture
Sensing (Sub-7GHz): Consider as baseline; DMG sensing (60GHz): Consider as reference
Consider as baseline
No need to redesign
Consider as reference
Need to redesign IMMW sensing and only take DMG sensing as reference, but not revise based on DMG sensing

## Slide 6
Initial design consideration (Sensing)
Waveform/Sequence design
Reuse newly designed NDP
Channel modeling
Ray-tracing-based
DDHC-based
Sensing by proxy (SBP)
Signal proc & Feedback
IMMW sensing procedure
Technology
Other?
Robustness
RX operating point/
RF/Analog/Digital gain
Other?
(Reuse)
Efficiency
Sensing availability window or ？
Q matrix
TX power
Multiple sensing measurement sessions
CSI
Other?
Multi-Link
TBD
IMMW sensing
Consider really necessary types
Others?
IMMW sensing types
Minimize modification of 11bf, according to IMMW architecture
Consider Multi-Link Operation
Others?
IMMW sensing procedure

## Slide 7
802.11az Key Radio and Positioning Techniques [6]
Medium efficient operation via dynamic (demand dependent) measurement rate.
Adaptation to next generation mainstream 802.11ax Trigger Based Operation (MIMO, Trigger Frame, NDP frame)
Authenticity and privacy and anti-spoofing mechanism via PMF in the unassociated mode and PHY level randomized measurement sequences (HE LTF sequences protection).
Improved accuracy via MIMO and larger BW available in the <7Ghz band for 11ax.
MIMO enablement for measurement for improved accuracy especially for NLOS or NNLOS conditions.
Passive location with fixed overhead independent of number of users
802.11az (bk) have well defined protocol for Ranging, we do not need to redesign it again

## Slide 8
Procedure & Technology in 802.11az/bk
802.11az/bk have well defined protocol for Ranging, no need to completely redesign
Minimize redesign according to IMMW architecture
Ranging (Sub-7GHz): Consider as baseline; DMG Ranging (60GHz): Consider as reference
Consider as baseline
No need to redesign
Consider as reference
Need to redesign IMMW ranging and only take DMG ranging as reference, but not revise based on DMG ranging

## Slide 9
Initial design consideration (Ranging)
IMMW ranging procedure
Technology
IMMW ranging
Consider really necessary types
Others?
IMMW ranging
Measurement exchange variants
Minimize modification of 11az/bk, according to IMMW architecture
Consider Multi-Link Operation
Others?
IMMW ranging procedure
Waveform/Sequence design
Reuse newly designed NDP
Security
Secure XXX LTF
PASN
Signal processing and feedback
TOA
TOD
Phase shift
AOA
AOD
Other
Other?
Robustness
DMG First path BFT
Secure XXX LTF
Efficiency
DMG LOS assessment
Availability window
Multiple ranging measurement sessions
Multi-Link
TBD

## Slide 10
Summary
There is strong motivation to add Sensing and Ranging in IMMW
  Sensing and Ranging for IMMW
  IMMW for Sensing and Ranging
In order to add Sensing and Ranging in IMMW, we could consider the following design logic
  Sensing (Sub-7GHz) in 802.11bf could be considered as baseline, but no need to redesign Sub-7GHz sensing;
  Need to redesign IMMW sensing and only take DMG sensing (60GHz) in 802.11bf as reference, but not revise based on DMG sensing
  Ranging (Sub-7GHz) in 802.11az/bk could be considered as baseline, but no need to redesign Sub-7GHz ranging;
  Need to redesign IMMW ranging and only take DMG ranging (60GHz) in 802.11az/bk as reference, but not revise based on DMG ranging
  Minimize redesign according to IMMW architecture

## Slide 11
Reference
[1] https://www.ieee802.org/11/Reports/tgbf_update.htm
[2] https://www.ieee802.org/11/Reports/tgaz_update.htm
[3] https://www.ieee802.org/11/Reports/tgbk_update.htm
[4] https://mentor.ieee.org/802.11/dcn/24/11-24-0116-02-immw-immw-draft-proposed-par.docx
[5] Du R, Hua H, Xie H, Song X, Lyu Z, Hu M, Xin Y, McCann S, Montemurro M, Han TX, Xu J. An overview on IEEE 802.11 bf: WLAN sensing. arXiv preprint arXiv:2310.17661. 2023 Oct 20.
[6] http://www.kt.agh.edu.pl/~kulakowski/evolution/09_wifi2.pdf
[7] https://mentor.ieee.org/802.11/dcn/20/11-20-1712-02-00bf-wifi-sensing-use-cases.xlsx
[8] https://go.abiresearch.com/lp-the-commercial-market-value-for-wifi-sensing, Andrew Zignani, Andrew Spivey, ABI research, December 2022
[9] https://mentor.ieee.org/802.11/dcn/16/11-16-0137-04-00az-ngp-use-case-document.pptx

## Slide 12
SP 1
Do you agree that sensing and ranging support/operation should be defined in IMMW?