## Slide 1: Harmonization Proposal for 11bi D1.0
Date: 2024-04
Authors:

## Slide 2: Abstract
[1] “24/0681r1 TGbi – Epoch Structure Proposal” was introduced to TGbi in April 2024
[2] “24/579r0 Periodic Obfuscation (automatic epoch)” was a new proposal introduced to TGbi recently in March 2024 (also known as “periodic obfuscation” or “automatic epoch”)
The above two were merged in [3] “24/604r3 Periodic Frame Anonymization” and will need some harmonization to merge into draft D0.3
In this presentation we discuss the following:
  Current assumption in D0.3
  Whether individual epoch is needed
  Some initial observations and thoughts on [1] and [2]
  A harmonized proposal for D1.0
    Since we are running out of time for D1.0, it’s best to have a clearly defined “lowest common denominator” solution rather than multiple vaguely defined options. Addition options can be revisited after D1.0.

## Slide 3: Some current assumptions of EPOCH, Frame Anonymization, and STA MAC Address Rotation in TGbi
Concept of epoch and transition periods
  Individual epoch (periodic or one-shot)
  Group epoch (periodic)
AP and STA agree on an epoch length (where the anonymization parameters stay unchanged) and start time using some initial signaling
In each epoch, AP and STA derive the Frame Anonymization (FA) parameters that apply within the epoch (e.g., STA MAC address, SN_offsets and PN_offset) automatically without extra signaling
AP assigns a new AID to each associated STA for each new epoch (using unicast encrypted signaling to each STA)
Most of the above are captured/assumed in the current draft D0.3

## Slide 4: Thoughts on Individual EPOCH
To allow a STA to set up an individual epoch (periodic or one-shot) with an AP per the STA’s preference.
However, if this STA sets up something different than other group epochs (if exist), this STA will be the only STA changing its parameters at the epoch boundaries so it will stand out in the crowd and be easily trackable.
However, we do understand that sometimes a STA may prefer something different than the default group epoch:
  Given a STA can already achieve this by requesting a new group epoch (with it as the first participant and other STAs may join later), perhaps we could just limit the individual epoch to the one-shot case?

## Slide 5: Default Group EPOCH Proposal [1]
High-level recap of the proposal:
  An AP sets up a default group epoch for STAs to join (during assoc or post-assoc)
  The AP indicates to the associated STAs (unicast securely) the # of STAs in each group
  When a STA associates with the AP, the STA can join the default group, request for a new group, or just not participate in any of group epoch
  Some MAC collision resolution mechanism due to derived MAC addresses

## Slide 6: Observation and Thoughts on the proposal
The concept of the default group and non-default group(s) is independent of the actual anonymization mechanism (e.g., how to obfuscate a subset of MAC header subfields) and the length of the epoch.
The proposal requires the AP to actively keep track of the # of participating STAs in each group and update the STAs securely and individually
  STAs come and go all the time (e.g., hotspot scenarios). Also, most STAs do not diassociate cleanly. Due to the signaling overhead and extra processing involved, an AP may not be able to update the STAs with the most up-to-date accurate info in real-time.
  It means a STA will not know precisely the # of participating STAs anyways. Can the STA trust the number the AP indicates and is the signaling overhead still worth it?
Also, since the STA will learn the # of participants in a group, is it possible a STA will not want to join a group unless the # of participants exceeds N (e.g., N=10) but if all STAs think this same way, who would start a new group for the greater good?

## Slide 7: Suggestions
Discuss
  Is it worth the AP processing and signaling overhead to keep track of the # of STAs in a group and update the STAs individually? Perhaps we could say the AP indicates the approximate # of STAs to alleviate the stringent keeping track requirements?
  How to encourage a STA to start a new group?
    Say default group has epoch of 10min and it’s the only group so far. Now a STA associates with the AP and want a 1min epoch. The STA sees there’s no such group and it will be the only STA in this group thus susceptible to tracking. What’s in it for the STA to ask for this new 1min group epoch?

## Slide 8: Periodic Obfuscation Proposal [2] (automatic epoch)
High-level recap of the proposal:
  Both AP and STA agree to an epoch period and start time
  For each epoch, both sides compute a random offset_mask as a function of TSF, a pairwise key, etc.
    XOR the offset_mask with selected subfields (specified in the spec) of the MAC header
      E.g., the STA MAC address (A1 for DL frames and A2 for UL frames), SN, PN, QoS control, GCMP header, etc.
  For each epoch, both sides compute a random per-BSS AID_offset per TSF using a per-BSS key
    Apply the AID_offset to all the associated STAs

## Slide 9: Observations and Thoughts on the proposal
Adding a per-BSS offset to all the AIDs is prone to insider attack
  An attacker only needs to subscribe to the hotspot operator then he/she can access the per-BSS offset legitimately to track all the other STAs. Note having a small epoch length (e.g., ms) doesn’t solve this issue.
  Note the protection of AID is crucial because it is one of the weakest links among all other privacy info and it is hard to hide.
Adding the same offset to all the AIDs does not seem to provide privacy benefits as the whole block of AIDs just shift around together, especially when the epoch is long like in seconds or mins
For retransmissions, the same obfuscation parameters used in the original tx need to be used. Since retx can occur tens of ms later, the transmitter will need to cache the original obfuscation info for every retx PPDU, which could be a lot if the epoch length is very short (e.g., in ms).

## Slide 10: Observations and Thoughts on the proposal (cont’d)
Drive down the epoch to 1ms adds a lot of complexity and it’s not clear how the epoch boundaries are handled with the +/- time delta that accounts for clock drift. Also, not clear how to deal with retx.
XOR applied to SN and PN will leak privacy info. In fact, using XOR to hide any sequentially increasing value is a bad idea if the mask does not change frequently (see [4] slide #17 for explanation).

## Slide 11: Comparison
 | Existing FA assumption | Periodic Obfuscation
AID prone to insider attack? | No (+) | Yes (-)
Requires explicit signaling for AP to assign new AIDs in each epoch | Yes (-) | No (+)
Requires explicit signaling for FA parameters in each epoch? | No. All derived per TSF per STA | No. All derived per TSF per STA
Potential STA MAC address collision? | Yes, because the value is derived | Yes, because the value is derived

## Slide 12: Comparison (cont’d)
Time scale/schemes comparison
Epoch length | Existing FA | Periodic Obfuscation
1ms | A1 packet filtering will need to be reprogrammed every ms (-) Epoch boundary jitter hard to handle (-) Re-tx handling is complicated (-) Per-PPDU retx context could be large (-) AID re-assignment is not feasible (-) | A1 packet filtering will need to be reprogrammed every ms (-) Epoch boundary jitter hard to handle (-) Re-tx handling is complicated (-) Per-PPDU retx context could be large (-) AID hiding becomes more effective (barring insider attacks) (+)
100ms – 10s of seconds | Signaling overhead could still be too high (-) Re-tx handling is still complicated (-) AID re-assignment more feasible (+) | AID hiding not effective (-) XOR will leak info from SN and PN (-)
5min | No issues (+) | AID hiding not effective (-) XOR will leak info from SN and PN (-)

## Slide 13: Observation
The periodic obfuscation is prone to insider attack, even with a 1ms epoch.
Even if we ignore the insider attack, if the epoch length is too short (say 1ms) it will create lots of complexity and memory issues, full of stringent h/w requirements.
If the epoch length is too long, using XOR is not desirable, and AID is essentially not obfuscated.

## Slide 14: Proposal for Harmonization for D1.0
Limit individual epoch to only one-shot (and no periodic)
Use [1] as the framework for setting up group epoch
  AP sets up a default group epoch
  STA can request AP to set up a new group epoch
  AP advertises the # of STAs participating in each group
Having epoch lengths no shorter than 5 minutes defined in the spec
  This will allow assigning new AIDs more feasible to avoid insider attack
  Other shorter values TBD
For the actual obfuscation/anonymization:
  AP assigns new AIDs securely for all associated STAs in each epoch with explicit signaling
  Autogen the random pariwise STA MAC address, PN_offset, and SN_offsets. Use addition of offsets for PN and SN.
  Use the mask idea of [2] to autogen a random mask to XOR the selected subfields of the MAC header such as QoS control, GCMP header, etc. (discuss which subfield)
Have a MAC collision resolving mechanism

## Slide 15: References
[1] 24/0681r1 TGbi – Epoch Structure Proposal
[2] 24/579r0 Periodic Obfuscation (automatic epoch)
[3] 24/604r3 Periodic Frame Anonymization (text proposal for [1] and [2] merged above)
[4] 23/0873r02 Client Frame Tracking Countermeasures (CFTC)