## Slide 1: Preamble and PE transmission in PPDU using DRU
Date: 2024-7-11
Authors:

## Slide 2: Introduction
The DRU consists of subcarriers spreading across a certain bandwidth to overcome PSD limitations.
Most contributions focus on Data transmission by using DRU.
  In [1]-[7], there are many high level design principles of DRU, e.g. distributed BW, DRU size, puncturing, and hybrid mode, etc.
  In [8]-[15], DRU tone plan and pilot design are discussed.
In this presentation, we will share our thoughts on Preamble and PE transmission in PPDU using DRU.

## Slide 3: Problem
When DRU is introduced, how should PPDU’s Preamble and PE be transmitted to match the performance of Data?
  We mainly focus on UL TB transmissions.
L-STF
L-LTF
L-SIG
SIG
RL-SIG
UHR-STF
UHR-LTF
Data
PE
Example: UHR PPDU

## Slide 4: Legacy preamble
L-STF
L-LTF
L-SIG
SIG
RL-SIG
UHR-STF
UHR-LTF
Data
PE
Example: UHR PPDU
When PPDU using DRU transmission:
  L-STF, L-LTF, and L-SIG (RL-SIG) fields are duplicated over all the 20 MHz channels which overlap with the DRU assigned to the non-AP STA.
    For compatibility with legacy STA detection

## Slide 5: UHR-STF, UHR-LTF and PE
L-STF
L-LTF
L-SIG
SIG
RL-SIG
UHR-STF
UHR-LTF
Data
PE
Example: UHR PPDU
When PPDU using DRU transmission:
  The set of tones used in UHR-STF and UHR-LTF sequences should be the same as the set of tones in the DRU used by the Data field.
    To ensure AGC and channel estimation consistent with DRU
  The PE field should be transmitted with the same average power as the Data field, and be commensurate with the tones of the occupied DRU(s) in the Data field.
    For implementation simplicity

## Slide 6: SIG (1/2)
When DRU used in a UHR TB PPDU, for example, the SIG is U-SIG.
  The SIG field is duplicated over all the 20 MHz channels which overlaps with the DRU assigned to the STA.
    In order to be compatible with STAs which do not support DRU but can also decode SIG.
    Although in some cases, the Tx power of SIG is slightly lower than Data, we can appropriately reduce the Tx power of Data to match preamble’s performance, and avoid introducing new PPDU format due to special processing of SIG.
      The max difference between Data and SIG is just 0.11dB, see appendix.
L-STF
L-LTF
L-SIG
SIG
RL-SIG
UHR-STF
UHR-LTF
Data
PE
Example: UHR PPDU

## Slide 7: SIG (2/2)
Example 1: 80MHz UHR TB PPDU using DRU
t
f
L-STF
L-LTF
L-SIG
U-SIG
RL-SIG
L-STF
L-LTF
L-SIG
U-SIG
RL-SIG
L-STF
L-LTF
L-SIG
U-SIG
RL-SIG
L-STF
L-LTF
L-SIG
RL-SIG
20MHz
UHR-STF, UHR-LTF, Data, PE
STA1
U-SIG

## Slide 8: Summary
L-STF, L-LTF, and L-SIG (RL-SIG) fields:
  Duplicated over all the 20 MHz channels which overlap with the DRU assigned to the non-AP STA. The used tones are continuous.
SIG field:
  Duplicated over all the 20 MHz channels which overlap with the DRU assigned to the user, assuming that DRUs are only used in UL TB and UL non-TB SU transmissions.
UHR-STF, UHR-LTF, and PE fields:
  The set of tones used in UHR-STF/LTF sequences and PE should be the same as the set of tones in the DRU used by Data field.

## Slide 9: References
[1] 11-23-1919-00-00bn-dRU Proposal
[2] 11-23-1988-02-00bn-High Level Thoughts on DRU Design
[3] 11-23-2020-01-00bn-High-Level Perspectives on Distributed Tone RU for 11bn
[4] 11-23-2200-03-00bn-Distribution bandwidth of DRU
[5] 11-24-0014-00-00bn-Further Thoughts on dRU
[6] 11-24-0400-00-00bn-Hybrid PPDU and Distribution Bandwidth for DRU
[7] 11-24-0520-01-00bn-Discussion on DRU
[8] 11-23-2021-01-00bn-Principle and Methodology for dRU Tone Plan Design
[9] 11-23-2031-02-00bn-Data Tones Grouping in Tone-Distributed RUs
[10] 11-24-0078-01-00bn-A dRU Design Approach for 20 MHz
[11] 11-24-0401-00-00bn-Multiple DRU Follow Up
[12] 11-24-0402-00-00bn-20 MHz Tone Plan and Pilot Design for DRU
[13] 11-24-0468-01-00bn-DRU Tone Plan for 11bn
[14] 11-24-0476-01-00bn-Tone Plan Design for Distributed RU
[15] 11-24-0501-01-00bn-Pilot Design Considerations for dRU

## Slide 10: Appendix
RU Size | Field | Tx Power (dBm) |  |  | Gap=UHRmodulated－PreUHRmodulated (dB) |  | 
 |  | DRUBW20 | DRUBW40 | DRUBW80 | DRUBW20 | DRUBW40 | DRUBW80
RU26 | Pre-UHR modulated* | 11.11, 11.43 | 14.12, 14.44 | 17.13, 17.45 | -0.90, -1.22 | -0.90, -1.22 | -3.91, -4.23
 | UHR modulated | 10.21 | 13.22 | 13.22 |  |  | 
RU52 | Pre-UHR modulated | 11.11, 11.43 | 14.12, 14.44 | 17.13, 17.45 | 0.35, 0.03 | -0.90, -1.22 | -0.90, -1.22
RU52 | UHR modulated | 11.46 | 13.22 | 16.23 |  |  | 
RU106 | Pre-UHR modulated | 11.11, 11.43 | 14.12, 14.44 | 17.13, 17.45 | 0.43, 0.11 | 0.43, 0.11 | -0.82, -1.14
RU106 | UHR modulated | 11.54 | 14.55 | 16.31 |  |  | 
RU242 | Pre-UHR modulated | / | 14.12, 14.44 | 17.13, 17.45 | / | 0.34, 0.02 | -0.24, -0.56
RU242 | UHR modulated | / | 14.46 | 16.89 | / |  | 
RU484 | Pre-UHR modulated | / | N/A | 17.13, 17.45 | / | / | 0.34, 0.02
RU484 | UHR modulated | / | N/A | 17.47 | / | / | 
Note 1: PSD = -1dBm/MHz
*Note 2: The two values in the pre-UHR modulated field correspond to the L-STF/L-LTF field and the L-SIG/U-SIG/UHR-SIG field, respectively.
Since the L-STF/L-LTF field uses 52 tones, L-SIG/U-SIG/EHT-SIG field uses 56 tones.

## Slide 11: SP 1
Do you agree to add the following text to the TGbn SFD?
If a DRU for a PPDU occupies more than one 20 MHz channel, then the L-STF, L-LTF, L-SIG, and RL-SIG fields are duplicated over all the 20 MHz channels which are occupied by the DRU.
Y/N/A: //

## Slide 12: SP 2
Do you agree to add the following text to the TGbn SFD?
If a DRU for a PPDU occupies more than one 20 MHz channel, then the SIG field is duplicated over all the 20 MHz channels within a given 80MHz frequency subblock which are occupied by the DRU.
  The content of SIG field between different 80MHz frequency subblocks is TBD.
  Note: The SIG field is U-SIG in a UHR TB PPDU
Y/N/A: //

## Slide 13: SP 3
Do you agree to add the following text to the TGbn SFD?
The set of tones used by the PE field should be same as the set of tones in the DRU used by the Data field.
Y/N/A: //