## Slide 1: Time-domain A-PPDU for Collision Reduction and Priority Access
Date: 2024-04-25
Authors:
Name | Affiliation | Address | Phone | Email
Ning Gao | OPPO |  |  | gaoning1@oppo.com
Chaoming Luo |  |  |  | luochaoming@oppo.com
Liuming Lu |  |  |  | luliuming@oppo.com
Yapu li |  |  |  | liyapu1@oppo.com
Liangxiao Xin |  |  |  | v-xinliangxiao@oppo.com
Dong Wei |  |  |  | v-dong.wei@oppo.com

## Slide 2: Introduction
Compared with the EHT, the UHR aims at increasing throughput by 25%, reducing MPDU loss by 25% as well as reducing the latency by 25% for the 95th percentile of the latency distribution.
However, collisions will result in a waste of channel, retransmission as well as a large delay or jitter due to the double backoff mechanism, so collision reduction could help UHR with all three goals. [1,4,5]
Meanwhile, there is a strong demand for priority channel access of UHR STAs which have low latency traffic. [2,3]
In this contribution, we intend to introduce a Time-domain A-PPDU to achieve the collision reduction and the priority access at the same time.

## Slide 3: Proposed: Time-domain A-PPDU
Compared with EDMG A-PPDU, the proposed Time-domain A-PPDU is a concatenation of two independent and complete PPDUs shown as bellow.
The format of the First PPDU and the Second PPDU can be completely different. (e.g. a non-HT duplicate PPDU and a UHR PPDU)
The two PPDUs are allowed to carry distinct frames and traffics. (e.g. a Data frame and a Control frame)
The purpose of the First PPDU is to create a guard interval to protect the Second PPDU from overlapping with other PPDUs.
The length of the First PPDU should be longer than other PPDUs and could be dynamically adjusted according to the current network.
The available formats of the First PPDU within a BSS should be announced by the AP like EDCA Parameters Set.

## Slide 4: How to use the Time-domain A-PPDU
A UHR STA with low latency traffic (e.g. the STA 1 in the figure below) could contend for the channel by transmitting a Time-domain A-PPDU while following the EDCA rule.
If a collision happens, due to the existence of the First PPDU, the Second PPDU is able to present on the medium later than other PPDUs.
Therefore, the TXOP responder (e.g. AP) could detect and receive the Second PPDU successfully which includes a RTS frame and response a CTS frame to STA 1.
Consequently, the STA 1 win the channel with priority and this collision is avoided.
However, collisions between UHR STAs with LL traffic may still happen and result in double backoff.

## Slide 5: Analysis
Advantages
  Reduce collision and double backoff
  Priority Access for LL UHR STA
  Easy for implementation
  Limited influence on the fairness
Disadvantages
  Extra constant access delay due to the First PPDU
  Collision between LL UHR STAs may still happen
  Hidden Node Problem

## Slide 6: Summary
A Time-domain A-PPDU is proposed in this contribution to achieve collision reduction as well as priority access at the same time.
The Time-domain A-PPDU is composed of a First PPDU and a Second PPDU
  The First PPDU is used to create a guard interval to protect the Second PPDU from overlapping with other PPDUs.
  The Second PPDU is carrying the intended frame.
The format or length of the First PPDU can be seen as another kind of EDCA parameter.

## Slide 7: Reference
[1] 11-22-1519-00-0uhr-requirements-of-low-latency-in-uhr
[2] 11-23-1065-00-0uhr-low-latency-channel-access
[3] 11-23-2126-00-00bn-low-latency-channel-access-follow-up
[4] 11-24-0284-01-00bn-low-latency-low-collision-low-power-uhr-medium-access
[5] 11-24-0031-00-00bn-deterministic-backoff

## Slide 8: Appendix: EDMG A-PPDU
The EDMG A-PPDU defined in 11ay is a concatenation of EDMG PPDUs shown as bellow.
The first PPDU of an EDMG A-PPDU includes L-STF, L-CEF, L-Header, EDMG-Header-A, EDMG-STF, EDMG-CEF, and Data fields, and each subsequent PPDU includes EDMG-Header-A and Data fields only.