## Slide 1: Distribution Bandwidth within 80 MHz for DRU
Date: 2024-05-12
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
In the last F2F meeting, various topics for DRU were extensively discussed [1-12]
In this contribution, we discuss the distribution bandwidth especially within a 80 MHz channel to efficiently support DRU considering the following cases
  Non-puncturing
  Preamble puncturing
  Hybrid PPDU

## Slide 3: Non-Puncturing
For any non-punctured 80 MHz channels to which DRUs are applied, we propose to allow the following distribution bandwidth modes
  80 MHz
    This is reasonable in terms of the power boosting gain and data rate
  20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz)
    In order to support STAs which are only capable of a narrow operating bandwidth, e.g., 20 MHz, this mode is essential
Further discussion is needed for the following modes
  40 MHz + 40 MHz
    This cannot support 20 MHz operating STAs and STAs which are operating in 40 MHz can be supported by 20 MHz + 20 MHz + 40 MHz mode
  20 MHz + 20 MHz + 20 MHz + 20 MHz
    This may be unfavorable for 80 MHz operating STAs

## Slide 4: Preamble puncturing (1/2)
When one of the 20 MHz channels is punctured in an 80 MHz channel, we propose to allow 20 MHz + 40 MHz mode
  Even though 60 MHz distribution bandwidth can be designed for higher power boosting gain and data rate, its tone plan varies depending on the location of the punctured 20 MHz channel
  20 MHz + 40 MHz mode is better in terms of the implementation
    In addition, by using MDRU proposed in [4], we can increase the data rate without sacrificing the power boosting gain
  As for 20 MHz + 20 MHz + 20 MHz mode, we need more discussion
    It may not be useful considering 80 MHz operating STAs

## Slide 5: Preamble puncturing (2/2)
When one of the 40 MHz channels is punctured in a certain 80 MHz channel, we propose to allow the following distribution bandwidth modes
  40 MHz
    This is reasonable in terms of the power boosting gain and data rate
  20 MHz + 20 MHz
    In order to support 20 MHz operating STAs, this mode is indispensable

## Slide 6: Hybrid PPDU (1/2)
In [8][9], 160 MHz and 320 MHz hybrid PPDUs were proposed
  They also consider that there is no mix of DRU and RRU within an 80 MHz channel
We also agree with 160 MHz and 320 MHz hybrid PPDUs and no mix within an 80 MHz channel
  In these hybrid PPDUs, the distribution bandwidth modes proposed in slide 3 to 5 can be also allowed in 80 MHz channels where DRUs are applied

## Slide 7: Hybrid PPDU (2/2)
In addition, we propose the 80 MHz hybrid PPDU which was introduced in [3]
  There is no mix within a 40 MHz channel
  We also propose to allow 40 MHz and 20 MHz + 20 MHz distribution bandwidth modes in a non-punctured 40 MHz channel where DRUs are applied
    The former is reasonable in terms of the power boosting gain and data rate
    The latter is essential to support 20 MHz operating STAs
  If one of 20 MHz channels is punctured in a 40 MHz channel where DRUs are applied, only 20 MHz distribution bandwidth is allowed

## Slide 8: Conclusion
We have discussed distribution bandwidth modes allowed within a 80 MHz channel for DRU considering the following cases
  Non-puncturing
  Preamble puncturing
  Hybrid PPDU

## Slide 9: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  In a non-punctured 80 MHz PPDU, the following distribution bandwidth modes are allowed for DRU
    80 MHz
    20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz)
Y/N/A: //

## Slide 10: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  In an 80 MHz PPDU where one of the 20 MHz channels is punctured, the following distribution bandwidth mode is allowed for DRU
    20 MHz + 40 MHz (or 40 MHz + 20 MHz)
Y/N/A: //

## Slide 11: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  In an 80 MHz channel where one of the 40 MHz channels is punctured, the following distribution bandwidth modes are allowed
    40 MHz
    20 MHz + 20 MHz
Y/N/A: //

## Slide 12: Straw Poll #4
Do you agree to add the following text to the TGbn SFD?
  11bn supports 160 MHz and 320 MHz hybrid PPDUs
    There is no mix within an 80 MHz channel
    80 MHz and 20 MHz + 20 MHz + 40 MHz (or 40 MHz + 20 MHz + 20 MHz) distribution bandwidth modes are allowed in a non-punctured 80 MHz channel where DRUs are applied
    20 MHz + 40 MHz (or 40 MHz + 20 MHz) distribution bandwidth mode is allowed in an 80 MHz channel where DRUs are applied and one of 20 MHz channels is punctured
    40 MHz and 20 MHz + 20 MHz distribution bandwidth modes are allowed in an 80 MHz channel where DRUs are applied and one of 40 MHz channels is punctured
Y/N/A: //

## Slide 13: Straw Poll #5
Do you agree to add the following text to the TGbn SFD?
  11bn supports an 80 MHz hybrid PPDU
    There is no mix within a 40 MHz channel
    40 MHz and 20 MHz + 20 MHz distribution bandwidth modes are allowed in a non-punctured 40 MHz channel where DRUs are applied
    20 MHz distribution bandwidth is allowed in a 40 MHz channel where DRUs are applied and one of 20 MHz channels is punctured
Y/N/A: //

## Slide 14: References
[1] 11-23-2200-03-00bn-distribution-bandwidth-of-dru
[2] 11-24-0332-00-00bn-discussion-on-drus
[3] 11-24-0400-00-00bn-hybrid-ppdu-and-distribution-bandwidth-for-dru
[4] 11-24-0401-00-00bn-multiple-dru-follow-up
[5] 11-24-0402-01-00bn-20-mhz-tone-plan-and-pilot-design-for-dru
[6] 11-24-0429-00-00bn-range-extension-with-dru
[7] 11-24-0468-01-00bn-dru-tone-plan-for-11bn
[8] 11-24-0476-01-00bn-tone-plan-design-principles-for-distributed-ru
[9] 11-24-0477-02-00bn-high-level-perspective-on-dru-follow-up
[10] 11-24-0500-00-00bn-follow-up-on-high-level-thoughts-on-dru-design
[11] 11-24-0501-02-00bn-pilot-design-considerations-for-dru
[12] 11-24-0520-01-00bn-discussion-on-dru