## Slide 1: Non-AP STA Triggered DSO
Date: 2024-06-12
Authors:
Name | Affiliations | Address | Phone | email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Liuming Lu | OPPO |  |  | 
Ning Gao | OPPO |  |  | 
Yapu Li | OPPO |  |  | 

## Slide 2: Abstract
Proposes a mechanism for a non-AP STA to solicit the dynamic subband operation (DSO) during a TXOP.

## Slide 3: Recap – DSO and Interference Report
Several contributions introduced DSO [1]-[4]
  In a nutshell, AP as the TXOP holder transmits an initial control frame (ICF) to trigger non-AP STAs to switch to a non-primary sub-band.
Several contributions introduced interference report [5]-[10]
  UHR non-AP STA can report it’s in-device-interference and OBSS interference to AP, so that AP would not schedule transmissions during the unavailable time of the STA.
  The interference may be periodic or aperiodic, predictable or difficult to predict long in advance.

## Slide 4: Proposal
In order to handle interference (e.g., in device Rx of BT signal, Rx of 5G NR signal), propose to allow an UHR non-AP STA to solicit dynamic sub-band transmission during a TXOP.
  Applicable if there is aperiodic interference which is difficult to predict long in advance.
  Applicable if the interference occurs on a portion or the whole of the STA’s operating channel width.
  The STA may send interference information (BW, duration, etc.) to the AP and request/suggest the AP to schedule dynamic sub-band transmission if the AP is the TXOP holder. (Example 1 & 2, see next slides)
  The STA may send interference information to the AP and indicate dynamic sub-band transmission to the AP if the STA is the TXOP holder. (Example 3, see next slides)
  The STA may also indicate sub-band switch delay (value depends on implementation) to the AP.

## Slide 5: Example 1 – AP is the TXOP holder

## Slide 6: Example 2 – AP is the TXOP holder

## Slide 7: Example 3 – STA is the TXOP holder

## Slide 8: Summary
When there is aperiodic and instant interference during a TXOP, there is little to no time to do negotiation, the best choice is allow non-AP STAs to solicit/indicate dynamic sub-band transmission to the AP, to avoid failure in receiving Data or BA.
  Simply cancel transmission to the interfered STA may waste the spectrum and time.
The STA should indicate to the AP information such as duration of interference, target subchannel, sub-band switch delay.

## Slide 9: Straw Poll 1
Do you agree that an UHR non-AP STA may solicit dynamic sub-band transmission during the associated AP’s TXOP?
  The STA indicates to the AP information including but not limited to
    duration of interference,
    target subchannel
    sub-band switch delay
  Detailed signaling is TBD

## Slide 10: Straw Poll 2
Do you agree that an UHR non-AP STA may indicate dynamic sub-band transmission during its TXOP?
  The STA indicates to the AP information including but not limited to
    duration of interference,
    target subchannel
    sub-band switch delay
  Detailed signaling is TBD

## Slide 11: References
[1] 11-22-2204-00-0uhr-dynamic-subband-operation
[2] 11-23-1892-00-00bn-thoughts-on-dynamic-subchannel-operation
[3] 11-23-2027-02-00bn-considerations-for-dso-sub-band-switch-delay
[4] 11-23-2141-03-00bn-further-discussion-on-dynamic-subband-operation
[5] 11-23-0816-01-0uhr-enhancements-for-latency-sensitive-traffic-and-in-device-coexistence
[6] 11-23-0298-00-0uhr-improved-reliability-in-presence-of-interference
[7] 11-23-0665-01-0uhr-resource-management-for-multi-ap-coordination
[8] 11-23-1103-00-0uhr-in-device-interference-discussion
[9] 11-23-2002-02-00bn-in-device-coexistence-and-interference-follow-up
[10] 11-23-1934-00-00bn-in-device-interference-mitigation-follow-up
[11] Draft P802.11REVme_D5.0
[12] Draft P802.11be_D5.01