## Slide 1: Operating Mode Request
Date: 2024-05-13
Authors:

## Slide 2: Abstract
A STA may change its operating mode and notify other recipient STAs of a change in its operating mode.
In addition to notifying other STAs of its own operating mode changes, a STA may want to request a second STA to run in a certain operating mode.
This submission presents Operating Mode Request for such purpose.

## Slide 3: Introduction
A STA may change its operating mode (BW, NSS) and notify other STAs by different mechanisms, for example [1]
    Operating Mode Indication (OM Control subfield, Transmit/Receive Operating Mode)
    Operating Mode Notification (OM field in OMN frame/element)
    (Extended) Channel Switch Announcement element (New Channel Number field -> BW)
    Notify Channel Width frames
    HT/VHT/HE/EHT Operation element [2]
    EML Operating Mode Notification [2]
These mechanisms are used only for notification/indication purposes but not for request/negotiation of a certain Operating Mode among STAs.
New requirement: A STA may request another STA to run in a certain Operating Mode
  e.g., multi-AP coordination (inter-BSS/ESS/vendor/admin); a STA asks a second STA to change the second STA’s operating mode (BW/NSS, or certain capable functions to be enabled/disabled/updated)

## Slide 4: Proposal: Operating Mode Request
  An initiating STA may request a responding STA to change the responding STA’s operating mode
    The operating mode may include BW, NSS, and maybe other settings/fields/elements
    The initiating STA may have different reasons for the Operating Mode Request
      for example the initiating STA has or will have certain changes (e.g., operating mode, network conditions or throughput/latency/QoS requirements) and requests the responding STA to change its operating mode (e.g., for better throughput, latency, QoS, etc.)
    The responding STA may have its own reasons to be running in certain operating mode and may accept or deny the Operating Mode Request.

## Slide 5: Operating Mode Request: Examples
  Non-AP STA to AP: a non-AP STA may request/recommend an AP to change the AP’s operating mode, e.g., to increase the AP’s BW/NSS if the AP is operating in low BW/NSS (maybe due to power save or interference).
  AP to AP: an AP (or non-AP) may request/recommend another AP to change its operating mode, e.g., to change the BW (or primary channel selection) to reduce/avoid interference on primary/non-primary channels or for other coordination purposes.
  AP to non-AP STA: an AP may request/recommend a non-AP STA to change the non-AP STA’s operating BW/NSS, e.g., due to power save, buffer status, or latency sensitive traffic.
  Non-AP STA to non-AP STA: a non-AP STA may request another non-AP STA to change its operating mode, e.g., based on conditions and requirements of the P2P and WLAN connections.

## Slide 6: Operating Mode Request: Options (1/2)
  Operating Mode Request (OMR) can be used as standalone or together with existing protocols such as OMI/OMN.
  The request may have different request types, e.g., recommend/demand a certain OM.
  The request may include a reason code, for example channel planning, coordinated spatial reuse and latency sensitive traffic, from the initiating/requesting STA.
  The request may be accepted or denied by the responding/recipient STA.
    usually the AP controls the BSS and STAs send OMN/OMI to inform other STAs that there are operating mode changes.
    A STA (AP or non-AP) may have its own reasons to decide on certain operating mode parameters.

## Slide 7: Operating Mode Request: Options (2/2)
  The request may be solicited or unsolicited, w/ or w/o the requirement of response frame
    ACK after the frame containing the OMR confirms the request was received.
    Response to the OMR indicates whether the responding/recipient STA accepts or denies the request.
    ACK/response may have options for explicit and implicit, i.e., if OMR is ACKed but the responder sends no OMI/OMN or any other related response frames then it means the responder has rejected the OMR.
    If the responding/recipient STA decides to accept the request, it sends an OMI or initiate an OMN procedure (in case of AP) with the updated OM (or other mechanisms such as Notify Channel Width and HT/VHT/HE/EHT Operation element).

## Slide 8: Operating Mode Request: Open Issues
  Solutions need to consider the following:
    Security and misuse concerns, e.g., a STA can manipulate others to keep changing their parameters (integrity check or encryption, such as proposed in MAC header protection [3,4,5])
    Efficiency and scalability, should be compact
    Legacy STAs, back compatibility, fairness
    STAs in power save mode
    Consistency
    …

## Slide 9: Conclusion
This contribution presents Operating Mode Request/Response
  It allows an initiating STA to request a responding STA to change the responding STA’s operating mode.
  The operating mode may include BW, NSS, and other parameters.
  The OM response could just be the existing signals/procedures, such as OMI, OMN, etc.
  The initiating/responding STA may be an AP, non-AP STA, AP MLD, or non-AP MLD.

## Slide 10: References
[1] IEEE P802.11-REVme/D5.0, February 2024
[2] IEEE P802.11be/D5.0, November 2023
[3] IEEE 802.11-23/1997r1, MAC header protection, Po-Kai Huang (Intel)
[4] IEEE 802.11-23/1888r1, MAC Header Protection - follow-up, Abhishek Patil (Qualcomm)
[5] IEEE 802.11-24/0525r0, MAC header/data integrity with relaxed receiver requirement, Li-Hsiang Sun (Mediatek)