## Slide 1: Overlapped indication for aperiodic low latency traffic
Date: 2024-05-13
Authors:

## Slide 2: Introduction
Support of aperiodic low latency (LL) traffic is important for 11bn
  TXOP preemption opportunity is made via …
    Short PPDUs with xIFS gaps [1,2,6,9,10]
    Preemption request and response exchange [3,7,8,11]
  Unified preemption request frame and LL traffic protection [4]
  Preemption priority indication [5]
  Overlapped indication in TB-PPDU to enable UL preemption [12]
Independent of LL channel access mechanism LL traffic awareness is necessary
This contribution provides evaluation of overlapped indication for TXOP preemption
  Introduce use case in EDCA UL TXOP
  Simulation results for:
    Reliability of ongoing PPDU with several MCS and probability of overlapped indication detection
    Latency improvements from using overlapped indication in UL preemption
    Total throughput efficiency impact

## Slide 3: Recap: problem of aperiodic LL traffic awareness
LL traffic originates at LL_STA that is neither TXOP holder nor responder
  LL_STA needs to wait until TXOP ends to start contention for channel access
  LL traffic arrival is unpredictable
  LL_STA channel access can suffer long delays in dense scenarios
LL_STA
Channel access delay
AP (TXOP responder)
STA 1 (TXOP Holder)
PPDU
CTS
BA
RTS
PPDU
LL data
Other STAs could win contention
LL arrival
TXOP
BA

## Slide 4: Overlapped LL Indication (OLLInd) for LL awareness
OLLInd assumptions
  Short OFDM signal synchronized to OFDM symbols of ongoing PPDU
    OLLInd TX power previously agreed with AP or derived from preamble information in ongoing PPDU
  Indicates LL traffic arrival and can identify LL_STA
    Can also give a basic buffer status indication (above or below certain threshold)
  AP can detect OLLInd with simple correlation detector
LL_STA
AP (TXOP responder)
STA 1 (TXOP Holder)
CTS
RTS
Ongoing PPDU
LL arrival
OLLInd
Preemption mechanism possible
Fast LL awareness
TXOP

## Slide 5: UL preemption using overlapped LL Indication (OLLInd)
Basic TXOP preemption assumptions
  Reduce PPDU size to allow preemption opportunities (PPDU length ~1ms)
  TXOP holder can send preemption allowed indication in UL PPDU
Once AP is aware of LL traffic a preemption mechanism can be applied
  AP can send preemption indication (PI) frame to notify STAs of preemption event and …
    Trigger LL data, collect BSR, use NFRP or UORA, allow EDCA, etc.
LL_STA
Reduced access delay
AP (TXOP responder)
STA 1 (TXOP Holder)
TXOP
PPDU
CTS
BA
RTS
PPDU
PI+BA
OLLInd
LL arrival
LL data
BA
PPDU
BA
Ongoing PPDU
TF

## Slide 6: Comparison with basic frame-base preemption method
Increased efficiency
  Inserting IFS gaps longer than SIFs is not necessary
  BSR or NFRP is not necessary (OLLInd can identify the LL_STA and give basic buffer status)
Additional processing and signaling at the AP
  Correlation filter to detect OLLInd (low complexity compared to OFDM demodulation)
  AP indicates LL_STA target RSSI to achieve desired SIR

## Slide 7: High reliability for ongoing PPDU and OLLInd
Simulation set up
  Channel type D
  Ongoing PPDU: 20MHz SU-PPDU
  OLLInd: 20 MHz 11ax waveform.
Wide range of MCS supported for ongoing PPDU transmission
  Low MCS => short OLL Ind. with moderate power
  High MCS => Long OLL ind. with low power
  SNR gap 0 to 3dB on PER
OLL Ind. Prob. Detection > 99%
OLL Ind. Prob. False alarm < 2.5%
Target PER < 10%
Nsym = # OFDM symbols in
OLLInd

## Slide 8: Latency gains increase with number of contending STAs
Single BSS UL traffic only, MCS 4, 20MHz
  Max PPDU duration 1ms. Max TXOP duration 5ms
  One LL STA: traffic CBR 2Mbps, 1.5KB MPDU
    AC: VO
  Non-LL STAs: traffic CBR 4Mbps, 1.5KB MPDU
    AC: BE
LL STA latency gains
  > 60% latency reduction with > 8 contending STAs
Impact to non-LL STAs
  3% Latency reduction with 8 contending STAs
  Overall throughput unaffected
Gain
Loss
LL STA
Non-LL STA
All STAs
Gain

## Slide 9: High latency gains for LL-STAs Low latency gains for AC_VI non-LL STAs
Single BSS UL traffic only, MCS 4, 20MHz
  Max PPDU duration 1ms. Max TXOP duration 5ms
  One LL STA: traffic CBR 2Mbps, 1.5KB MPDU
    AC: VO
  Non-LL STAs: traffic CBR 4Mbps, 1.5KB MPDU
    AC: VI
LL STA latency gains
  ~34% with low number of contending STAs
  >80% with > 8 contending STAs
Impact to non-LL STAs
  Small latency reduction for non-LL STAs
    Due to LL STA not contending as often
  Marginal throughput loss in dense scenarios (12 STAs)
Gain
Loss
LL STA
Non-LL STA
All STAs
Gain

## Slide 10: Large latency gains for LL-STA contending with AC_VO STAs
Single BSS UL traffic only, MCS 4, 20MHz
  Max PPDU duration 1ms. Max TXOP duration 5ms
  One LL STA: traffic CBR 2Mbps, 1.5KB MPDU
    AC: VO
  Non-LL STAs: traffic CBR 4Mbps, 1.5KB MPDU
    AC: VO
50% to 98% LL STA latency gains
Low impact to non-LL STAs
  Small latency loss with 4 STAs (short contention time)
  Small latency gain with 8 STAs (long contention time)
  Marginal throughput loss in dense scenarios (12 STAs)
Gain
Loss
Loss
LL STA
Non-LL STA
All STAs
Gain

## Slide 11: Conclusion
An overlapped LL indication solves the problem of LL traffic awareness at STAs not part of ongoing TXOP traffic exchange
Overlapped LL indication design achieves …
  Low impact on reliability of ongoing PPDU for wide range of MCS
  High detection probability
Preemption with overlapped LL indication gives large latency reduction
  50% to 98% latency reduction for LL-STAs
  Small impact to non-LL STAs
    Some positive cases of up to 7% latency reduction
    No more than 3% latency increase in negative cases
    Marginal throughput loss in dense scenarios (12 STAs)

## Slide 12: SP 1
Do you support the use of an overlapped indication for non-AP STAs to inform AP of traffic arrival

## Slide 13: References
[1] 11-23/1229r1 Preemption for low latency application (Follow up)
[2] 11-23/1886r3 Preemption techniques to meet low-latency (LL) targets
[3] 11-23/1909r1 Transmission Method of Low Latency Traffic
[4] 11-23/1950r0 Considerations on Preemption Request
[5] 11-23/1939r1 Priority Based Preemption Method
[6] 11-24/0103r1 TXOP level preemption for Low latency application in 802.11bn
[7] 11-24/0091r0 Enhanced Scheduling Method for LL Traffic Follow up
[8] 11-24/0168r0 TXOP Preemption in 11bn
[9] 11-24/0416r1 Target STA Prioritization in EDCA-based Preemption Mechanisms during a DL TXOP
[10] 11-24/0470r0 Re-thinking latency: the missing pieces
[11] 11-24/0431r2 Signal for preemption request
[12] 11-23/1194r0 Overlapped Indication to Support Preemption