## Slide 1: Harmonization of Waveform
Date: 2024-05-15
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-24/0849r1
May 2024

## Slide 2: Abstract
In this contribution, we discuss the harmonized design for different scenarios in AMP.
Doc.: IEEE 802.11-24/0849r1

## Slide 3
Background
  Four solutions have been proposed and discussed so far
    Solution 1: active transmission [1];
    Solution 2: close range backscatter with full duplex [2];
    Solution 3: long range backscatter with bi-static [1];
    Solution 4: legacy 802.11 devices enhanced with AMP features, e.g., extremely low power consumption, energy harvesting capability, etc. [3]
  Clearly, harmonization is needed
    Different solutions may diverge vastly in PHY and MAC design.
    Harmonization needs to start from basic design, e.g., waveform.
    Objective: optimal design for all solutions but may not be optimal design for each individual solution, thus compromise needed
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-24/0849r1
May 2024

## Slide 4
Frame Types
  Considering wireless power transfer (WPT), 4 potential frame types need to be considered for new/enhanced design.
    DL communication: triggering frame + data frame
    UL data: data frame
    WPT: wireless power transfer frame
    CW: CW for backscattering
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-24/0849r1
May 2024
 | DL comm. | UL data | WPT | CW
S1: Active | √ | √ | √ | 
S2: Backscatter (close range) | √ | √ | √ | √
S3: Backscatter (long range) | √ | √ | √ | √
S4: Legacy enhanced | √ |  | √ | 

## Slide 5
Waveform Types
  Different waveforms have been proposed and discussed so far as in the below table
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-24/0849r1
May 2024
 | DL comm. | UL data | WPT | CW
S1: Active | MC-OOK (AP) | OOK/PSK/FSK/DSSS (AMP) | TBD (energizer) | 
S2: Backscatter (close range) | TBD (AP/M) | OOK (AMP) | Pulse/OFDM (AP/M) | Pulse/OFDM (AP/M)
S3: Backscatter (long range) | MC-OOK (AP) | OOK/PSK/FSK/DSSS (AMP) | TBD (energizer) | TBD (assistant node)
S4: Legacy enhanced | MC-OOK (AP) |  | TBD (energizer) | 

## Slide 6
DL/UL Waveforms
  DL: Triggering, DL data, Charging, CW
    S2: WPT and CW are jointly done.
    S3: WPT and CW can be either joint or separate, i.e., energizer and assistant nodes can be integrated or independent.
    S4: enhancement for the trigger frame and data communication with legacy protocols, e.g., 802.11b/n, thus no need to re-design.
    WPT waveform
      Sine wave: simple but not compatible with OFDM thus may need hardware upgrade.
      SC-OFDM: simple and compatible with OFDM, low PAPR.
      MC-OFDM: complicated but fully compatible with OFDM, high PAPR.
    OFDM based DL with simple reception
  UL: UL data
    Harmonize active transmission and backscattering.
    Waveform much simpler than OFDM is needed.
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-24/0849r1
May 2024

## Slide 7
Harmonized Waveform
  Objective: optimal design for all solutions but may not be optimal design for each individual solution, thus compromise needed
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-24/0849r1
May 2024
 | DL comm. | UL data | WPT | CW
S1: Active | OFDM based OOK (AP) | OOK/PSK/FSK (AMP) | SC/MC-OFDM (energizer) | 
S2: Backscatter (close range) | OFDM based OOK (AP/M) | OOK (AMP) | SC/MC-OFDM (AP/M) | SC/MC-OFDM (AP/M)
S3: Backscatter (long range) | OFDM based OOK (AP) | OOK/PSK/FSK (AMP) | SC/MC-OFDM (energizer) | SC/MC-OFDM (energizer/assistant node)
S4: Legacy enhanced | OFDM based OOK (AP) |  | SC/MC-OFDM (energizer) | 

## Slide 8
Harmonized Waveform
  DL: DL comm., WPT, CW
    Both MC-OOK and SC/MC-OFDM can be supported by OFDM transmitter thus can co-exist with legacy networks
    WPT and CW are jointly designed, i.e., energizer and assistant nodes are integrated
    OFDM based DL with different activated SCs
  UL: UL data
    Simple waveform: OOK as baseline and further consider PSK/FSK
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-24/0849r1
May 2024

## Slide 9
Summary
  In this submission, the harmonization of waveform issues is discussed with following observations and conclusions:
    Waveform harmonization is potentially feasible with compromised design;
    For DL transmission including wireless power transfer, OFDM based waveform with simple reception can be employed with different number of activated SCs;
    For UL, simplicity is of ultimate importance and thus OOK/PSK/FSK can be considered.
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-24/0849r1
May 2024

## Slide 10: Reference
[1] 11-23-2203-01-0amp-updated-technical-report-on-support-of-amp-iot-devices-in-wlan
[2] 11-24-0537-00-0amp-close-range-amp-wifi-reader-feasibility-study
[3] 11-23-1159-00-0amp-thoughts-on-amp-iot-and-par
Doc.: IEEE 802.11-24/0849r1
May 2024