## Slide 1: Further Discussions on In-Device Coexistence
Date: 2024-05-12
Authors:

## Slide 2: Introduction
Several contributions about in-device coexistence (IDC) were discussed in UHR SG and 11bn TG[1-6].
In this contribution, we propose further considerations during IDC procedure for efficient low latency traffic delivery.

## Slide 3: Recap: In-Device Coexistence [1-6]
According to discussions on the IDC [1-6], in-device coexistence interference may happen in a device with WLAN due to transmissions by other wireless system (e.g., Bluetooth, UWB, LAA/NR-U, etc.)
In that case, the WLAN STA may not transmit and/or receive with a peer STA (e.g., AP) through its link until the IDC event ends
To minimize the impact of the situation, the WLAN STA need to report to AP such the situation (e.g., unavailability information(e.g., time)) by solicited or unsolicited manner
If the AP gets the unavailability duration of a non-AP STA, the AP will avoid transmitting DL frames to the non-AP STA during the unavailability duration

## Slide 4: Recap: In-Device Coexistence [1-6]
Example
AP
STA
Unavailable duration (UD)
No DL transmission
DL
DL
BA
BA
ICF
ICR
DL
BA
Ori
TXOP
UD Info
UL frame

## Slide 5: Motivation
Notified unavailable duration can be long (e.g., 5ms ~)
Low latency (LL) traffic for the STA can happen during the duration
  AP will try to transmit the traffic after unavailable duration
Co-ex event can be finished earlier than the notified duration
  The notified unavailable duration can be different from the real unavailable duration
AP
STA
UD Info
Original Unavailable duration (UD)
Co-ex event communication
DL LL Data
LL data
Delay of LL Data
ICF
UL frame
DL data
BA
ICR

## Slide 6: Proposed IDC operation (1)
When a coexistence event is finished earlier, the STA transmits to AP a frame (e.g., PS-Poll, etc.) indicating its availability
  Before invoking a backoff procedure, the STA may further wait for a specific duration (e.g., medium sync delay)
During a STA’s unavailable duration, if the AP receives a frame from the STA and has its buffered traffic, the AP transmits the buffered traffic (e.g., low latency traffic) to the STA
AP
STA
UD Info
Original Unavailable duration
Co-ex event communication
DL LL Data for STA
LL data
UL frame
UL
frame
BA
AI
UD: Unavailable duration
AI: Available Indication

## Slide 7: Proposed IDC operation (2)
During the unavailable duration of a STA, when AP receives LL traffic for the STA, AP can transmit an initial control frame to the STA to check the STA status
  ICF may contain the LL traffic indication
When the STA receives an initial control frame indicating LL traffic from the AP during its unavailable period, STA transmits to AP the ICR frame
  STA may indicate its available state in the response frame
If the AP receives ICR frame in response to the ICF, the AP transmits to the STA the LL traffic.
Otherwise, the AP may retransmit the ICF later
AP
STA 1
Original Unavailable duration
Co-ex event communication
UL frame
ICR
DL traffic (STA1)
BA
UD Info
AI
LL Data for STA
UD: Unavailable duration
AI: Available Indication
ICF
ICF

## Slide 8: Conclusion
We proposed methods for delivering the low latency traffic efficiently during the coexistence event
  STA can report its available state to AP during its reported unavailable duration when the STA is in the unavailable duration
  During the unavailable duration of a STA, if AP has LL traffic for the STA, the AP can send to the STA a frame to check the STA’s status

## Slide 9: References
[1] 23/0816, Enhancements for latency sensitive traffic and in-device-coexistence
[2] 23/1103, in-device interference discussion
[3] 23/1964, Coexistence Protocols for UHR
[4] 23/2002, In-device coexistence and interference follow-up
[5] 24/0094, Probe-before-Talk and Unsolicited Unavailability Announcement for Co-ex Management
[6] 24/0509, Thoughts on in-device coexistence and P2P for 11bn