## Slide 1: ICR Consideration
Date: 2024-05-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Candidate ICF/ICR
The ICF/ICR is used for the initial control information negotiation/notification e.g. in-device interference co-existence, power save low-capacity listening mode.
The ICF/ICR also needs to act as initial frame exchange for EMLSR, TXOP protection the same way as RTS/CTS
Frame exchange initiated by an AP
  Option 1: BSRP Trigger and Multi-STA BA.
  Option 2: BSRP Trigger and QoS Null
  Option 3: New Trigger variant and new control responding frame.
Frame exchange initiated by a non-AP STA
  Option 1: BAR and Multi-STA BA when soliciting device is a non-AP STA.
  Option 2: BSRP Trigger and Multi-STA BA.
  Option 3: New Trigger variant and new control responding frame

## Slide 3: Per-User and Common Initial Control Information
Per-user initial control information
  In a broadcast ICF, the AP can announce the maximal Nss, BW for a STA’s power save that the AP will ask the STA to use for the DL MU PPDU reception and UL TB PPDU transmission.
  In a broadcast Multi-STA BA, the AP can transmit the in-device interference for a STA besides the BA acknowledgement for the STA.
    This is useful when the AP has interference and receive part or no MPDUs from a STA in the STA’s RU.
Common initial control information
  In a unicast ICF or ICR, the initial control information is the common initial control information.
  In a broadcast ICF or ICR, the initial control information for all addressed/associated UHR STAs is the common initial control information, e.g.
    The AP’s unavailable time.

## Slide 4: Multi-STA BA vs QoS Null and ICR with New Control Subtype (1)
The QoS Null can be used when no additional initial control information is carried in responding frame.
The HE Control field in a QoS Null frame may have no enough room to carry the required initial control information.
The variable length HE Control field can provide enough room. However, it requires the additional change to HE Control field.
The ICR with the new control subtype provides the enough room for carrying the initial control information.
However, this increases the additional control subtype decoding.

## Slide 5: Multi-STA BA vs QoS Null and ICR with New Control Subtype (2)
BA in mmWave band provides the traffic load control besides acknowledging the soliciting A-MPDU.
Multi-STA BA can be used as unicast and broadcast frame.
Multi-STA BA can carry additional control information besides BA bitmap to acknowledging A-MPDU(s) and/or MPDU(s).
  It is easy to carry per-user initial control information and initial control information for all addressed STAs.
Adding in-device coexistence information (e.g. unavailable time notification) is harmonized with the other Multi-STA BA enhancement.
When being used as ICR solicited by ICF, a Multi-STA BA may not need to carry BA Bitmap field for acknowledging the frames in the A-MPDU(s).
Multi-STA BA needs to be ICR at least when the ICR carries the feedbacks (i.e. unavailability feedback).

## Slide 6: Common Initial Control Info in ICR Multi-STA BA (1)
The Common Initial Control Info field carries one, or multiple Common Initial Control Per AID TID Info fields.
  The AID11 field with a special value, e.g. 2012, in a Per AID TID Info field indicate that the Per AID TID Info field is the Common Initial Control Per AID TID Info field.
Each Common Initial Control Per AID TID Info field has the Common Initial Info field with 4, 8, 16, 32, 64, 128 octets.
  The Fragment Number subfield indicates the length of Common Initial Info field.
    The same coding of Fragment Number subfield for the length of Block Ack Bitmap field is used.
Per-STA Initial Control Info List
Variable
Common Initial Control Info
Variable
Common Initial Control Per AID TID Info
……
Common Initial Control Per AID TID Info
0, 1, or more Common Initial Control Per AID TID Info fields
Specific AID value, e.g. 2012
2
4, 8, 16, 32, 64, 128
Common Initial Control Per AID TID Info field
Common Initial Info
Padding
Padding
Security Per AID TID
18
Padding
Padding with Per AID TID Info List

## Slide 7: Common Initial Control Info in ICR Multi-STA BA (2)
The combination of the Common Initial Control Per AID TID Info field(s) in a Common Initial Control Info field satisfies.
  The Common Initial Control Per AID TID Info field(s) carries all the required common initial control information.
  The number of the Common Initial Control Per AID TID Info field(s) in the Common Initial Control Info field is smallest compare any other combinations of Common Initial Control Per AID TID Info field(s) to carry the required common initial control information.
  The unused bits in Common Initial Info field(s) are least compare any other combinations of Common Initial Control Per AID TID Info field(s) to carry the required common initial control information.
  Only the Common Initial Info field in the last Common Initial Control Per AID TID Info field has unused bits.

## Slide 8: Per-STA Initial Control Info in ICR Multi-STA BA (1)
The initial control information for a STA can be carried after the Common initial control information.
The Per-STA Initial Control Info field carries one, or multiple Per-STA Initial Control Per AID TID Info fields.
  The AID11 field with addressed STA’s AID, in a Per AID TID Info field indicate that the Per AID TID Info field is the Per-STA Initial Control Per AID TID Info field.
    This is suitable for uncast Multi-STA BA.
Each Per-STA Initial Control Per AID TID Info field has the Per-STA Initial Info field with 4, 8, 16, 32, 64, 128 octets.
  The Fragment Number subfield indicates the length of Common Initial Info field.
    The same coding of Fragment Number subfield for the length of Block Ack Bitmap field with the exception B0 usage is used.
2
4, 8, 16, 32, 64, 128
Per-STA Initial Control Per AID TID Info field
Per-STA Initial Info

## Slide 9: Per-STA Initial Control Info in ICR Multi-STA BA (2)
The combination of the Per-STA Initial Control Per AID TID Info field(s) in a Per-STA Initial Control Info field satisfies.
  The Per-STA Initial Control Per AID TID Info field(s) carries all the required per-STA initial control information.
  The number of the Per-STA Initial Control Per AID TID Info field(s) in the Per-STA Initial Control Info field is smallest compare any other combinations of Per-STA Initial Control Per AID TID Info field(s) to carry the required per-STA initial control information.
  The unused bits in Per-STA Initial Info field(s) are least compare any other combinations of Per-STA Initial Control Per AID TID Info field(s) to carry the required per-STA initial control information.
  Only the Per-STA Initial Info field in the last Per-STA Initial Control Per AID TID Info field has unused bits.

## Slide 10: Summary
The various candidate ICRs are compared
  We prefer Multi-STA BA as ICR at least when carrying the feedbacks.
The frame format of ICR Multi-STA BA is discussed.

## Slide 11: SP 1
Do you support to use M-STA BA for Initial Control Response frame (ICR) for DL and UL, at least when carrying feedbacks (i.e. unavailability feedback)?